## Slide 1: JCTVC-H0252
Oguz Bici, Jani Lainema, Kemal Ugur
Nokia
CE9: Results of SP experiments on simplification of merge process

## Slide 2: Summary
Goal: Reduce complexity of the first pruning process.
Proposal:
  Parallelizable, reduced set of comparisons within spatial candidates
    Worst case comparisons reduced to 5 compared to 10 in HM5.
    All spatial and temporal MVP candidates can be derived independently in parallel
  No comparison with TMVP
    Also improves error resiliency
  Coding efficiency: 0.0% for RA and 0.1% LD

## Slide 3: Details – Reduced comparisons for spatial candidates
HM5: Candidate removed if any of previous candidate has same motion
Proposed: Reduced comparisons.
B0
B1
B2
A1
A0
Candidates | Candidates required to compare against | 
 | HM5 | Proposal
A1 | N/A | N/A
B1 | A1 | A1
B0 | A1 – B1 | B1
A0 | A1 – B1 – B0 | A1
B2 | A1 – B1 – B0 – A0 | A1 – B1
Benefits: Less logic required to decide inclusion of a spatial candidate
Simpler to parallelize

## Slide 4: Details – No TMVP comparison
HM5: TMVP compared against every available spatial candidate
Proposed: No comparison with TMVP.
Benefits:
  Reduced complexity
    Worst case comparisons reduced by 4
    Reduced cycles: No comparisons required after TMVP derived
  Error resiliency

## Slide 5: Results
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.0% | 0.1% | -0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 0.1% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% |  |  | 
Class D | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.1%
Class F | -0.1% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1% |  |  | 
Enc Time[%] | 102% |  |  | 100% |  |  | 101% |  | 
Dec Time[%] | 97% |  |  | 100% |  |  | 99% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.1% | 0.2% | 0.5% | 0.1% | -0.2% | 0.5% |  |  | 
Class C | 0.1% | -0.2% | 0.1% | 0.1% | 0.2% | 0.0% |  |  | 
Class D | 0.0% | -0.1% | 0.4% | 0.0% | 0.7% | 0.3% |  |  | 
Class E | 0.3% | 0.0% | 0.3% | 0.2% | 0.2% | 0.5% |  |  | 
Overall | 0.1% | 0.0% | 0.3% | 0.1% | 0.2% | 0.3% |  |  | 
 | 0.1% | 0.0% | 0.3% | 0.1% | 0.2% | 0.4% |  |  | 
Class F | -0.1% | 0.2% | -0.1% | -0.1% | -0.9% | -0.5% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 98% |  |  |  |  | 
0.0% for RA cases
0.1% for LD cases

## Slide 6: Results of “no TMVP comparison”
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | 0.1%
Class B | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1% | 0.0%
Class C | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% |  |  | 
Class D | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% | 0.2% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0%
 | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.1%
Class F | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% |  |  | 
Enc Time[%] |  |  |  |  |  |  |  |  | 
Dec Time[%] |  |  |  |  |  |  |  |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.1% | 0.1% | 0.3% | 0.2% | -0.1% | 0.7% |  |  | 
Class C | 0.1% | 0.1% | 0.2% | 0.1% | 0.3% | 0.0% |  |  | 
Class D | 0.1% | -0.2% | 0.3% | 0.1% | 0.8% | 0.3% |  |  | 
Class E | 0.4% | 0.4% | 0.3% | 0.4% | 0.0% | 0.6% |  |  | 
Overall | 0.2% | 0.1% | 0.3% | 0.2% | 0.3% | 0.4% |  |  | 
 | 0.2% | 0.1% | 0.3% | 0.2% | 0.2% | 0.4% |  |  | 
Class F | 0.0% | -0.2% | -0.2% | 0.0% | -1.1% | -0.2% |  |  | 
Enc Time[%] |  |  |  |  |  |  |  |  | 
Dec Time[%] |  |  |  |  |  |  |  |  | 
Also proposed in JCTVC-H0133

## Slide 7: Results of “reduced set of spatial comparisons”
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
Class B | 0.0% | -0.1% | -0.1% | 0.0% | 0.1% | 0.1% | -0.1% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | -0.1% | 0.0% | 0.1% | 0.0% |  |  | 
Class D | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.2% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class F | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] |  |  |  |  |  |  |  |  | 
Dec Time[%] |  |  |  |  |  |  |  |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.0% | 0.1% | 0.2% | 0.0% | -0.1% | -0.2% |  |  | 
Class C | 0.0% | -0.3% | 0.0% | 0.0% | -0.1% | 0.0% |  |  | 
Class D | 0.0% | 0.1% | 0.0% | 0.0% | -0.1% | 0.0% |  |  | 
Class E | -0.1% | -0.4% | 0.0% | -0.2% | 0.2% | -0.1% |  |  | 
Overall | 0.0% | -0.1% | 0.0% | -0.1% | -0.1% | -0.1% |  |  | 
 | 0.0% | -0.1% | 0.1% | -0.1% | 0.0% | 0.0% |  |  | 
Class F | -0.1% | 0.3% | 0.1% | -0.1% | 0.3% | -0.2% |  |  | 
Enc Time[%] |  |  |  |  |  |  |  |  | 
Dec Time[%] |  |  |  |  |  |  |  |  | 
Question was raised in the reflector about “reduced set of spatial comparisons”
Results show this simplification has no loss but a slight gain
Anchor is: HM5 + ”noTMVP comparison”

## Slide 8: Conclusion
Worst case duplication checks reduced to 5 from 10
Simpler logic to decide inclusion of a spatial candidate
Improved parallelization
Error resiliency enhanced by exempting TMVP from duplication checks.
Limited impact on the coding efficiency
Recommended for adoption