## Slide 1
Cyclic POC (JCTVC-H0257, m23132)
J.Koyama, K.Kazui, S.Shimada and A.Nakagawa
FUJITSU LABORATORIES LTD.
Copyright 2012 FUJITSU LIMITED
Notes: <number>

## Slide 2: Summary
We propose to change the definition of picture order count (POC) so that the POC value can be cyclic.
  POC value is stored in unsigned 32-bit register.
  No changes of the syntax and the pixel decoding process
<number>

## Slide 3: Introduction
POC in WD5.0
  32-bit signed integer, [-231, 231-1]
  Each picture in the same sequence must have an unique POC value.
  → IDR shall be inserted when POC value reaches to 231.
  → 1.1 year for 60Hz sequence
Remote surveillance cameras used in public infrastructure systems
  Low delay video transmission
  → For remote camera control
  → Intra line refresh is used instead of intra picture refresh.
  24/365 operation
  AVC-based product example: http://www.fujitsu.com/global/services/computing/peripheral/video/products/ip920e/
<number>

## Slide 4: Problem
The restriction in the current POC definition is problematic for low delay video encoder in 24/365 operation
  Burden in encoder design, difficulty in validation
    Implementing a function of an IDR picture insertion in the middle of the sequence is a burden because it happens quite rare (1.1 year).
  Degradation in video quality
    The buffer size for Intra line refresh is reduced to the averaged size of a picture for low delay operation.
    Sudden degradation in picture quality happens at an inserted IDR picture since enough number of bits cannot be assigned to the IDR.
<number>

## Slide 5: Proposal
Modified definition of the POC value
  POC value can be cyclic.
  POC value is stored in 32-bit unsigned integer.
Implementation (Example)
  unsigned int uiPocA, uiPocB, uiPocC, uiPocD
  signed int iPocDiff
  Addition (+) and subtraction (-) for POC reconstruction
    (+) uiPocC = uiPocA + uiPocB
    (- ) uiPocD = uiPocA - uiPocB
  Note: Carry bit is discarded
  POC difference and comparison (signed integer)
    Difference btw. PocA and PocB: iPocDiff = (int)(uiPocA − uiPocB);
    PocA is larger than PocB: True if iPocDiff > 0
    PocA is smaller than PocB: True if iPocDiff < 0
    PocA is equal to PocB: True if iPocDiff == 0
<number>
All POC-related operation still works even if POC value is wrapped.

## Slide 6: Summary of the proposed POC definition
<number>
Item | WD5.0 | Proposal
Range | [231, 231-1] | [0, 232-1]
Cyclic (wrapped) POC | No allowed | Allowed
Pictures with same POC value | No allowed | Allowed
Picture with POC value 0 | IDR picture only | Any picture
Signaling in slice header | pic_order_cnt_lsb [0, 2log2_max_pic_order_cnt_lsb_minus_4 + 4] | ←
Range of POC difference | [-215, 215-1] | ←

## Slide 7: Conclusion
We recommend to adopt modified POC definition into HEVC.
  POC value can be cyclic.
  32-bit unsigned integer, rather in 32-bit signed integer
  No changes in the syntax and the pixel reconstruction process
<number>

## Slide 8
<number>