## Slide 1
Non-CE1: Dimension reduced rangeTabLPS for the interval subdivision of the arithmetic coding engine
JCTVC-H0265

## Slide 2: JCTVC-H0265
Dimensions of rangeTabLPS changed from 64x4 to 16x8
Size of rangeTabLPS reduced by from 256 to 128 elements
Two different probability quantizations for rangeTabLPS rows:
Uniform: Equidistant probability values require additional LUT (mapState) for accessing rangeTabLPS with pStateIdx
codIRangeLPS = rangeTabLPS[mapState [pStateIdx]][qCodIRangeIdx]
Exponential: Rows in rangeTabLPS are accessed by pStateIdx using a bit-shift
codIRangeLPS = rangeTabLPS[pStateIdx>>2][qCodIRangeIdx]

## Slide 3: JCTVC-H0265
Quantization for probability interval subdivision

## Slide 4: JCTVC-H265
Three configurations are tested:
Uniform quantization
Exponential quantization
Exponential quantization with optimized table elements (based on bin distribution and distribution of codIRange mapped to each particular rangeTabLPS table element)

## Slide 5: JCTVC-H0265