## Slide 1
AHG15 : Independent control of Max CU and LCU for small LCU case (JCTVC-H0269)
Chanyul Kim, Jongbum Choi
(Samsung)
Notes: <number>

## Slide 2: Summary
<number>
Suggest modification of min/max CU independent of LCU.
Change:
Average coding gain is obtained compared to different LCU size in HM
  -0.6% / -0.4%/ -0.2% for HE (Anchor : LCU 32x32)
  -1.9%/ -1.1%/ -1.1% for HE (Anchor : LCU 16x16)
Cross-check (JCTVC-H0623)
  Thanks to LG

## Slide 3: Algorithm description (1)
<number>
log2_diff_bpu_lcu_size =0
Exactly the same as HM method
log2_diff_bpu_lcu_size !=0
BPU= 64 but LCU is 32
(A)

## Slide 4: Algorithm description (2)
<number>
(B)

## Slide 5: Algorithm description (2)
<number>
HM 5.0
Proposed one
log2(LCU_size) = log2(Max_CU_size) =(log2_min_coding_block_size_minus3 + log2_diff_max_min_coding_block_size +3)
- LCU is the same as Max CU size
log2(LCU_size) = log2(Max_CU_size) = (log2_min_coding_block_size_minus3 + log2_diff_max_min_coding_block_size +3)
Log2(BPU_size) = log2(LCU) + log2_diff_lcu_max_coding_block_size
- BPU is the equal or larger than LCU size

## Slide 6: Experimental results (1)
<number>
(BPU = 64 and LCU = 32) vs (LCU size =32, HM anchor)

## Slide 7: Experimental results (2)
<number>
(BPU = 64 and LCU = 16 ) vs (LCU size =16, HM anchor)

## Slide 8: Conclusions
<number>
Independently control between LCU and Max CU
The proposed method support the current HM and more flexibility only apply one bit in SPS.
(1) log2_diff_lcu_max_coding_block_size =0  The same method of HM
(2) log2_diff_lcu_max_coding_block_size !=0  The same processing unit with more gain.
Coding efficiency increase depending on small LCU size.
We anticipate that the proposed method be adopted into next HM.