## Slide 1: CE2: Subset 4.4: Test Results on Harmonization of JCTVC-G283, JCTVC-G442 and JCTVC-G980
Xin Zhao, Jicheng An, Xun Guo, Shawmin Lei (MediaTek)
Liwei Guo, Xianglin Wang, Marta Karczewicz (Qualcomm)
Akira Minezawa, Kazuo Sugimoto, Shun-ichi Sekiguchi (Mitsubishi )
Atsuro Ichigaya, Shinichi Sakaida (NHK)
Siwei Ma, Wen Gao (Peking Univ.)
Presenter: Xin Zhao

## Slide 2: Background
Same RQT structure is shared between luma (Y) and chroma (U, V) components
Chroma generally presents smoother textures than Luma, and applying the same RQT depth of luma to chroma is not efficient
G283, G442 and G980 proposes solutions for separate chroma RQT setting

## Slide 3: Harmonized solution on Chroma RQT
In SPS, new configuration max_transform_hierarchy_depth_inter_chroma and max_transform_hierarchy_depth_intara_chroma are included
seq_parameter_set_rbsp( ) { | Descriptor
… | …
log2_diff_max_min_transform_block_size | ue(v)
log2_min_pcm_coding_block_size_minus3 | ue(v)
max_transform_hierarchy_depth_inter_luma | ue(v)
max_transform_hierarchy_depth_intra_luma | ue(v)
max_transform_hierarchy_depth_inter_chroma | ue(v)
max_transform_hierarchy_depth_intra_chroma | ue(v)
chroma_pred_from_luma_enabled_flag | u(1)
loop_filter_across_slice_flag | u(1)
… | …
} | 

## Slide 4: Harmonized solution on Chroma RQT
2012/2/1
Copyright © MediaTek Inc. All rights reserved.
4
Chroma RQT depth (DepthC) is implicitly derived
Examples
  MaxDepth_inter_chroma=1, DepthL=0  DepthC=0
  MaxDepth_inter_chroma=1, DepthL=2  DepthC=1
 | DepthC
Inter | DepthC = min( DepthL, MaxDepth_inter_chroma )
Intra | DepthC = min( DepthL, MaxDepth_intra_chroma )

## Slide 5: Harmonized solution on Chroma RQT
2012/2/1
Copyright © MediaTek Inc. All rights reserved.
5
For special case of MaxDepth_inter(intra)_chroma=0
Examples
  MaxDepth_inter_chroma=0, DepthL=1, SIZE2Nx2N
  DepthC=0
  MaxDepth_inter_chroma=0, DepthL=0, SIZENxN
  DepthC=0
DepthC = min( DepthL, SIZE2Nx2N ? 0 : 1 )

## Slide 6
2012/2/1
Copyright © MediaTek Inc. All rights reserved.
6
MaxChromaDepth=1 |  | ⊿rate Y | ⊿rate U | ⊿rate V | Enc. Time | Dec. Time
AI | HE | 0.0% | -2.4% | -2.5% | 100% | 99%
 | LC | 0.0% | -1.8% | -2.0% | 101% | 99%
RA | HE | 0.0% | -1.6% | -1.6% | 99% | 100%
 | LC | 0.0% | -1.1% | -1.7% | 99% | 100%
LD | HE | 0.0% | -0.8% | -1.0% | 99% | 99%
 | LC | 0.0% | -1.1% | -1.1% | 100% | 100%
RAHE-10 |  | 0.0% | -3.0% | -2.8% | 99% | 100%
Experimental Results
TEST 0: Chroma 32x32 Transform is not applied

## Slide 7
2012/2/1
Copyright © MediaTek Inc. All rights reserved.
7
MaxChromaDepth=1 |  | ⊿rate Y | ⊿rate U | ⊿rate V | Enc. Time | Dec. Time
AI | HE | -0.1% | -2.5% | -2.4% | 101% | 99%
 | LC | 0.0% | -2.1% | -2.4% | 101% | 99%
RA | HE | -0.1% | -1.7% | -1.7% | 100% | 100%
 | LC | 0.0% | -1.3% | -1.9% | 100% | 100%
LD | HE | 0.0% | -1.2% | -1.2% | 100% | 100%
 | LC | 0.0% | -1.2% | -1.5% | 100% | 100%
RAHE-10 |  | 0.0% | -4.5% | -4.1% | 100% | 100%
Experimental Results
TEST 1: Chroma 32x32 Transform is applied

## Slide 8
2012/2/1
Copyright © MediaTek Inc. All rights reserved.
8
SlideEditing |  | ⊿rate Y | ⊿rate U | ⊿rate V
LD-HE | MaxDepth_chroma=1 | -0.1% | -1.1% | -0.6%
 | MaxDepth_chroma=2 | -0.5% | -0.6% | -0.9%
Reasons to signal in SPS
MaxDepth 1 vs. 2
Higher U, V resolution, e.g., YUV 4: 4: 4 ?

## Slide 9
In SPS, max RQT depth is signaled separately for luma and chroma
The chroma RQT depth is implicitly derived
Two cases with and without 32x32 chroma transform are tested
Summary

## Slide 10: Thank you!