## Slide 1: CE10 Subtest 1: Chroma Deblocking Filter
Qian Huang, Jicheng An, Xun Guo, Shawmin Lei
MediaTek
Presented by Xun Guo
8th JCT-VC Meeting in San Jose
1-10 February, 2012
Notes: <number>

## Slide 2: Overall Summary
Some modifications in chroma deblocking filter
  Added filtering on/off decision
    Chroma components make decision independently
  Also filter inter boundaries
    The boundaries with Bs > 0 could be filtered.
    MV differences are not considered for chroma  Less filtering than luma.
Experimental results
  Objective quality
    Average BD-rate reductions of 0.2%, 0.7% and 0.9% for AI, RA and LD chroma components, respectively
  Subjective quality
    Similar to HM5.0
Run time
  Almost the same as that of HM5.0
<number>

## Slide 3: Outline
Filtering Decision in HM5.0
Proposed Filtering Decision for Chroma
Simulation Results
Conclusions
<number>
Notes: <number>

## Slide 4: Filtering Decision in HM5.0
Only apply on luma
<number>
d1 = |p20 - 2*p10 + p00| + |q20 - 2*q10 + q00| + |p23 - 2*p13 + p03| + |q23 - 2*q13 + q03| < beta (QPluma)
d2 = |p24 - 2*p14 + p04| + |q24 - 2*q14 + q04| + |p27 - 2*p17 + p07| + |q27 - 2*q17 + q07| < beta (QPluma)

## Slide 5: Proposed Filtering Decision for Chroma
Filtering on/off decision for each 4x4 boundary with Bs > 0
  At most 2 pixels on each side of the boundary are used
  No addition line buffer is needed
<number>
d = |p10 – p11| + |q10 – q11| + |p20 – p21| + |q20 – q21|
d < beta (QPchroma)

## Slide 6: Simulation Results
<number>
Anchor – HM5.0
Recommended test conditions in JCTVC-G1200
Thank Intel for crosschecking (JCTVC-H0298)
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Overall | 0.0% | -0.4% | -0.5% | 0.0% | 0.0% | 0.0% |  |  | 
 | 0.0% | -0.4% | -0.5% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 99.47% |  |  | 99.27% |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Overall | 0.0% | -0.6% | -0.6% | 0.0% | -0.9% | -0.9% | 0.0% | -0.6% | -0.5%
 | 0.0% | -0.6% | -0.6% | 0.0% | -0.9% | -0.9% | 0.0% | -0.6% | -0.5%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 99.67% |  |  | 99.79% |  |  | 99.92% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Overall | 0.0% | -0.6% | -0.7% | 0.0% | -1.2% | -1.1% |  |  | 
 | 0.0% | -0.6% | -0.7% | 0.0% | -1.2% | -1.0% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 99.66% |  |  | 100.15% |  |  |  |  | 
 | Low delay P HE |  |  | Low delay P LC |  |  | Low delay P HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Overall | 0.0% | -0.6% | -0.8% | -0.1% | -1.2% | -1.3% |  |  | 
 | -0.1% | -0.6% | -0.8% | 0.0% | -1.7% | -1.3% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 100.04% |  |  | 100.56% |  |  |  |  | 

## Slide 7: Conclusions
A modified chroma deblocking filter is proposed
  Filtering on/off decision is added for chroma boundaries
  Inter boundary filtering is added
Objective performance
  Average BD-rate reductions of 0.2%, 0.7% and 0.9% for AI, RA and LD chroma components, respectively
Subjective quality
  Similar to HM5.0
Decoding time is almost the same as that of HM5.0
<number>

## Slide 8
Thank you
Notes: <number>