## Slide 1: Non-CE4: Clipping of Transformed Coefficients before De-quantization
Xiang Li, Xun Guo and Shawmin Lei
MediaTek
JCTVC-H0312
Presented by Xun Guo
8th JCT-VC Meeting in Geneva
1-10, Feb., 2012
Notes: <number>

## Slide 2: Summary
To solve the potential dynamic range overflow in de-quantization process
  Discussed by BoG of quantization in Geneva meeting
  When quantization matrix is used, the dynamic range of de-quantization process may exceed 32 bits
Propose to clip level value before de-quantization
<number>

## Slide 3: De-quantization with Quantization Matrix
iShift = M-1+DB+4
if (iShift > QP/6)
coeffQ[i][j] = (level[i][j]*W[i][j]*IQ[QP%6] + offset)>>(iShift-QP/6), offset = 1<<(iShift-QP/6-1), with i=0…nW-1, j = 0..nH-1 (1)
else
coeffQ[i][j] = (level[i][j]*W[i][j]*IQ[QP%6]) << (QP/6-iShift), with i=0…nW-1, j = 0..nH-1 (2)
  M=log2(N), N stands for transform size
  DB=B-8, B is the bit-depth of input video
  level represents quantized transformed coefficient (16-bit)
  IQ(x) indicates de-quantization step (7-bit)
  W denotes quantization matrix (8-bit)
The dynamic range of the de-quantization process in (2) can be modeled as
L+W+IQ[QP%6]+QP/6-M+DB-3, where L is level value (3)
<number>

## Slide 4: Issue Analysis
When QP≥48, M=2 (4x4 transform) and DB=0 (8-bit video), the dynamic range of (3) is 16+8+6+3=33 bits => overflow may occur in de-quantization process
Such overflow may be introduced by transmission error or generated by “evil” encoder – The overflow shall be avoided at decoder
<number>

## Slide 5: Proposed Method
Limit the range of (3) by
L+W+IQ[QP%6]+QP/6-M+DB-3 ≤ 32
Considering overflow occurs only when QP/6=8, M=2, DB=0
L+8+6+QP/6-M-3 ≤ 32
=> L ≤ 21-QP/6+M
Clipping the level before de-quantization
if (21-QP/6+M≥16)
level = max( -215, min(215-1, level))
else
level = max( -220-QP/6+M, min(220-QP/6+M-1, level))
<number>

## Slide 6: Simulation Results
HM-5.0-QM (rev1710), default quantization matrices
<number>

## Slide 7: Conclusions
Thank Microsoft for crosschecking – JCTVC-H0366
Potential overflow in de-quantization process is avoided
No impact on coding performance under common test conditions
Essentially, only a code revision of several lines is needed
Propose to adopt it into WD and HM software
<number>

## Slide 8
Thank you
Notes: <number>