## Slide 1: AHG15: On Signaling of Several Syntax Elements in SPS
Xiang Li, Jicheng An, Xun Guo and Shawmin Lei
MediaTek
JCTVC-H0313
Presented by Xun Guo
8th JCT-VC Meeting in Geneva
1-10, Feb., 2012
Notes: <number>

## Slide 2: HM5.0: CU & TU Size Information in SPS
seq_parameter_set_rbsp( ) { | Descriptor
profile_idc | u(8)
… | 
log2_min_coding_block_size_minus3 | ue(v)
log2_diff_max_min_coding_block_size | ue(v)
log2_min_transform_block_size_minus2 | ue(v)
log2_diff_max_min_transform_block_size | ue(v)
log2_min_pcm_coding_block_size_minus3 | ue(v)
max_transform_hierarchy_depth_inter | ue(v)
max_transform_hierarchy_depth_intra | ue(v)
… | 
rbsp_trailing_bits( ) | 
} | 
<number>
CU size: 8x8-64x64, 2-3 bits
min TU size < min CU size
TU size: 4x4-32x32, 2 bits

## Slide 3: log2_diff_max_min_coding_block_size
Difference between maximum and minimum CU sizes
CU sizes in HM5.0: 8x8 ~ 64x64
Difference between max/min CU sizes: 0~3
2 or 3 bits should be sufficient
Proposal
  Use fix-length coding instead of vlc
  ue(v) => u(2)/u(3)
<number>

## Slide 4: log2_min_transform_block_size_minus2
Minimum TU size
Minimum TU size should be no larger than minimum CU size
Proposal
  Signal the difference between the minimum TU size and minimum CU size
  log2_min_cu_size_minus_min_tu_size
<number>

## Slide 5: log2_diff_max_min_transform_block_size
Difference between maximum and minimum TU sizes
TU sizes in HM5.0: 4x4 ~ 32x32
Difference between max/min TU sizes: 0~3
2 or 3 bits should be sufficient
Proposal
  Use fix-length coding instead of vlc
  ue(v) => u(2)/u(3)
<number>

## Slide 6: max_transform_hierarchy_depth_inter
Maximum RQT depth for inter
TU sizes in HM5.0: 4x4 ~ 32x32
Range of RQT depth for inter: 1~4
max_transform_hierarchy_depth_inter_minus1 is actually used in HM5.0
2 bits should be sufficient
Proposal
  Use fix-length coding instead of vlc
  ue(v) => u(2)
<number>

## Slide 7: max_transform_hierarchy_depth_intra
Maximum RQT depth for intra
TU sizes in HM5.0: 4x4 ~ 32x32
Range of RQT depth for intra: 1~4
max_transform_hierarchy_depth_intra_minus1 is actually used in HM5.0
2 bits should be sufficient
Proposal
  Use fix-length coding instead of vlc
  ue(v) => u(2)
<number>

## Slide 8: Proposed Revisions in SPS
<number>

## Slide 9: Conclusions
Signaling of maximum/minimum CU and TU size information is improved
The implicit constraints between minimum CU and TU sizes are included into the semantics so that improper TU and CU size settings in practice can be avoided
Propose to adopt the revisions into WD and HM software
<number>

## Slide 10
Thank you
Notes: <number>