## Slide 1
www.hisilicon.com
The Right silicon for your next BIG idea
Layered quantization matrices representation and compression
Yunfei Wang, Tsinghua
Jianhua Zheng, HiSilicon
Yun He, Tsinghua
JCTVC-G314

## Slide 2: Outline
Summary of the contribution
Layered Quantization Matrix coding
Experimental Results
Conclusions

## Slide 3: Summary of the contribution
Layered quantization matrix representation and coding structure.
Matrix is represented as coded layers and predicted layers, matrix coefficients are divided into multiple layers.
By changing the number of coded layers, it easily shift from matrix lossless coding to matrix lossy coding with high compression ratio.
Support a large range variation of compression ratio.
-1.87 x (lossless), 4.5x (1.7) 10.87x(2.87) 20.26x(4.23)
-1.96 x(lossless), 4.47x(0.54) 9.94x(1.38), 17.59x (2.83)
Crosscheck by JCTVC-H0231 (SONY) and JCTVC-H0152 (Canon)

## Slide 4: Layered quantization matrices representation and compression
matrix coefficients are divided into multiple layers.
Two types layers: Coding matrix from lower layers to higher layers
coded layer – residue of the predicted value and the original element is coded.
predicted layer – residue in higher layer is not coded to reduce the generated bits.
4x4 matrix, layer: 0~3
8x8 matrix, layer: 0~4
16x16 matrix, layer: 0~5
32x32 matrix, layer: 0~6
NxN matrix, layer: 0~log2N+1
layers for quantization matrix

## Slide 5: Layered quantization matrices representation and compression
Prediction:
Stage 1: vertical stage. if it can be vertical interpolated, then element is vertical interpolated by reference elements R1 and R2, (R1 and R2 are the nearest coded elements in the same column).
Stage 2: horizontal stage. The rest elements are predicted by horizontal interpolation. (R1 and R2 are the nearest coded elements in the same row)
interpolation within the stage can be paralleled.
Interpolation (take layer 3 as an example):
( R1 + R2 + 1 ) >>1
( 4R1 + 2R2 + 3 ) / 6

## Slide 6: Layered quantization matrices representation and compression
  Copy mode
  - Matrix is derived directly from its reference matrix One bit is signaled
  - Down sampling in copy mode: the elements with even indexes are extracted directly from the reference matrix.
  Symmetry mode: half of the elements are coded. One bit is signaled
  Differential coding:
  differential coding between two adjacent matrix sets is employed, the values in the differential matrix are coded.

## Slide 7: Layered quantization matrices representation and compression

## Slide 8: Experimental results
  TEST1: only the coding performance of matrix itself is measured
Average(symmetry QMs) | Average(anchor) | lossless | lossy opt1 | lossy opt2 | lossy opt3
Total Bit | 9595.05 | 3768.20 | 1646.20 | 748.80 | 425.80
MaxError | 0.00 | 0.00 | 23.60 | 29.20 | 33.60
AvgError | 0.00 | 0.00 | 0.62 | 1.54 | 2.97
compression ratio(anc/pro) | 1.00 | 2.43 | 5.50 | 12.12 | 21.21
Subtest2.4, symmetry QM results

## Slide 9: Experimental results
  TEST1: only the coding performance of matrix itself is measured
Chart: compression ratio_vs_error
| 0 | 0 | 0.61535439999999997 | 1.5360727999999999 | 2.9685039999999998
compression ratio(anc/pro) | 1 | 2.4289 | 5.5035 | 12.1214 | 21.2073
Chart: AvgError_vs_QM bits
| 9595.0499999999993 | 3768.2 | 1646.2 | 748.8 | 425.8
compression ratio(anc/pro) | 0 | 0 | 0.61535 | 1.5361 | 2.9685
symmetry QM results

## Slide 10: Experimental results
  TEST1: only the coding performance of matrix itself is measured
Average(asymmetry QMs) | Average(anchor) | lossless | lossy opt1 | lossy opt2 | lossy opt3
Total Bit | 9536.21 | 6418.60 | 2783.60 | 1228.20 | 677.00
MaxError | 0.00 | 0.00 | 8.60 | 15.00 | 17.80
AvgError | 0.00 | 0.00 | 0.46 | 1.23 | 2.68
compression ratio(anc/pro) | 1.00 | 1.50 | 3.44 | 7.76 | 13.97
Subtest2.4, asymmetry QM results

## Slide 11: Experimental results
  TEST1: only the coding performance of matrix itself is measured
asymmetry QM results
Chart: compression ratio_vs_error
| 0 | 0 | 0.46343500000000004 | 1.2270175999999999 | 2.6835630000000004
compression ratio(anc/pro) | 1 | 1.4988 | 3.4374 | 7.758 | 13.9651
Chart: AvgError_vs_QM bits
| 9536.2071428571417 | 6418.6 | 2783.6 | 1228.2 | 677
AvgError | 0 | 0 | 0.46344 | 1.227 | 2.6836

## Slide 12: Conclusions
The main feature of this approach,
only one pass processing need to compress the quantization matrices, so the encoding time and design complexity to compress quantization matrix are very low.
controlling the number of coded layers, it is easily shift from matrix lossless coding to matrix lossy coding with high compression ratio.
If a small error affordable, the lossy coding approach will reach high compression ratio.
The proposed approach is comparable with both lossless QM coding and lossy QM coding
Recommendation:
Support both lossless and lossy method in quantization matrix coding.
Continue investigate improving the compression ratio of quantization matrix and support layered quantization matrix representation and coding in HM6.

## Slide 13
Thank you!
www.hisilicon.com