## Slide 1: JCTVC-H0321 AHG18: Resolution Adaptation Coding (ARC) using single resolution in DPB
P.Bordes
8th JCTVC Meeting: San-José, Feb. 1st-10th, 2012

## Slide 2: AHG18: Adaptive Resolution Coding (ARC) study
  Current implementation (HM5.0-ARC) requires both resolutions in DPB
    Increase DPB memory size
  AHG18-mandate 5:
    “Determine the necessity of keeping both resolutions in buffer and suitable limitations on DPB for managing complexity “
  Proposal
    Use single (reconstructed) resolution in DPB
    Frame Resolution Adaptation done “on the fly”
    at prediction stage.

## Slide 3: Approach
  Reference Pictures up/down sampling filters are separable
  Motion Compensation Interpolation filters are separable
  Pred(xcur,ycur) = [ MCIH(fracx) o MCIV(fracy) o SCV(y) o SCH(x) ] (refPic(xref,yref))
SCV(y) o SCH(x)
MCIH(fracx) o MCIV(fracy)

## Slide 4: Approach (2)
  Reference Pictures up/down sampling filters are separable
  Motion Compensation Interpolation filters are separable
  Pred(xcur,ycur) = [ MCIH(fracx) o MCIV(fracy) o SCV(y) o SCH(x) ] (refPic(xref,yref))
  Separable filters can be permutted
  Pred(xcur,ycur) = [MCIV(fracy) o SCV(y) o MCIH(fracx) o SCH(x) ] (refPic(xref,yref))

## Slide 5: Filters…
5
JCTVC-H0289
  Up-Sampling
    { 0, 64, 0, 0} phase 0
    {-8, 40, 40, -8} phase 1
  Down-Sampling
    {1, 3, -7, -15, 33, 113, 113, 33, -15, -7, 3, 1} half phase
  Interpolation (luma)
    { 0, 0, 0, 64, 0, 0, 0, 0 }, frac 0
    { -1, 4, -10, 58, 17, -5, 1, 0 }, frac 1
    { -1, 4, -11, 40, 40, -11, 4, -1 }, frac 2
    { 0, 1, -5, 17, 58, -10, 4, -1 } frac 3
  Interpolation + scaling (luma)
phase | frac | N | shiftz
0 | 0 | 4 | 7
 | 1 | 5 | 13
 | 2 | 5 | 13
 | 3 | 5 | 13
1 | 0 | 4 | 7
 | 1 | 5 | 13
 | 2 | 5 | 13
 | 3 | 5 | 13
frac | N | shiftz
0 | 6 | 8
1 | 13 | 14
2 | 13 | 14
3 | 13 | 14

## Slide 6: Results
6
JCTVC-H0289
  LP and LB configurations
    High-to-Low and Low-to_High, 9 frames

## Slide 7: Results
7
JCTVC-H0289
  LP and LB configurations
    High-to-Low and Low-to_High, 9 frames
  RA configurations
    High-to-Low and Low-to_High, 16 frames

## Slide 8: Results
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -1,0% | -4,8% | -5,2% | -1,2% | -4,2% | -5,1%
Class B | -1,7% | -6,7% | -6,4% | -1,2% | -5,4% | -5,2%
Class C | -1,1% | -2,9% | -3,4% | -1,0% | -2,4% | -3,1%
Class D | -2,3% | -4,7% | -4,5% | -1,7% | -4,9% | -4,0%
Class E |  |  |  |  |  | 
Class F | -2,8% | -5,0% | -4,2% | -2,2% | -4,1% | -4,3%
Overall | -1,6% | -4,9% | -4,9% | -1,3% | -4,3% | -4,3%
 | -1,6% | -4,9% | -4,9% | -1,4% | -4,4% | -4,2%
Enc. Time | 128% |  |  | 137% |  | 
Dec. Time | 150% |  |  | 152% |  | 
 | Low Delay B - HE |  |  | Low Delay B - LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -1,0% | -3,7% | -4,0% | -1,4% | -4,9% | -4,2%
Class C | -0,8% | -2,7% | -1,9% | -0,9% | -1,2% | -1,6%
Class D | -0,8% | -2,4% | -1,8% | -1,1% | -3,7% | -2,4%
Class E | -2,8% | -9,0% | -6,1% | -3,7% | -8,8% | -7,6%
Class F | -1,4% | -3,1% | -2,1% | -0,7% | -3,2% | -1,6%
Overall | -1,3% | -3,9% | -3,1% | -1,4% | -4,2% | -3,3%
 | -1,3% | -3,9% | -3,1% | -1,4% | -4,2% | -3,4%
Enc. Time | 117% |  |  | 121% |  | 
Dec. Time | 131% |  |  | 138% |  | 
 | Low Delay P - HE |  |  | Low Delay P - LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -1,1% | -5,2% | -5,0% | -1,2% | -5,6% | -5,1%
Class C | -0,5% | -2,3% | -1,5% | -0,6% | -1,1% | -1,3%
Class D | -1,0% | -2,8% | -2,4% | -1,9% | -3,4% | -3,8%
Class E | -3,6% | -9,9% | -7,1% | -4,8% | -9,5% | -8,0%
Class F | -1,0% | -2,4% | -0,6% | -1,3% | -2,5% | -2,8%
Overall | -1,3% | -4,3% | -3,2% | -1,8% | -4,2% | -4,1%
 | -1,4% | -4,3% | -3,1% | -1,8% | -4,3% | -4,1%
Enc. Time | 112% |  |  | 115% |  | 
Dec. Time | 133% |  |  | 138% |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0,1% | -0,2% | -0,6% | -0,1% | -0,9% | -0,8%
Class B | -0,3% | -1,2% | -1,0% | -0,5% | -0,9% | -0,5%
Class C | -0,2% | -0,7% | -0,2% | -0,1% | -1,1% | -1,2%
Class D | -0,2% | 0,3% | 1,4% | 0,0% | -0,1% | -1,0%
Class E |  |  |  |  |  | 
Class F | 0,0% | 0,0% | -0,9% | 0,2% | 0,6% | -0,9%
Overall | -0,2% | -0,5% | -0,1% | -0,2% | -0,7% | -0,9%
 | -0,2% | -0,9% | 0,3% | -0,2% | -0,7% | -0,7%
Enc. Time | 119% |  |  | 122% |  | 
Dec. Time | 126% |  |  | 133% |  | 
 | Low Delay B - HE |  |  | Low Delay B - LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0,1% | -0,7% | -0,9% | -0,4% | -1,0% | -0,9%
Class C | -0,2% | -0,5% | 0,7% | 0,0% | 0,2% | -0,2%
Class D | -0,2% | -0,7% | 0,4% | 0,2% | -2,1% | -1,1%
Class E | -0,7% | -1,9% | -1,7% | -0,7% | -0,9% | -2,0%
Class F | 0,2% | -0,1% | 0,0% | 0,3% | -0,2% | 0,3%
Overall | -0,2% | -0,7% | -0,3% | -0,1% | -0,8% | -0,7%
 | -0,2% | -0,8% | -0,1% | -0,1% | -0,8% | -0,6%
Enc. Time | 114% |  |  | 114% |  | 
Dec. Time | 125% |  |  | 128% |  | 
 | Low Delay P - HE |  |  | Low Delay P - LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0,2% | -0,7% | -0,9% | -0,4% | -0,7% | -0,7%
Class C | -0,3% | -0,5% | 0,6% | -0,2% | 0,1% | -0,4%
Class D | -0,2% | -1,0% | -0,1% | -0,2% | -1,4% | -1,1%
Class E | -0,6% | -2,2% | -2,0% | -0,5% | -1,3% | -2,1%
Class F | -0,1% | 0,6% | -0,4% | 0,2% | 0,2% | -15,2%
Overall | -0,3% | -0,7% | -0,5% | -0,2% | -0,6% | -3,8%
 | -0,3% | -0,8% | -0,3% | -0,2% | -0,8% | -0,7%
Enc. Time | 111% |  |  | 112% |  | 
Dec. Time | 124% |  |  | 128% |  | 
High to Low (part2)
Low to High (part1+part2)

## Slide 9: Conclusion
  Propose a solution to keep only single (reconstructed) resolution in DPB
    Modify MV interpolation filters
    Reduce DPB size requirements at Decoder side (ME still use both resolutions for SAD)
    Improves original HM5.0_ARC gains
    Can be extended to non-dyadic up/down sampling
    Decoder (and encoder) complexity is increased
      => Reduction of ARC Filters length may be studied