## Slide 1
H0336 – CE4 Subtest 4.1: Higher granularity of quantization parameter scaling
Tammy Lee, Jeonghoon Park
Samsung Electronics Co., Ltd
Feb. XX, 2012
Notes: <number>

## Slide 2: Introduction
The quantization step size (QStep) of HEVC Test Model
  QStep increases by approximately 12.25% with each increment of QP
  QStep doubles when QP is increased by 6
  QStep mapping is too coarse for fine and accurate rate/quality control
  QStep mapping is not flexible to fit different application scenario
Proposed adaptive delta QP signaling on higher granularity of quantization
  It is proposed to have new syntax to signal delta QP scale
  To support the finer granularity as well as the original granularity, the granularity of quantization is doubled
<number>

## Slide 3: High granularity QStep mapping (1)
A straightforward extension of current Qstep mapping
  Double QP scaling accuracy
  Qstep increases by approximately 5.95% with each increment of QP
  Qstep doubles when QP is increased by 12
Quantiser process
  Inverse quantiser
Advantage of straightforward extension
  Easy adaptation of other modules that is related to QP
    Deblocking filter
    CABAC context model initialization
    Lambda value (Encoder side)
<number>
, with QP = 0…103
Yij = (Zij * DeqScaleij(QP % 12) << (QP/12)) >> dqbits
DeqScale[12] = {40, 42, 45, 48, 51, 54, 57, 60, 64, 68, 72, 76}
, with QP = 0…51
12
8

## Slide 4: Adaptive delta QP signaling (1)
To support the flexibility between better rate/quality control and dQP bits overhead, new syntax to signal delta QP scale is proposed
  Slice level QP can be kept as highest level always
  QP of current CU calculated as
  dQP_Scale controls CU-level QP update speed
  dQP=1 with different dQP_Scale
    dQP_Scale = 1  Qstep increase 5.95%
    dQP_Scale = 2  Qstep increase 12.25%
<number>
QP_curr = QP_pred + dQP * dQP_Scale
dQP=1 with different dQP_Scale
dQP_Scale = 2
dQP_Scale = 1
QP_pred
QP_pred+1
QP_pred+2

## Slide 5: Adaptive delta QP signaling (2)
To emulate current HEVC QP mapping solution,
  Set Slice QP = even value (: doubled value of 22, 27, 32, 37) and dQP_scale = 2
Example of CU-level QP update speed
  Slice QP = even and dQP_Scale = 1 or 2
dQP_Scale = 2
dQP_Scale = 1
QP 0 1 2 3 4 5 6 7 8 9 10 11 …
Qstep 0.625 0.6875 0.8125 0.875 1 1.125 1.25 1.375 1.625 1.75 2 2.25 …
QP 0 2 4 6 8 10 12 14 16 18 20 22 …
Qstep 0.625 0.6875 0.8125 0.875 1 1.125 1.25 1.375 1.625 1.75 2 2.25 …
<number>

## Slide 6: Experimental result
Experiment on HM5.0
  Common test configuration QP 44 54 64 74 ( equivalent to 22, 27, 32, 37 in HM5.0)
  Additional test with QP+1 45 55 65 75 ( equivalent to 22.5, 27.5, 32.5, 37.5 in HM5.0)
  Bit rate difference (QP+1) vs QP
    Avg. 15.8  7.6%
     When slice-based QP control is enabled, the higher granularity supports fine and accurate rate/quality control
<number>
 | Results | AIHE | AILC | RAHE | RALC | RAHE10 | LBHE | LBLC | Avg
HM5 | BD-rate-Y | -0.3% | -0.3% | 0.2% | 0.2% | 0.4% | 0.3% | 0.3% | 0.1%
 | dBitRate | -11.2% | -10.6% | -17.7% | -16.8% | -16.2% | -19.6% | -18.7% | -15.8%
Prop. | BD-rate-Y | 0.6% | 0.8% | 0.6% | 0.6% | 0.7% | 0.6% | 0.5% | 0.6%
 | dBitRate | -4.9% | -4.8% | -8.5% | -8.0% | -8.0% | -9.7% | -9.2% | -7.6%

## Slide 7: Summary
Double the QStep granularity of HEVC
  12.25% -> 5.95% QStep increase with each QP increment
  Avg. 15.8% ->7.6% bit difference with each QP difference by 1
Adaptive delta QP signalling with dQP_Scale in slice header
  Control CU level QStep/QP update speed
    Trade-off of better rate/qualilty control and dQP bits overhead
  Slice level high QP mapping granularity
  Easy adaptation of other modules that is related to QP
<number>

## Slide 8
Thank you !
<number>