## Slide 1: Line memory reduction fix for independent slices and tiles
Semih Esenlik
Ann-Kathrin Seifert
Matthias Narroschke
Thomas Wedi
Panasonic Corporation
8th JCT-VC meeting, San Jose 01.-10. February 2012

## Slide 2: Outline
Background:
Loop filtering across slice and tile boundaries.
Problem:
Application of double padding at independent tile/slice boundaries.
Proposal
Results

## Slide 3
Loop filtering accross slice/tile boundaries
Two flags in the SPS to control the loop filters at tile and slice boundaries:
  loop_filter_across_slice_flag
  loop_filter_across_tile_flag
If loop_filter_across_slice_flag is 0, loop filters do not cross slice boundaries.
Similar situation for loop_filter_across_tile_flag.

## Slide 4
Line memory at independent slice and tile boundaries
Example (loop_filter_across_slice_flag is equal to 0):
  During the processing of LCU 8 with ALF, pixels from LCU 14 are not required.
  During the processing of LCU 14 with ALF, pixels from LCU 8 are not required.
If loop_filter_across_slice_flag is 0; no line memory required for ALF along slice boundaries.
If loop_filter_across_tile_flag is 0; no line memory required for ALF along tile boundaries.

## Slide 5
Problem
Double padding occurs at independent slice and tile boundaries.
Virtual Boundary padding is applied on top of boundary padding although it is not actually required.

## Slide 6
Proposal
Two simple rules are included in Virtual Boundary padding operation for line memory reduction:
  If loop_filter_across_slice_flag is 0, then Virtual Boundary padding is not applied at horizontal slice boundaries.
  If loop_filter_across_tile_flag is 0, then Virtual Boundary padding is not applied at horizontal tile boundaries.
*Remark: Virtual Boundary padding is currently not applied at frame boundaries already.

## Slide 7
Proposal
In the slice header following syntax element is signalled:
num_sgu_alf_padding: Number of Slice Granularity Units that lie at a bottom LCU where VB processing is applied.
num_sgu_alf_padding is signalled in order to facilitate LCU-based decoding.
If num_sgu_alf_padding is not signalled, it is not possible to know whether an LCU lies at a bottom slice boundary in LCU-based decoding.

## Slide 8: Simulation results: Multiple tiles mode
HM5.1 is used in simulations:
Tiles mode: Each LCU row is a tile.

## Slide 9: Simulation results: Multiple slices mode
HM5.1 is used in simulations:
Slice mode: Each LCU row is a slice.

## Slide 10: Visual analysis, multiple tiles
Sequence: RaceHorses, LD HE,
QP 37, frame no. 251
HM5.1
Proposal
PROPOSAL

## Slide 11: Visual analysis, multiple tiles
Sequence: RaceHorses, RA_HE, QP32, frame 74
HM5.1
PROPOSAL

## Slide 12: Visual analysis, multiple tiles
Sequence: BQMall, RA_HE, QP37, frame 347
HM5.1
PROPOSAL

## Slide 13: Conclusion
Problem:
  Double padding at independent slice and tile boundaries. At independent slice and tile boundaries boundary padding and VB padding are applied at the same time.
Proposal:
  Switch off VB padding at independent slice and tile boundaries, since no line memory is required.
Benefits:
  Coding gain 0.2% for independent tiles and 0.1% for independent slices.
  Improvement in the subjective quality.