## Slide 1: Low-delay support for APS
Semih Esenlik
Matthias Narroschke
Virginie Drugeon
Thomas Wedi
Panasonic Corporation
8th JCT-VC meeting, San Jose 01.-10. February 2012

## Slide 2: Outline
Background: LCU-based ALF and SAO.
Problem: Coding loss in LCU-based ALF/SAO in the case of multiple slices per picture.
Proposal: Low-Delay APS fragmentation
Conclusion

## Slide 3: Background: LCU-based ALF/SAO
Generate
Filter 1
Reuse
Filter 1
Reuse
Filter 1
Reuse
Filter 1
Generate
Filter 2
Reuse
Filter 2
Reuse
Filter 1
Reuse
Filter 2
List of filters for reuse
Filter 1
Filter 2
LCU-based filter parameter estimation instead of frame-based estimation.
Each LCU can either:
  Generate new filter coefficients or
  Reuse filters that are generated in a previous LCU.
Frame

## Slide 4: Problem of LCU-based ALF/SAO
Generate
Filter 1
Reuse
Filter 1
Reuse
Filter 1
Reuse
Filter 1
Generate
Filter 2
Reuse
Filter 2
Reuse
Filter 1
Reuse
Filter 2
In the LCU-based SAO and ALF approaches filter parameters are signalled in the slice header or interleaved within the LCU data.
At the slice boundaries the spatial prediction mechanism has to be broken.
Problem: Reduction in the SAO and ALF coding gain due to the fact that reuse of filters among slices is not possible.
Slice 1
Slice 2

## Slide 5: Problem: Coding results for H0274
 | One slice per picture | Multi slice per picture | Number of slices per frame | Coding loss due to filter table refresh
Class B | 1.8% | 3.1% | 8 | 1.3%
Class E | 1.2% | 1.5% | 2 | 0.3%
Class F | 1.7% | 2.1% | 4 | 0.4%
Following table presents the coding loss of H0274* compared to HM5.0.
H0274 utilizes LCU-based ALF and SAO filter parameter estimation.
Coding gain of ALF and SAO drops as the number of slices per picture increases.
Coding loss in the last column stems from the fact that filters cannot be reused in the following slice.
*CE8.a.4: One-stage/Two-stage SAO and ALF with LCU-based syntax

## Slide 6: Proposal: Low-delay APS fragmentation
Current LCU-based ALF/SAO proposals:
Coding of ALF/SAO data within each slice and no sharing of ALF/SAO data between slices.
Problem:
Significantly reduced coding efficiency for multiple slices per picture.
Solution:
Coding of ALF/SAO data in APS fragments, which share ALF/SAO data.

## Slide 7: Proposal: Low-delay APS fragmentation
Additional syntax element APS_inner_id to identify APS fragments.
The first APS fragment (identified by APS_inner_id == 0) is similar to current APS model, it carries:
  Deblocking
  Q-matrix
  SAO and ALF parameters
Additional SAO and ALF parameters are sent in following fragments as they are available.
All the slices in a frame has to refer to same APS_id.
If a slice refers to [APS_id = M, APS_inner_id = N], all APS fragments with APS_id = M and APS_inner_id <= N are activated.

## Slide 8: Example 1
Generate
Filter 1
Reuse
Filter 1
Reuse
Filter 1
Reuse
Filter 1
Generate
Filter 2
Slice 1
Slice 2
Reuse
Filter 2
Reuse
Filter 2
Reuse
Filter 3
Reuse
Filter 1
Reuse
Filter 2
Reuse
Filter 3
APS_id 1, APS_inner_id 0
QMATRIX_param
DB_param
Filter 1
Filter 2
APS_id 1, APS_inner_id 1
Filter 3
Generate
Filter 3
First APS fragment is transmitted as soon as the encoding of slice 1 is complete.
Additional filter parameters are sent in fragments.
APS fragments can be scheduled according to delay requirements.

## Slide 9: Example 1, combined parameter lists
Generate
Filter 1
Reuse
Filter 1
Reuse
Filter 1
Reuse
Filter 1
Generate
Filter 2
Slice 1
Slice 2
Reuse
Filter 2
Reuse
Filter 2
Reuse
Filter 3
Reuse
Filter 1
Reuse
Filter 2
Reuse
Filter 3
Combined parameters list
QMATRIX_param
DB_param
Filter 1
Filter 2
Generate
Filter 3
Combined parameter sets are constructed by appending fragments.
Slice 2 can now reuse filters 1 and 2 from slice 1, since they are in its combined parameters list.
Combined parameters list
QMATRIX_param
DB_param
Filter 1
Filter 2
Filter 3

## Slide 10: Example 2
Generate
Filter 1
Reuse
Filter 1
Reuse
Filter 1
Reuse
Filter 1
Generate
Filter 2
Slice 1
Slice 2
Reuse
Filter 2
Reuse
Filter 2
Reuse
Filter 3
Reuse
Filter 1
Reuse
Filter 2
Reuse
Filter 3
APS_id 1, APS_inner_id 0
QMATRIX_param
DB_param
Filter 1
Filter 2
Filter 3
Generate
Filter 3
Fragmentation is based on the delay requirements. In the current example no fragmentation is done.
Possible scenario: Picture based filter estimation.
As opposed to signalling parameters in the slice, slice 2 can reuse filters 1 and 2.

## Slide 11: Conclusion
Problem:
  Signalling of ALF and SAO parameters in the slice header causes significant coding loss in the case of LCU-based ALF and SAO approaches.
Proposal:
  Move shared SAO and ALF parameters to the APS. Keep LCU-specific information in the slice.
  Provide a fragmentation scheme for APS.
Benefit:
  Eliminate the coding loss due to partitioning of a frame into multiple slices for ALF and SAO.

## Slide 12: Syntax

## Slide 13: Syntax

## Slide 14: Syntax