## Slide 1: AHG 15: SPS and PPS syntax modifications
Virginie Drugeon, Viktor Wahadaniah, Matthias Narroschke, Thomas Wedi
Panasonic Corporation
8th JCT-VC meeting, San Jose, 1-10 February 2012
Notes: Jul 31, 2026
<number>

## Slide 2: Outline
Block size signalling
Slice granularity
Proposed SPS syntax
Conclusion

## Slide 3: Block size signalling
List of syntax elements related to block sizes in the SPS:
Current coding in working draft 5:
Block size |  | Range of possible values (common test conditions)
Minimum CU size | MinCU or SCU | 8x8 / 16x16 / 32x32 / 64x64 / 128x128?
Maximum CU size | MaxCU or LCU | 16x16 / 32x32 / 64x64 / 128x128?
Minimum transform size | MinTr | 4x4 / 8x8 / 16x16 / 32x32
Maximum transform size | MaxTr | 4x4 / 8x8 / 16x16 / 32x32
Minimum PCM CU size | MinPCMCU | 8x8? / 16x16 / 32x32
Maximum PCM CU size | MaxPCMCU | 8x8? / 16x16 / 32x32
log2_min_coding_block_size_minus3 | ue(v)
log2_diff_max_min_coding_block_size | ue(v)
log2_min_transform_block_size_minus2 | ue(v)
log2_diff_max_min_transform_block_size | ue(v)
if ( pcm_enabled_flag ) { | 
log2_min_pcm_coding_block_size_minus3 | ue(v)
log2_diff_max_min_pcm_coding_block_size | ue(v)
} | 

## Slide 4: Block size signalling
Relationships between the block sizes:
Proposal:
  Use the dependencies between the block sizes to code them
  Code the LCU size first with log2_max_coding_block_size_minus4

## Slide 5: Slice granularity
Syntax element slice_granularity in PPS:
  Is coded using fixed length code
  Values depend on the selected minimum and maximum CU sizes
  Value 0 is
    more probable
    the only possible value for several combinations
Proposals for improvement:
  Proposal 1:
    Move slice_granularity to SPS
    Use truncated Golomb codes to signal
    Use dependency to selected SCU and LCU sizes
  Proposal 2:
    Use exp-Golomb codes to signal

## Slide 6: Proposed SPS syntax
seq_parameter_set_rbsp( ) { | Descriptor
… | 
log2_max_coding_block_size_minus4 | ue(v)
log2_diff_min_max_coding_block_size | ue(v)
log2_diff_max_transform_block_coding_block_size | ue(v)
log2_diff_min_max_transform_block_size | ue(v)
if ( pcm_enabled_flag ) { | 
log2_diff_max_pcm_coding_block_size | ue(v)
log2_diff_max_min_pcm_coding_block_size | ue(v)
} | 
max_transform_hierarchy_depth_inter | ue(v)
max_transform_hierarchy_depth_intra | ue(v)
chroma_pred_from_luma_enabled_flag | u(1)
loop_filter_across_slice_flag | u(1)
sample_adaptive_offset_enabled_flag | u(1)
adaptive_loop_filter_enabled_flag | u(1)
if ( pcm_enabled_flag ) | 
pcm_loop_filter_disable_flag | u(1)
temporal_id_nesting_flag | u(1)
inter_4x4_enabled_flag | u(1)
if ( log2_max_coding_block_size_minus4 != 0 && log2_diff_min_max_coding_block_size != 0 ) | 
slice_granularity | te(v)
… | 
rbsp_trailing_bits( ) | 
} | 

## Slide 7: Conclusion
A modified syntax is proposed for
  Block sizes coding
  Slice granularity coding
Advantages of the proposed syntax:
  Cleaner design:
    Wrong block sizes combinations cannot be signalled anymore
    Wrong values of slice granularity cannot be signalled anymore
  Coding redundancies removed