## Slide 1: APS partial update
Virginie Drugeon, Semih Esenlik, Viktor Wahadaniah, Matthias Narroschke, Thomas Wedi
Panasonic Corporation
8th JCT-VC meeting, San Jose 01.-10. February 2012
Notes: Jul 29, 2026
<number>

## Slide 2: Outline
Parameter sets partial update: state of the art
Proposal
Proposed APS syntax
Conclusion

## Slide 3: State of the art
Currently proposed approaches for partial update:
Drawbacks of these approaches:
  What information is copied from where?  rules are needed!
  Long chain of references are not robust to errors
Multiple APS referenced in slice header | Copy data from already transmitted APS
Slice header
APS 1
APS 2
APS n
Slice header
APS 1
APS 2
APS n

## Slide 4: Proposal
Slice header: only one APS id signaled
Inside APS for each set of data (Q-matrix, SAO, ALF, ...):
  „copy“ flag to know whether a new parameter set signalled or the parameter set is copied from another APS
  reference to other APS to know where to copy from

## Slide 5: Proposed syntax
Restrictions:
The APS refered to shall not copy the parameters from another APS to avoid long chains of references
An APS shall not refer to itself
aps_rbsp( ) { | Descriptor
aps_id | ue(v)
aps_scaling_list_data_present_flag | u(1)
if ( aps_scaling_list_data_present_flag ) | 
aps_scaling_list_data_copy_flag | u(1)
aps_deblocking_filter_present_flag | u(1)
if ( aps_deblocking_filter_present_flag ) | 
aps_deblocking_filter_copy_flag | u(1)
aps_sample_adaptive_offset_present_flag | u(1)
if ( aps_sample_adaptive_offset_present_flag ) | 
aps_sample_adaptive_offset_copy_flag | u(1)
aps_adaptive_loop_filter_present_flag | u(1)
if ( aps_adaptive_loop_filter_present_flag ) | 
aps_adaptive_loop_filter_copy_flag | u(1)
if( aps_scaling_list_data_present_flag && !aps_scaling_list_data_copy_flag ) | 
scaling_list_param( ) | 
else | 
aps_id_QM | ue(v)
if( aps_deblocking_filter_present_flag && !aps_deblocking_filter_copy_flag ) { | 
disable_deblocking_filter_flag | u(1)
if (!disable_deblocking_filter_flag) { | 
beta_ offset_div2 | se(v)
tc_offset_div2 | se(v)
} | 
} | 
else if(aps_deblocking_filter_present_flag && aps_deblocking_filter_copy_flag ) | 
aps_id_deb | ue(v)
if( aps_sample_adaptive_offset_present_flag && !aps_sample_adaptive_offset_copy_flag ) | 
sao_param( ) | 
else if(aps_sample_adaptive_offset_present_flag && aps_sample_adaptive_offset_copy_flag) | 
aps_id_sao | ue(v)
if( aps_adaptive_loop_filter_present_flag && !aps_adaptive_loop_filter_copy_flag ) | 
alf_param( ) | 
else if(aps_adaptive_loop_filter_present_flag && aps_adaptive_loop_filter_copy_flag) | 
aps_id_alf | ue(v)
rbsp_trailing_bits( ) | 
} | 
Semantics of present flags are changed to indicate whether the tool is used by the refering slice or not.

## Slide 6: Conclusion
Proposal for APS partial update with:
  Introduction of „copy“ flag on top of the „present“ flags
  Direct referencing to other APS
Avantages of the proposed approach:
  Bitrate reduction
  No ambiguities to determine what is copied from where
  Error robustness by avoiding long chains of references