## Slide 1
1
Cheung Auyeung
Sony Electronics Inc.
Feburary 1, 2012
Complexity reduction of significance map coding
JCTVC-H0383
Notes: 1

## Slide 2: Summary
Proposed to reduce the complexity of the coding of significant_coeff_flag by removing a 15 elements lookup table and multiple branches in HM5 and WD5 at a cost of three additional contexts.
Average luminance BDR
 | QP=22,27,32,37 |  |  | QP=12,17,22,27 |  | 
 | HE | LC | HE-10 | HE | LC | HE-10
I | 0.00% | 0.00% |  | -0.01% | 0.00% | 
RA | -0.01% | 0.01% | 0.03% | -0.01% | -0.01% | -0.01%
LB | 0.01% | -0.01% |  | -0.01% | -0.02% | 

## Slide 3: HM5 4x4 Context Assighments
In HM5, the 4x4 significance map has different grouping/mapping for luma and chroma context assignments as indicated by the colors.
  A 15 elements lookup table is used in HM5 and WD5 for the 4x4 chroma context assignments.
  Multiple branches are in HM5 and WD5 to differentiate the luma and chroma context indexes.
0
1
4
5
2
3
4
5
6
6
8
8
7
7
8
0
1
2
4
1
1
2
4
3
3
5
5
4
4
5
grouping/mapping of 4x4 luma context
grouping/mapping of 4x4 chroma context

## Slide 4: Proposed 4x4 Contexts Assignments
0
1
4
5
2
3
4
5
6
6
8
8
7
7
8
0
1
2
4
1b
2
4
3
3
5
5
4a
4a
5
grouping/mapping of 4x4 luma context
grouping/mapping of 4x4 chroma context
1a
Proposed to use the same grouping/mapping for luma and chroma contexts assignments as indicated by the same color in luma and chroma grouping/mapping.
  Contexts 1a, 1b, and 4a are added to the chroma contexts.
  Removed the 15 lookup table in HM5 and WD5 for 4x4 chroma context assignments
  Removed multiple branches in HM5 and WD5 to differentiate the luma and chroma context assignments.

## Slide 5: Simulations and Cross-Checks
Algorithms were integrated into HM5.0 with FIX250.
Simulations were performed in a Microsoft HPC cluster.
  All intra simulations are performed on AMD Opteron Processor 6136 @ 2.4GHz.
  All RA simulations are performed on Intel Xeon X5690 @ 3.47GHz.
  All LD simulations are performed on Intel Xeon X5680 @ 3.33GHz.
Crosschecks are provided by Sharp in JCTVC-H0609.
  Thank you very much.

## Slide 6: BDR at QP=22,27,32,37
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.00% | -0.02% | -0.02% | 0.00% | 0.01% | -0.01% |  |  | 
Class B | 0.00% | -0.03% | 0.01% | 0.00% | 0.00% | 0.03% |  |  | 
Class C | 0.01% | -0.06% | -0.02% | 0.00% | -0.01% | 0.00% |  |  | 
Class D | 0.00% | 0.01% | -0.04% | 0.00% | 0.02% | -0.02% |  |  | 
Class E | 0.00% | 0.00% | 0.00% | 0.00% | 0.02% | -0.02% |  |  | 
Overall | 0.00% | -0.02% | -0.01% | 0.00% | 0.01% | 0.00% |  |  | 
 | 0.00% | -0.02% | -0.01% | 0.00% | 0.01% | 0.00% |  |  | 
Class F | -0.01% | -0.14% | -0.20% | 0.00% | -0.05% | -0.03% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 99% |  |  | 100% |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | -0.03% | -0.11% | -0.21% | 0.00% | 0.07% | -0.17% | 0.03% | 0.15% | 0.13%
Class B | 0.00% | -0.06% | -0.01% | 0.02% | 0.15% | 0.20% | 0.03% | -0.05% | -0.09%
Class C | -0.04% | -0.06% | 0.07% | 0.02% | -0.03% | -0.06% |  |  | 
Class D | 0.03% | -0.19% | 0.08% | -0.01% | 0.31% | -0.24% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | -0.01% | -0.10% | 0.01% | 0.01% | 0.14% | -0.03% | 0.03% | 0.04% | 0.00%
 | -0.01% | -0.13% | 0.01% | 0.01% | 0.11% | -0.07% | 0.04% | 0.07% | 0.05%
Class F | -0.08% | -0.22% | -0.18% | -0.02% | -0.08% | -0.05% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.01% | 0.02% | 0.10% | -0.04% | -0.12% | 0.17% |  |  | 
Class C | 0.01% | -0.01% | 0.09% | 0.03% | 0.08% | 0.06% |  |  | 
Class D | -0.02% | -0.05% | 0.10% | -0.02% | 0.63% | -0.09% |  |  | 
Class E | 0.07% | -0.37% | -0.43% | 0.03% | 0.09% | -0.10% |  |  | 
Overall | 0.01% | -0.08% | 0.00% | -0.01% | 0.16% | 0.03% |  |  | 
 | 0.01% | -0.05% | -0.03% | -0.01% | 0.19% | 0.05% |  |  | 
Class F | -0.08% | -0.31% | -0.18% | 0.08% | -0.03% | 1.06% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 97% |  |  | 99% |  |  |  |  | 

## Slide 7: BDR at QP=12,17,22,27
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | -0.01% | -0.01% | -0.02% | 0.00% | -0.01% | -0.01% |  |  | 
Class B | -0.01% | -0.01% | -0.01% | 0.00% | -0.01% | -0.01% |  |  | 
Class C | -0.01% | -0.01% | 0.01% | 0.01% | 0.00% | 0.01% |  |  | 
Class D | 0.00% | -0.02% | -0.02% | -0.01% | -0.01% | 0.00% |  |  | 
Class E | 0.00% | -0.03% | -0.02% | 0.00% | 0.00% | 0.01% |  |  | 
Overall | -0.01% | -0.02% | -0.01% | 0.00% | -0.01% | 0.00% |  |  | 
 | -0.01% | -0.01% | -0.01% | 0.00% | -0.01% | 0.00% |  |  | 
Class F | -0.07% | -0.09% | -0.13% | -0.02% | -0.05% | -0.02% |  |  | 
Enc Time[%] | #NUM! |  |  | #NUM! |  |  |  |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.00% | 0.03% | -0.09% | 0.00% | 0.03% | 0.03% | -0.02% | 0.00% | -0.03%
Class B | -0.01% | -0.05% | 0.04% | -0.02% | 0.00% | 0.11% | 0.00% | -0.03% | -0.01%
Class C | -0.01% | 0.04% | 0.02% | 0.00% | 0.09% | 0.12% |  |  | 
Class D | 0.00% | -0.03% | -0.06% | -0.02% | 0.07% | 0.11% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | -0.01% | -0.01% | -0.01% | -0.01% | 0.05% | 0.10% | -0.01% | -0.01% | -0.02%
 | -0.01% | -0.02% | 0.00% | -0.01% | 0.04% | 0.10% | -0.01% | -0.01% | 0.01%
Class F | -0.18% | -0.13% | -0.13% | 0.05% | 0.00% | 0.00% |  |  | 
Enc Time[%] | #NUM! |  |  | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  |  | #NUM! |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | -0.01% | -0.02% | 0.01% | -0.02% | 0.05% | 0.14% |  |  | 
Class C | -0.02% | -0.02% | 0.03% | -0.02% | 0.09% | 0.18% |  |  | 
Class D | -0.01% | 0.08% | 0.01% | -0.02% | 0.29% | 0.16% |  |  | 
Class E | -0.02% | -0.18% | 0.27% | -0.01% | 0.40% | 0.08% |  |  | 
Overall | -0.01% | -0.02% | 0.06% | -0.02% | 0.19% | 0.14% |  |  | 
 | -0.01% | -0.03% | 0.07% | -0.02% | 0.19% | 0.15% |  |  | 
Class F | -0.07% | -0.07% | -0.15% | 0.32% | 0.35% | -0.05% |  |  | 
Enc Time[%] | #NUM! |  |  | #NUM! |  |  |  |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  |  |  |  | 

## Slide 8: Conclusion
This proposal removed a 15 elements lookup table and multiple branches to select the context index.
  WD text is also simplified at a cost of three additional contexts
  For both normal QPs and low QPs, the BD-rate for all test cases are from -0.02% to 0.03% .
Proposed to be adopted to HM5.