## Slide 1: New Class E videoconferencing source content
Wonkap Jang, Jill Boyce, Danny Hong, Adeel Abbas
Vidyo Inc.
Notes: <number>

## Slide 2: Background/Objective
Concerns about “Deinterlace” artifacts in the existing Class E sequences were raised by JCT participants
Vidyo was asked to capture new replacement Class E sequences without such artifacts
  An initial test sequence was provided to T. Suzuki, who confirmed that the camera did not create such artifacts, before the provided sequences were captured
<number>
JCTVC-H0389

## Slide 3: Camera Specification
Sony EVI-HD7V
Specification
  Approx. 2M effective pixels
  10x optical zoom
  Shutter speed = 1/60 was used for the capture
  Gain from -3 to +18dB
<number>
JCTVC-H0389
Notes: <number>

## Slide 4: New Sequence Information
Video conferencing scenes
  Camera was mounted on tripod, no panning or zooming
  1, 2, and 4 people present in the sequences
1280x720 60 fps
Sequences
  Johnny_1280x720_60p.yuv
  KristenAndSara_1280x720_60p.yuv
  FourPeople_1280x720_60p.yuv
Encoding bitrates in a similar range, but slightly higher than existing Class E sequences
<number>
JCTVC-H0389

## Slide 5: Still images of sequences
<number>
JCTVC-H0389
Johnny_1280x720_60p.yuv
KristenAndSara_1280x720_60p.yuv
FourPeople_1280x720_60p.yuv

## Slide 6: Encoding Comparison - HE
<number>
JCTVC-H0389
AI-HE |  |  |  |  | 
 | QPISlice | kbps | Y psnr | U psnr | V psnr
Johnny | 22 | 20485.81 | 44.14 | 48.24 | 48.85
 | 27 | 11347.23 | 41.99 | 46.46 | 47.04
 | 32 | 6478.12 | 39.67 | 44.64 | 45.25
 | 37 | 3763.34 | 37.09 | 43.23 | 43.88
KristenAndSara | 22 | 22578.48 | 44.52 | 47.68 | 48.43
 | 27 | 13444.23 | 42.26 | 45.72 | 46.60
 | 32 | 8119.34 | 39.68 | 43.85 | 44.84
 | 37 | 4927.93 | 36.83 | 42.46 | 43.46
FourPeople | 22 | 30714.96 | 43.98 | 47.10 | 48.22
 | 27 | 18764.23 | 41.48 | 44.83 | 46.05
 | 32 | 11505.15 | 38.65 | 42.89 | 44.08
 | 37 | 7016.50 | 35.54 | 41.56 | 42.64
Vidyo1 | 22 | 21465.29 | 44.95 | 47.63 | 48.58
 | 27 | 12545.44 | 42.53 | 45.89 | 46.59
 | 32 | 7473.71 | 39.83 | 44.20 | 44.77
 | 37 | 4490.20 | 36.91 | 42.96 | 43.40
Vidyo3 | 22 | 22292.51 | 44.91 | 48.87 | 48.86
 | 27 | 13548.89 | 42.49 | 47.09 | 46.42
 | 32 | 8360.97 | 39.71 | 45.80 | 44.27
 | 37 | 5006.85 | 36.58 | 44.75 | 42.72
Vidyo4 | 22 | 23685.42 | 44.92 | 48.98 | 49.18
 | 27 | 13629.03 | 42.15 | 46.86 | 47.08
 | 32 | 7781.89 | 39.31 | 45.04 | 45.21
 | 37 | 4403.11 | 36.49 | 43.59 | 43.76
LB-HE |  |  |  |  | 
 | QPISlice | kbps | Y psnr | U psnr | V psnr
Johnny | 22 | 1543.04 | 43.02 | 48.06 | 48.59
 | 27 | 426.43 | 41.25 | 46.48 | 47.08
 | 32 | 190.18 | 39.21 | 44.90 | 45.49
 | 37 | 99.72 | 36.80 | 43.57 | 44.16
KristenAndSara | 22 | 2030.78 | 43.30 | 47.22 | 48.05
 | 27 | 713.72 | 41.23 | 45.40 | 46.35
 | 32 | 322.75 | 38.89 | 43.65 | 44.61
 | 37 | 165.58 | 36.27 | 42.34 | 43.38
FourPeople | 22 | 2280.42 | 42.66 | 46.46 | 47.71
 | 27 | 887.66 | 40.39 | 44.44 | 45.77
 | 32 | 435.96 | 37.80 | 42.65 | 43.92
 | 37 | 226.96 | 34.94 | 41.48 | 42.62
Vidyo1 | 22 | 2032.81 | 43.69 | 47.09 | 48.06
 | 27 | 736.80 | 41.41 | 45.72 | 46.36
 | 32 | 355.04 | 38.89 | 44.37 | 44.76
 | 37 | 188.64 | 36.14 | 43.26 | 43.49
Vidyo3 | 22 | 2712.95 | 43.56 | 48.67 | 48.36
 | 27 | 885.95 | 41.24 | 47.17 | 46.42
 | 32 | 417.61 | 38.66 | 45.96 | 44.42
 | 37 | 222.81 | 35.70 | 45.12 | 43.01
Vidyo4 | 22 | 2328.03 | 43.44 | 48.46 | 48.70
 | 27 | 735.13 | 41.04 | 46.55 | 46.74
 | 32 | 323.80 | 38.46 | 44.90 | 44.95
 | 37 | 167.91 | 35.77 | 43.54 | 43.54

## Slide 7: Encoding Comparison - LC
AI-LC |  |  |  |  | 
 | QPISlice | kbps | Y psnr | U psnr | V psnr
Johnny | 22 | 22398.99 | 44.13 | 48.13 | 48.60
 | 27 | 12144.76 | 41.93 | 46.29 | 46.81
 | 32 | 6927.78 | 39.63 | 44.39 | 44.91
 | 37 | 4039.33 | 37.14 | 42.93 | 43.38
KristenAndSara | 22 | 24489.21 | 44.48 | 47.57 | 48.31
 | 27 | 14207.38 | 42.13 | 45.55 | 46.33
 | 32 | 8563.39 | 39.52 | 43.62 | 44.47
 | 37 | 5216.17 | 36.73 | 42.15 | 42.97
FourPeople | 22 | 32993.13 | 43.88 | 46.93 | 47.92
 | 27 | 19688.59 | 41.27 | 44.63 | 45.69
 | 32 | 12081.87 | 38.44 | 42.68 | 43.76
 | 37 | 7402.44 | 35.44 | 41.31 | 42.29
Vidyo1 | 22 | 22722.23 | 44.60 | 47.40 | 48.25
 | 27 | 13275.23 | 42.14 | 45.86 | 46.49
 | 32 | 7981.06 | 39.47 | 44.46 | 44.96
 | 37 | 4837.26 | 36.62 | 43.45 | 43.76
Vidyo3 | 22 | 23532.83 | 44.60 | 48.63 | 48.44
 | 27 | 14383.61 | 42.14 | 47.08 | 46.40
 | 32 | 8988.78 | 39.36 | 45.95 | 44.60
 | 37 | 5458.04 | 36.26 | 45.05 | 43.30
Vidyo4 | 22 | 24821.18 | 44.61 | 48.68 | 48.86
 | 27 | 14270.80 | 41.85 | 46.89 | 47.05
 | 32 | 8226.37 | 39.05 | 45.30 | 45.42
 | 37 | 4732.80 | 36.26 | 44.13 | 44.17
<number>
JCTVC-H0389
LB-LC |  |  |  |  | 
 | QPISlice | kbps | Y psnr | U psnr | V psnr
Johnny | 22 | 1430.19 | 42.83 | 47.64 | 48.20
 | 27 | 421.27 | 41.03 | 46.11 | 46.60
 | 32 | 187.75 | 38.85 | 44.48 | 44.97
 | 37 | 97.61 | 36.41 | 43.18 | 43.45
KristenAndSara | 22 | 1974.47 | 43.05 | 46.80 | 47.60
 | 27 | 707.73 | 40.89 | 45.05 | 45.75
 | 32 | 321.49 | 38.46 | 43.25 | 44.20
 | 37 | 164.82 | 35.79 | 42.00 | 42.77
FourPeople | 22 | 2242.21 | 42.35 | 46.01 | 47.16
 | 27 | 895.94 | 40.07 | 44.08 | 45.19
 | 32 | 435.59 | 37.40 | 42.34 | 43.46
 | 37 | 224.72 | 34.53 | 41.15 | 42.02
Vidyo1 | 22 | 2142.52 | 43.35 | 46.79 | 47.78
 | 27 | 788.16 | 41.11 | 45.53 | 46.25
 | 32 | 383.42 | 38.62 | 44.33 | 44.81
 | 37 | 211.74 | 35.91 | 43.33 | 43.61
Vidyo3 | 22 | 2847.73 | 43.12 | 48.34 | 47.98
 | 27 | 952.87 | 40.82 | 47.05 | 46.28
 | 32 | 453.18 | 38.31 | 45.92 | 44.67
 | 37 | 247.76 | 35.46 | 45.02 | 43.55
Vidyo4 | 22 | 2419.55 | 43.11 | 48.16 | 48.42
 | 27 | 785.52 | 40.77 | 46.52 | 46.79
 | 32 | 352.19 | 38.27 | 45.06 | 45.14
 | 37 | 190.42 | 35.66 | 43.87 | 43.84

## Slide 8: Conclusion
The sequences have been uploaded to the University of Hannover ftp site, ftp.tnt.uni-hannover.de , in the NewClassE directory, and can be accessed using the same login and password as for the other HEVC source sequences
Subjective viewing has been scheduled for Sat Feb. 4, in the viewing room, starting at 6:30pm
Vidyo will donate the content to the public domain
<number>
JCTVC-H0389