## Slide 1: JCTVC-H0396: CE10.3: Deblocking Filter Simplifications
Geert Van der Auwera, Xianglin Wang, Marta Karczewicz
Qualcomm Inc.

## Slide 2: Summary
Deblocking filter simplifications are proposed:
  Part 1:
    Weak filter: simplified delta, saving one multiplication
    Unification of luma and chroma delta
    BD-rates:
      AI-HE: -0.2%, AI-LC: -0.2%, RA-HE: -0.1%, RA-LC: 0.0%, RA-HE10: -0.2%, LB-HE: -0.1%, LB-LC: -0.1%, LP-HE: -0.1%, LP-LC: 0.3%
  Part 2: in addition to part 1
    Replace HM5 strong filter with HM5 “weak” filter
    Modify strong/weak filter decision
    Line memory requirement is reduced from 4 to 3 lines; lower filter complexity
    BD-rates:
      AI-HE: -0.1%, AI-LC: -0.1%, RA-HE: -0.1%, RA-LC: 0.0%, RA-HE10: -0.0%, LB-HE: -0.1%, LB-LC: 0.0%, LP-HE: -0.1%, LP-LC: 0.5%
      class F: -0.6% to -0.3%
  Subjective gains: enhanced texture detail

## Slide 3: Part 1: Weak Filter Delta Simplification
HM5:
   = ( 9(q0-p0) - 3(q1-p1) + 8 )/16
Proposed (luma and chroma):
  = ( 3(q0-p0) - (q1-p1) + 4 )/8
BD-rates (PSNR based results):
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | -0.2% | -0.1% | 0.1% | -0.2% | 0.0% | 0.2% |  |  | 
Class B | -0.2% | -0.2% | 0.0% | -0.2% | -0.2% | 0.0% |  |  | 
Class C | -0.1% | -0.1% | -0.1% | -0.2% | -0.2% | -0.1% |  |  | 
Class D | -0.1% | 0.0% | 0.0% | -0.1% | -0.2% | -0.1% |  |  | 
Class E | -0.1% | 0.3% | 0.3% | -0.1% | 0.9% | 0.7% |  |  | 
Overall | -0.2% | 0.0% | 0.0% | -0.2% | 0.0% | 0.1% |  |  | 
 | -0.2% | 0.0% | 0.1% | -0.2% | 0.0% | 0.1% |  |  | 
Class F | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.1% |  |  | 
Enc Time[%] | 101% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 99% |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | -0.1% | -0.1% | 0.0% | -0.1% | 0.1% | 0.3% | -0.2% | -0.5% | -0.2%
Class B | -0.1% | -0.1% | -0.1% | -0.1% | 0.1% | 0.0% | -0.1% | -0.1% | 0.0%
Class C | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.1% |  |  | 
Class D | -0.1% | -0.2% | -0.2% | 0.0% | 0.0% | -0.1% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | -0.2% | -0.2% | -0.1%
 | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | -0.3% | -0.1%
Class F | -0.1% | -0.2% | -0.1% | 0.0% | 0.0% | 0.1% |  |  | 
Enc Time[%] | 99% |  |  | 99% |  |  | 99% |  | 
Dec Time[%] | 101% |  |  | 100% |  |  | 101% |  | 

## Slide 4: Part 1: Weak Filter Delta Simplification
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.2% | -0.1% | 0.0% | -0.1% | -0.3% | 0.3%
Class C | -0.1% | -0.1% | -0.2% | 0.0% | 0.2% | 0.0%
Class D | -0.1% | -0.3% | -0.1% | -0.2% | 0.1% | 0.2%
Class E | -0.1% | 0.2% | -0.2% | -0.1% | 0.7% | 0.8%
Overall | -0.1% | -0.1% | -0.1% | -0.1% | 0.1% | 0.3%
 | -0.2% | 0.0% | -0.1% | -0.1% | 0.2% | 0.3%
Class F | -0.1% | -0.2% | -0.5% | 0.0% | -1.0% | -0.6%
Enc Time[%] | 97% |  |  | 101% |  | 
Dec Time[%] | 102% |  |  | 97% |  | 
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | 0.2% | 0.0% | 0.4% | 0.3% | 0.1%
Class C | 0.0% | 0.0% | -0.3% | 0.2% | 0.0% | 0.0%
Class D | -0.1% | 0.1% | -0.8% | 0.0% | -0.1% | 0.6%
Class E | -0.1% | -0.3% | -0.4% | 0.6% | 0.4% | 0.4%
Overall | -0.1% | 0.0% | -0.4% | 0.3% | 0.2% | 0.3%
Class F | 0.1% | 0.2% | 0.1% | 0.2% | -0.3% | -0.1%
Enc Time[%] | 98% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 
BD-rates continued:

## Slide 5: Chroma Filter Characteristics
Chroma filtering of edge discontinuity (a):
  (b) with HM5 luma delta, (c) with HM5 chroma delta, (d) with proposed chroma delta (identical to proposed luma delta)
(b) and (c) are identical and overshoot linear slope
(d) proposed chroma delta (=luma) has no overshoot

## Slide 6: Strong/Weak Filter Characteristics
Edge discontinuity filtering:
  Typical smooth and flat step for filtering with strong filter (a)
  (b) and (c) compare result of filtering with HM5 strong filter, HM5 weak filter, proposed weak filter
HM5 strong and weak filter both make edge into similar linear slope
Proposed weak filter preserves detail

## Slide 7: Part 2: Replace HM5 Strong Filter
HM5:
  p0’ = ( p2 + 2p1 + 2p0 + 2q0 + q1 + 4 )/8
  p1’ = ( p2 + p1 + p0 + q0 + 2 )/4
  p2’ = ( 2p3 + 3p2 + p1 + p0 + q0 + 4 )/8
  q0’ = ( p1 + 2p0 + 2q0 + 2q1 + q2 + 4 )/8
  q1’ = ( p0 + q0 + q1 + q2 + 2 )/4
  q2’ = ( p0 + q0 + q1 + 3q2 + 2q3 + 4 )/8
Proposed: replace with luma “weak” filter; reads 3 samples on each edge side
   = ( 9(q0-p0) - 3(q1-p1) + 8 )/16
   = Clip( -tc, tc,  )
  p0’ = p0 + 
  q0’ = q0 - 
  p = Clip( - tc/2, tc/2, ( (p2 + p0 + 1)/2 - p1 + )/2 )
  p1’ = p1 + p
  q = Clip( - tc/2, tc/2, ( (q2 + q0 + 1)/2 - q1 - )/2 )
  q1’ = q1 + q
Modified strong/weak filter decision; reads 3 samples on each edge side
Required line memory is reduced from 4 to 3 lines; lower filter complexity

## Slide 8: Part 2: Replace HM5 Strong Filter
BD-rates (PSNR based results):
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | -0.2% | -0.1% | 0.0% | -0.2% | 0.0% | 0.2% |  |  | 
Class B | -0.2% | -0.2% | 0.0% | -0.2% | -0.2% | 0.0% |  |  | 
Class C | -0.1% | -0.1% | -0.1% | -0.1% | -0.2% | -0.1% |  |  | 
Class D | -0.1% | 0.0% | 0.0% | -0.1% | -0.2% | -0.1% |  |  | 
Class E | -0.1% | 0.3% | 0.3% | 0.0% | 0.9% | 0.7% |  |  | 
Overall | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.1% |  |  | 
 | -0.1% | 0.0% | 0.1% | -0.1% | 0.0% | 0.1% |  |  | 
Class F | -0.6% | -0.1% | 0.0% | -0.5% | 0.0% | 0.1% |  |  | 
Enc Time[%] | 101% |  |  | 98% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 98% |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | -0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.2% | 0.0% | -0.3% | -0.4%
Class B | -0.1% | -0.1% | 0.0% | 0.0% | 0.2% | 0.1% | -0.1% | 0.0% | -0.1%
Class C | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | 0.1% |  |  | 
Class D | -0.1% | -0.1% | 0.1% | -0.1% | -0.1% | -0.1% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | -0.2% | -0.2%
 | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | -0.2% | -0.2%
Class F | -0.3% | -0.2% | -0.2% | -0.3% | -0.1% | 0.0% |  |  | 
Enc Time[%] | 99% |  |  | 98% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 103% |  | 

## Slide 9: Part 2: Replace HM5 Strong Filter
BD-rates continued:
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | 0.0% | 0.1% | 0.0% | -0.4% | -0.2%
Class C | -0.1% | -0.1% | 0.1% | 0.0% | 0.0% | -0.1%
Class D | -0.1% | -0.1% | -0.1% | -0.2% | 0.4% | -0.1%
Class E | -0.1% | 0.3% | -0.1% | 0.2% | 0.4% | 0.5%
Overall | -0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
 | -0.1% | 0.0% | -0.1% | 0.0% | 0.1% | 0.0%
Class F | -0.4% | -0.5% | -0.3% | -0.5% | -0.9% | -0.8%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 96% |  | 
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | 0.0% | -0.2% | 0.7% | 0.0% | -0.6%
Class C | 0.0% | 0.0% | -0.2% | 0.3% | 0.0% | 0.2%
Class D | 0.0% | 0.0% | 0.0% | 0.1% | -0.7% | 0.4%
Class E | 0.0% | 0.0% | 0.4% | 1.0% | 0.7% | 0.0%
Overall | -0.1% | 0.0% | 0.0% | 0.5% | 0.0% | 0.0%
Class F | -0.3% | 0.0% | -0.1% | -0.3% | -1.0% | -0.3%
Enc Time[%] | 98% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 

## Slide 10: Part 1: Subjective Quality Examples
Frame 240 from the class B “Kimono” sequence (Low delay P LC, QP=37). Enhanced texture detail is shown.
HM5.0
Proposal

## Slide 11: Part 1: Subjective Quality Examples
Frame 214 from class C “BQMall” sequence (Low delay P LC, QP=37). Improved texture detail and reduction of trailing edge is shown.
HM5.0
Proposal

## Slide 12: Part 2: Subjective Quality Examples
Frame 240 from the class B “Kimono” sequence (Low delay P LC, QP=37). Enhanced texture detail is demonstrated.
HM5.0
Proposal

## Slide 13: Part 2: Subjective Quality Examples
Frame 600 from class E “Vidyo3” sequence (Low delay P LC, QP=37).
HM5.0
Proposal

## Slide 14: Conclusion
Proposals:
  Part 1: Simpler weak filter delta, saving one multiplication
  Part 2: Replace strong filter, modify strong/weak filter decision, reducing line memory from 4 to 3 lines and reducing filter complexity
Texture detail is improved
Proposed to adopt parts 1 and 2 in HM6
Thanks to SKKU for cross checking!