## Slide 1: JCTVC-H0397 Context reduction of split_transform_flag in CABAC
Jun Xu, Ali Tabatabai
SONY

## Slide 2: Outline
Introduction
Proposed solutions & results
Conclusion

## Slide 3: Introduction
split_transform_flag
  Indicates splitting of TU in RQT
  4 contexts in WD
  10 contexts in HM5.0 software

## Slide 4: Proposal & results
One context for split_transform_flag
  Split flags from all depths share the same context
Thanks to Huawei for cross-checking
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.01% | -0.05% | -0.05% | 0.01% | -0.07% | -0.10% |  |  | 
Class B | 0.01% | -0.01% | -0.01% | 0.01% | -0.06% | -0.07% |  |  | 
Class C | 0.00% | -0.04% | -0.03% | 0.00% | -0.05% | -0.08% |  |  | 
Class D | 0.00% | 0.05% | -0.04% | 0.00% | -0.02% | -0.02% |  |  | 
Class E | 0.00% | -0.08% | -0.04% | 0.00% | -0.16% | -0.14% |  |  | 
Overall | 0.00% | -0.02% | -0.03% | 0.01% | -0.07% | -0.08% |  |  | 
 | 0.00% | -0.02% | -0.02% | 0.00% | -0.07% | -0.08% |  |  | 
Class F | -0.01% | 0.05% | 0.03% | 0.01% | 0.15% | -0.10% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 101% |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.11% | 0.03% | -0.22% | 0.06% | 0.18% | 0.03% | 0.05% | 0.04% | 0.24%
Class B | 0.04% | -0.02% | 0.04% | 0.04% | 0.00% | -0.17% | 0.08% | -0.03% | -0.21%
Class C | 0.02% | -0.14% | 0.03% | -0.01% | 0.07% | -0.15% |  |  | 
Class D | 0.00% | -0.13% | 0.09% | 0.02% | 0.42% | -0.11% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.03% | -0.07% | 0.02% | 0.02% | 0.15% | -0.12% | 0.07% | 0.00% | -0.01%
 | 0.03% | -0.09% | -0.01% | 0.02% | 0.13% | -0.14% | 0.07% | 0.00% | 0.02%
Class F | -0.05% | -0.19% | -0.16% | 0.06% | 0.14% | -0.04% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  |  | #NUM! |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.07% | 0.31% | 0.48% | 0.03% | -0.11% | 0.07% |  |  | 
Class C | 0.05% | -0.17% | 0.03% | -0.01% | 0.10% | 0.18% |  |  | 
Class D | 0.06% | 0.19% | 0.08% | -0.05% | 1.09% | 0.06% |  |  | 
Class E | 0.16% | 0.94% | -0.39% | -0.09% | -1.00% | -0.54% |  |  | 
Overall | 0.08% | 0.28% | 0.11% | -0.02% | 0.08% | -0.02% |  |  | 
 | 0.07% | 0.31% | 0.18% | -0.02% | 0.02% | -0.01% |  |  | 
Class F | 0.14% | -0.08% | 0.01% | -0.06% | -0.57% | -0.89% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 99% |  |  |  |  | 

## Slide 5: Conclusion
Reduce contexts in CABAC
  Contexts are reduced from 4(10) to 1
  Negligible changes in BD-rate.
Proposed to adopt into HEVC