## Slide 1: JCTVC-H0399 Harmonization of coefficient coding in HEVC
Jun Xu, Ali Tabatabai
SONY

## Slide 2: Outline
Introduction
Proposed solutions & results
Conclusion

## Slide 3: Introduction
In HM5.0, coefficient coding varies at
  MDCS for 4x4 and 8x8
  4x4 sub-block scan for 16x16 and 32x32
  Multi-level significance map coding for 16x16 and 32x32
TU sizes | Scan | LastPos | Multi-level Sig Map | Sig Map Context | level
4x4 | H/V/D | 2D(x,y) | - | Position based (4x4 only) | 16 in 1D
8x8 | H/V/D | 2D(x,y) | - | Position based (8x8 only) | 16 in 1D
16x16/16x4/4x16 32x32/32x8/8x32 | Sub-D | 2D(x,y) | 4x4 sub-block | mask based | 4x4 sub-block

## Slide 4: Proposals
Proposed to harmonize TU coding for diagonal scan
  TU based diagonal scan is replaced by 4x4 sub-block based diagonal scan, which means sub-block is scanned using diagonal scan and diagonal scan is applied inside each 4x4 sub-block.
  Multi-level significance map coding is applied and all contexts reuse 16x16 and 32x32 cases.
  Significance map context definition uses mask based approach as 16x16 and 32x32 cases.
  Level coding is changed accordingly due to the scan pattern.
TU sizes | Scan | LastPos | Multi-level Sig Map | Sig Map Context | level
4x4 | H/V | 2D(x,y) | - | Position based (4x4 only) | 16 in 1D
8x8 | H/V | 2D(x,y) | - | Position based (8x8 only) | 16 in 1D
4x4, 8x8 16x16/16x4/4x16 32x32/32x8/8x32 | Sub-D | 2D(x,y) | 4x4 sub-block | mask based | 4x4 sub-block

## Slide 5: Diagram
Example of 4x4 sub-block scan for 8x8 diagonal scan
Diagonal

## Slide 6: Results
Thanks to Qualcomm for cross-checking(JCTVC-H0684)
Common test conditions
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.15% | -0.01% | 0.08% | 0.00% | 0.14% | 0.16% |  |  | 
Class B | 0.07% | 0.17% | 0.10% | -0.06% | 0.06% | 0.16% |  |  | 
Class C | -0.11% | 0.05% | 0.04% | -0.23% | -0.11% | -0.11% |  |  | 
Class D | -0.14% | 0.05% | -0.06% | -0.27% | -0.14% | -0.13% |  |  | 
Class E | 0.10% | 0.26% | 0.23% | -0.03% | 0.28% | 0.24% |  |  | 
Overall | 0.00% | 0.11% | 0.07% | -0.13% | 0.03% | 0.05% |  |  | 
 | 0.00% | 0.11% | 0.08% | -0.14% | 0.03% | 0.04% |  |  | 
Class F | -0.17% | -0.22% | -0.35% | -0.25% | -0.19% | -0.22% |  |  | 
Enc Time[%] | 102% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 101% |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.02% | -0.20% | -0.28% | -0.11% | 0.09% | 0.01% | 0.14% | -0.22% | 0.03%
Class B | 0.01% | -0.04% | 0.09% | -0.07% | 0.05% | 0.14% | 0.06% | 0.01% | 0.01%
Class C | -0.24% | -0.09% | -0.05% | -0.34% | -0.20% | -0.06% |  |  | 
Class D | -0.25% | 0.02% | -0.05% | -0.42% | 0.55% | -0.31% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | -0.12% | -0.06% | -0.03% | -0.24% | 0.12% | -0.05% | 0.10% | -0.09% | 0.02%
 | -0.12% | -0.08% | -0.04% | -0.24% | 0.11% | -0.06% | 0.08% | -0.06% | 0.09%
Class F | -0.30% | -0.30% | -0.27% | -0.37% | -0.39% | -0.34% |  |  | 
Enc Time[%] | 101% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 99% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.01% | -0.11% | -0.09% | -0.10% | -0.69% | -0.35% |  |  | 
Class C | -0.20% | -0.14% | 0.16% | -0.47% | -0.39% | -0.58% |  |  | 
Class D | -0.23% | -0.26% | 0.29% | -0.51% | 0.78% | 0.20% |  |  | 
Class E | -0.12% | 0.30% | -0.72% | -0.14% | -0.86% | 0.50% |  |  | 
Overall | -0.13% | -0.08% | -0.05% | -0.30% | -0.28% | -0.11% |  |  | 
 | -0.13% | -0.04% | -0.03% | -0.30% | -0.24% | -0.15% |  |  | 
Class F | -0.41% | -0.39% | -0.71% | -0.39% | -1.31% | -1.03% |  |  | 
Enc Time[%] | 101% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 98% |  |  |  |  | 

## Slide 7: Results (Low QP)
Thanks to Qualcomm for cross-checking (JCTVC-H0684)
Low QP settings(12, 17, 22,27) as in CE11 subset 1
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.13% | 0.05% | 0.10% | 0.02% | 0.03% | 0.04% |  |  | 
Class B | 0.08% | 0.13% | 0.11% | 0.01% | -0.07% | -0.06% |  |  | 
Class C | -0.04% | 0.00% | -0.04% | -0.20% | -0.18% | -0.18% |  |  | 
Class D | -0.10% | -0.06% | -0.05% | -0.24% | -0.21% | -0.20% |  |  | 
Class E | 0.05% | 0.10% | 0.07% | -0.05% | -0.02% | -0.02% |  |  | 
Overall | 0.01% | 0.04% | 0.03% | -0.10% | -0.11% | -0.10% |  |  | 
 | 0.01% | 0.05% | 0.04% | -0.10% | -0.11% | -0.10% |  |  | 
Class F | -0.07% | -0.18% | -0.25% | -0.27% | -0.19% | -0.18% |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
1 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.03% | -0.14% | -0.28% | -0.2% | 0.0% | -0.1% | 0.22% | -0.07% | -0.12%
Class B | 0.05% | 0.17% | 0.07% | 0.0% | 0.1% | 0.0% | 0.06% | 0.13% | -0.03%
Class C | -0.31% | -0.06% | -0.24% | -0.5% | -0.3% | -0.3% |  |  | 
Class D | -0.33% | -0.14% | -0.20% | -0.5% | -0.2% | -0.3% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | -0.15% | -0.01% | -0.13% | -0.3% | -0.1% | -0.2% | 0.13% | 0.04% | -0.07%
 | -0.14% | -0.01% | -0.14% | -0.3% | -0.1% | -0.2% | 0.15% | 0.04% | -0.09%
Class F | -0.40% | -0.28% | -0.43% | -0.4% | -0.4% | -0.3% |  |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.04% | 0.22% | -0.08% | 0.1% | 0.0% | -0.1% |  |  | 
Class C | -0.34% | -0.06% | -0.08% | -0.5% | -0.4% | -0.4% |  |  | 
Class D | -0.33% | -0.01% | -0.16% | -0.6% | -0.4% | -0.4% |  |  | 
Class E | -0.08% | 0.08% | -0.21% | -0.2% | -0.5% | -0.1% |  |  | 
Overall | -0.17% | 0.07% | -0.13% | -0.3% | -0.3% | -0.2% |  |  | 
 | -0.16% | 0.04% | -0.16% | -0.3% | -0.3% | -0.2% |  |  | 
Class F | -0.44% | -0.43% | -0.49% | -0.5% | -0.4% | -0.7% |  |  | 

## Slide 8: Conclusion
Proposed to harmonize TU coefficient coding
  Harmonized coefficient coding for diagonal scan across all sizes
  Up to 0.3% coding gains and no complexity.
Proposed to adopt into HEVC