## Slide 1: JCTVC-H0400 Chroma QP extension
Jun Xu*, Alexis Tourapis**, Ehsan Maani*, Kazushi Sato*
*:SONY **: Magnum

## Slide 2: Outline
Introduction
Proposed solutions & results
Conclusion

## Slide 3: Introduction
In HM5.0, Chroma QP is derived from Luma QP the same as AVC
Problems
  Bit consumption between luma and chroma
    Normal QP: 80%vs 20%
    High QP (45, 50): 50% vs 50%
  rate control at low bit rate
    Inaccurate bit-to-QP mapping model
    Unpredictable/unachievable bit allocation
      Chroma bit may not be able achieve because of QP limit
qPI | <30 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51
QPC | =qPI | 29 | 30 | 31 | 32 | 32 | 33 | 34 | 34 | 35 | 35 | 36 | 36 | 37 | 37 | 37 | 38 | 38 | 38 | 39 | 39 | 39 | 39

## Slide 4: Proposal
Proposed to remove the mapping between Chroma QP and Luma QP
  Chroma QP in [0, 51]
  Within the concept of Chroma QP offset parameters:
Advantages
  Flexibility
    Chroma QP covers [0, 51]
    Can achieve current HM5.0 model with chroma QP offset parameters
  Functionality
    Potential support for other color formats
    Current HEVC focuses on YUV
QPCb = Clip(0, 51, QPY+Cb_QP_offset)
QPCr = Clip(0, 51, QPY+Cr_QP_offset),

## Slide 5: RD curves
High QPs (38, 42, 46, 50)
Chart: Y PSNR vs Bitrate
| 721.77280000000019 | 437.52319999999975 | 284.2792 | 196.15440000000001
HM5.0 | 30.9696 | 28.9807 | 27.1082 | 25.3614
Proposed+ChromaQPoffset=0 | 30.9725 | 28.9759 | 27.0853 | 25.2977
Propsoed+ChromaQPoffset=-2 | 30.9699 | 28.9771 | 27.0885 | 25.2993
Chart: U PSNR vs Bitrate
| 721.77280000000019 | 437.52319999999975 | 284.2792 | 196.15440000000001
HM5.0 | 35.4561 | 34.5014 | 34.027 | 33.5708
Proposed+ChromaQPoffset=0 | 33.862 | 31.9318 | 30.0695 | 28.3699
Proposed+ChromaQPoffset=-2 | 34.9547 | 32.9399 | 31.0613 | 29.3239

## Slide 6: Conclusion
Proposed to extend Chroma QP
  Flexibility
  Functionality
Proposed to adopt into HEVC