## Slide 1: JCTVC-H0401 Differentiated weighting parameter sets for weighted prediction
Jun Xu*, Alexis Tourapis**, Ehsan Maani*, Ali Tabatabai*
*:SONY **: Magnum

## Slide 2: Outline
Introduction
Proposed solutions & results
Conclusion

## Slide 3: Introduction
HM5.0 weighted prediction
  Uni-directional prediction: P’ = w0/1 × P0/1 + o0/1
  Bi-directional prediction: P’ = (w0 × P0 + o0 + w1 × P1 + o1) / 2
  HM5.1 chroma weighted prediction
    E.g. (8-bit) P’ = w × (P -128)+ o+128
Problems
  Weighting factors and offsets are shared for uni-prediction and bi-prediction
    Sub-optimal solution
    E.g. Cross-fade video
  Chroma weighted prediction
    Specially tuned for Chroma components around 128 (8-bit bitdepth)

## Slide 4: Proposal
Two weighting parameter sets
  One for uni-prediction
  The other for bi-prediction
  Bi-prediction weighting parameter sets are encode using prediction from uni-prediction weighting parameter sets.
Chroma weighted prediction
  Add one flag (chroma_offset_pred_flag) to select between two approaches in chroma weighted prediction
  E.g. (8-bit)
    If chroma_offset_pred_flag == 1
      P’ = w × (P -128)+ o+128
    else
      P ’ = w × P + o
WD changes in JCTVC-H0401.doc

## Slide 5: Conclusion
Proposed to improve weighted prediction
  differentiated weighting parameter sets
    Flexibility
    Functionality
  Chroma weighted prediction
    Flexible weighted prediction approaches
Proposed to adopt to HEVC