## Slide 1: Flexible Band Offset Mode in SAO
Ehsan Maani, Ohji Nakagami
Proposal
JCTVC-H0406
Jan 31 2012

## Slide 2: SAO in HM 5.0
4 Edge Offset (EO) modes
  4 offsets each
2 Band Offset (BO) modes
  16 offsets each
Decoder needs a temporary buffer to store offset information. Size of the buffer is proportional to max offsets (16)
Most offsets in BO modes are either zero or have small impact on distortion since not that many pixels in that band -> making the BO mode expensive to select
<number>
JCTVC-H0405

## Slide 3: Proposed changes in SAO
4 Edge Offset (EO) modes
  4 offsets each
1 Band Offset (BO) mode
  4 offsets
Simplified solution. Instead of introducing new modes with various offset numbers.
Size of temporary buffer at decoder is reduced by ~75%
BO mode is more affordable and thus selected more often
<number>
JCTVC-H0405

## Slide 4: Selection of Bands in BO mode
“First band with nonzero offset” is between 0 to 31. FL code is used to transmit.
Encoder selects the 4 bands with the most impact. Distortion impact of an offset only requires a few arithmetic operations since the offset, the pixel counts (in each band), and pixel sums are already known (pre-computed).
<number>
JCTVC-H0405
HM 5.0
Proposed
First band for which offset is transmitted
4 offsets if transmitted for 4 consecutive bands

## Slide 5: Results
<number>
JCTVC-H0405
 | All Intra HE |  | 
 | Y | U | V
Class A (8bit) | 0.0% | -0.1% | -0.2%
Class B | 0.0% | -0.3% | -0.4%
Class C | 0.0% | -0.1% | -0.1%
Class D | 0.1% | -0.1% | -0.1%
Class E | 0.0% | -0.4% | -0.5%
Overall | 0.0% | -0.2% | -0.2%
 | 0.0% | -0.2% | -0.3%
Class F | 0.4% | 0.1% | 0.6%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 
 | Random Access HE |  | 
 | Y | U | V
Class A (8bit) | 0.0% | -0.2% | -0.3%
Class B | 0.0% | -0.5% | -0.5%
Class C | 0.0% | -0.3% | -0.2%
Class D | 0.0% | -0.3% | -0.4%
Class E |  |  | 
Overall | 0.0% | -0.3% | -0.3%
 | 0.0% | -0.3% | -0.3%
Class F | 0.3% | 0.0% | 0.4%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | -0.7% | -0.4%
Class C | 0.0% | -0.6% | -0.4%
Class D | -0.1% | -0.5% | -0.4%
Class E | -0.1% | -1.2% | -1.6%
Overall | 0.0% | -0.7% | -0.7%
 | 0.0% | -0.7% | -0.7%
Class F | 0.2% | -0.3% | -0.4%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
 | Low delay P HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | -0.7% | -0.8%
Class C | 0.1% | -0.4% | -0.5%
Class D | 0.0% | -0.3% | -1.1%
Class E | -0.1% | -1.1% | -0.9%
Overall | 0.0% | -0.6% | -0.8%
 | 0.0% | -0.6% | -0.8%
Class F | 0.3% | -0.1% | 0.2%
Enc Time[%] | 100% |  | 
Dec Time[%] | 99% |  | 

## Slide 6: Visual Quality Evaluation
<number>
JCTVC-H0405
HM 5.0
BO percentage: 12%
Total SAO partitions: 3011
Proposed
BO percentage: 16%
Total SAO partitions: 3416
“C.PartyScene” frame #44, LowDelayP_HE, QP 37

## Slide 7: Conclusion
Simplified solution
  Harmonized number of offset across SAO modes
  Reduced decoder buffer to hold SAO parameters
Coding gain
  Coding gain for all natural images
<number>
JCTVC-H0405

## Slide 8
Notes: <number>