## Slide 1: Intra mode clean up: coding using logical mode numbering and its extension to 3MPM
Ehsan Maani, Ali Tabatabai
Proposal
JCTVC-H0407
Jan 31 2012

## Slide 2: HM5 Luma Intra Mode Numbering
Bit stream mode number
  No meaning
  Inherited from AVC. Supposedly sorted in their occurrence frequency (not true in HEVC)
Logical mode number
  Meaningful mode numbers. Similar directions have close numbers.
Because bit stream numbers have no meaning many look-up tables have to be inserted in the code
  MD Scan, Intra Smoothing, Intra Prediction, MD Transform
<number>
JCTVC-H0407

## Slide 3: Benefits of Logical Mode Numbering
Cleaner design
  Mode numbers have clear meaning (systematic naming)
Simple mapping
  Simple converting modes from 35 to 18 (or 19) for 4x4 PU ( clear LSB )
Removal of several look-up tables
  aucIntraDirToScanIdx, m_aucIntraFilter, g_aucAngIntraModeOrder, g_aucDCTDSTMode_Hor, g_aucDCTDSTMode_Ver
Simplifying Fast Intra Mode Decision Algorithms
  Since modes have clear names, various FMD algorithms can be envisaged -> e.g., a hierarchical approach (in analogy to fast motion estimation)
Facilitating other algorithms
  Neighboring and perpendicular modes can be easily derived. This simplifies some algorithms such as 3 MPM algorithms
<number>
JCTVC-H0407

## Slide 4: Proposed Intra Mode Naming
<number>
JCTVC-H0407
Systematic numbering
4x4 PUs only support even angular numbers
Simple mapping from 35 modes to 19 for 4x4 Pus
  Current HM5 mapping to planar is not accurate (just a patch-up solution)
Removal of several look-up tables and replacing them with simple logic
  aucIntraDirToScanIdx[5][36]
  m_aucIntraFilter[5][36]
  g_aucAngIntraModeOrder[36]
  g_aucDCTDSTMode_Hor[36]
  g_aucDCTDSTMode_Ver[36]
0: Planar, 1: DC

## Slide 5: Intra Mode Renaming Results
<number>
JCTVC-H0407
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
Class D | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | -0.1%
Class E | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1%
Overall | 0.0% | -0.1% | -0.1% | -0.1% | 0.0% | -0.1%
 | 0.0% | -0.1% | -0.1% | -0.1% | 0.0% | -0.1%
Class F | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Difference with HM5.0
  Modified Intra Mode Names
  19 Modes for 4x4 PUs (to have a symmetric solution – no gain)
  Different mapping from 35 to 19 modes for 4x4 PUs

## Slide 6: Extension to 3 MPM
Why 3 MPM?
  Simplified remaining mode coding
    FL codes can be used for remaining modes of all PU sizes
  Using the new Intra mode naming, computation of the 3rd MPM is simple
    does not need a look-up table
  Coding gain
    About 0.3%
  No additional complexity
    No additional context, or memory requirement – jus a few simple operations
<number>
JCTVC-H0407

## Slide 7: Computation/Decoding of 3 MPMs
<number>
JCTVC-H0407
Neighbouring modes condition | MPMs (three MPMs)
iLeftIntraDir == iAboveIntraDir | iLeftIntraDir, iLeftIntraDir- , iLeftIntraDir+
iLeftIntraDir != iAboveIntraDir | iLeftIntraDir, iAboveIntraDir, Planar/DC
is 2 for 4x4 PU size and 1 otherwise.
Decoding tree of 3 MPM :

## Slide 8: Appendix
uiIntraDirPred[0] = iLeftIntraDir;
uiIntraDirPred[1] = iAboveIntraDir;
if (iLeftIntraDir && iAboveIntraDir ) //angular or dc
{
uiIntraDirPred[2] = PLANAR_IDX;
}
else
{
uiIntraDirPred[2] = (iLeftIntraDir+iAboveIntraDir)<2? VER_IDX : DC_IDX;
}
<number>
JCTVC-H0407
if (iLeftIntraDir > 1)
{
iInc = (PU4x4 ? 2 : 1);
uiIntraDirPred[0] = iLeftIntraDir;
iLeftIntraDir-=2;
uiIntraDirPred[1] = 2 + ((iLeftIntraDir-iInc) & 0b1111);
uiIntraDirPred[2] = 2 + ((iLeftIntraDir+iInc) & 0b1111);
}
else
{
uiIntraDirPred[0] = PLANAR_IDX; uiIntraDirPred[1] = DC_IDX;
uiIntraDirPred[2] = VER_IDX;
}
iLeftIntraDir == iAboveIntraDir
iLeftIntraDir != iAboveIntraDir

## Slide 9: Results for 3 MPMs
<number>
JCTVC-H0407
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | -0.29% | -0.13% | 0.00% | -0.38% | -0.15% | -0.09%
Class B | -0.20% | -0.07% | -0.06% | -0.28% | -0.07% | -0.06%
Class C | -0.25% | -0.13% | -0.16% | -0.32% | -0.17% | -0.18%
Class D | -0.21% | -0.07% | -0.09% | -0.24% | -0.10% | -0.13%
Class E | -0.33% | -0.25% | -0.05% | -0.42% | -0.13% | -0.15%
Overall | -0.25% | -0.12% | -0.08% | -0.31% | -0.12% | -0.12%
 | -0.25% | -0.13% | -0.08% | -0.31% | -0.12% | -0.13%
Class F | -0.33% | -0.35% | -0.28% | -0.33% | -0.38% | -0.45%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
No additional context (compared to HM5.0)

## Slide 10: Conclusions
Cleaner design
  Mode numbers have clear meaning (systematic naming)
Simple mapping
  Simple converting modes from 35 to 18 (or 19) for 4x4 PU ( clearing LSB )
Removal of several look-up tables
  aucIntraDirToScanIdx, m_aucIntraFilter, g_aucAngIntraModeOrder, g_aucDCTDSTMode_Hor, g_aucDCTDSTMode_Ver
Simplifying Fast Intra Mode Decision Algorithms
  Since modes have clear names, various FMD algorithms can be envisaged -> e.g., a hierarchical approach (in analogy to fast motion estimation)
Simple extension to 3 MPM
  Brings coding gain
<number>
JCTVC-H0407

## Slide 11
Notes: <number>