## Slide 1: Harmonization of number of ALF classes between RA and BA modes
Ehsan Maani, Ali Tabatabai
Proposal
JCTVC-H0409
Jan 31 2012

## Slide 2: HM5 ALF Classification
16 classes for Region Adaptive (RA) mode
15 classed for Block Adaptive (BA) mode
Since the rest of the ALF code (both encoder and decoder) is shared between RA and BA modes, many branches should be included in different parts of the code
This contribution does not suggest a particular number (8, 15 , or 16) of classes, but rather suggests to use the same number of classes for the two modes
<number>
JCTVC-H0409

## Slide 3: ALF BA Classification
Merge the direction of the blocks with no activity
  Since they have no direction
This can be done by a small table or by checking the activity and skip direction calculation when zero
  BaClassTable[direction][activity]
<number>
JCTVC-H0409
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Quantized block activity
Block direction
HM 5.0
Proposed
1
2
3
4
6
7
8
9
0
11
12
13
14
Quantized block activity
Block direction
5
10
15

## Slide 4: Results
<number>
JCTVC-H0409
 | All Intra HE |  | 
 | Y | U | V
Class A (8bit) | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0%
Class E | -0.1% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0%
Class F | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 99% |  | 
 | Random Access HE |  | 
 | Y | U | V
Class A (8bit) | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | -0.1% | -0.1%
Class E |  |  | 
Overall | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0%
Class F | -0.1% | -0.2% | -0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 99% |  | 
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | 0.0% | 0.2%
Class C | 0.0% | -0.2% | 0.0%
Class D | 0.0% | -0.1% | 0.4%
Class E | 0.0% | 0.0% | -0.6%
Class F | -0.1% | 0.0% | -0.3%
Overall | 0.0% | -0.1% | 0.0%
 | 0.0% | -0.1% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
 | Low delay P HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | 0.2% | -0.3%
Class C | 0.0% | -0.1% | -0.1%
Class D | 0.0% | 0.2% | -0.1%
Class E | 0.0% | -0.3% | -0.2%
Class F | 0.0% | 0.3% | 0.1%
Overall | 0.0% | 0.1% | -0.1%
 | 0.0% | 0.1% | -0.1%
Enc Time[%] | 101% |  | 
Dec Time[%] | 101% |  | 

## Slide 5
Notes: <number>