## Slide 1: JCTVC-H0426 AHG21: Removal of reference picture list modification
M. M. Hannuksela, S. M. Gopalakrishna (Nokia)

## Slide 2: Summary of the Proposal
Removal of reference picture list modification
Reference picture lists 0 and 1 are formed directly from reference picture sets
  Signed POC difference values can be used conditionally in the reference picture set (RPS) syntax structure to allow specifying reference picture sets flexibly.
    A default negative sign is inferred for set 0 and a default positive sign is inferred for set 1, unless signs are provided explicitly for each item in reference picture sets.
  Reference picture list 0 = short-term reference picture set S0 followed by short-term reference picture set S1. Reference picture list 1 = short-term reference picture set S1 followed by short-term reference picture set S0.
Each long-term reference picture may be inserted at an indicated position in reference picture list 0 or 1, as controlled by the slice header.

## Slide 3: Motivation of the Proposal
The page count of the specification is reduced by about two pages
No essential change in bit count overhead according to the common conditions in JCTVC-G1036