## Slide 1: H0433: Reference Picture Set Signaling Method - RPS Delete Operation Signaling Method
Sachin Deshpande, Kiran Misra, Andrew Segall
Sharp Labs of America
<number>
Notes: <number>

## Slide 2: Motivation
HEVC WD5 does not support a delete operation on a previously signaled (via picture parameter set) reference picture set (RPS) to signal a new partial RPS.
JCTVC-G637:
  Proposed pruning of reference picture sets.
  The main use case supported was first GOP following a random access point where some of the pictures signaled in RPS are not available.
  It proposed a syntax which can signal number of short term reference pictures that are omitted from a particular RPS signaled in the PPS.
  Syntax in G637 only supports omitting consecutive negative short-term reference pictures from a reference picture set.
  There are situations where a selective omission of one or more reference pictures from a reference picture set is desired.
<number>
Notes: <number>

## Slide 3: Proposal
We propose a method to signal delete operation on a previously signaled RPS to efficiently signal a new RPS.
Our approach is useful in following use cases:
  U1: Signaling RPS for pictures in first GOP after a random access point (e.g. use case 2.1 in JCTVC-G1036d03)
  U2: Signaling RPS efficiently via a delete operation on a previous signaled RPS for the case where a reference picture was lost and was signaled by decoder to the encoder via feedback and the lost picture is no longer used as a reference picture by the encoder. (e.g. use case 3.3 in JCTVC-G1036d03 and similar use case in non low-delay conditions).
  U3: A memory optimizing encoder, which uses one (or more) LTRP for portion of the video.
Our proposed signaling consists of a flag in PPS and slice header and a bit field in slice header for each picture in RPS. The bit field signals 1 or 0 values to indicate keep/ delete corresponding reference picture from the indicated reference picture set
<number>

## Slide 4: Proposed Syntax: PPS
delete_pics_info_present_flag:
equal to 1 specifies that slice header may signal delete operation from the short-term reference picture set included in the picture parameter set
equal to 0 specifies that no delete operation is signaled in the slice header for the short-term reference picture set included in the picture parameter set

## Slide 5: Proposed Syntax: Slice Header
keep_pics_info_present_flag:
equal to 1 specifies that this slice header includes keep_pic_flag values indicating information regarding keeping or deleting short term reference pictures from the reference picture set with index short_term_ref_pic_set_idx.
equal to 0 specifies that this slice header does not include information regarding keeping or deleting short term reference pictures from the reference picture set with index short_term_ref_pic_set_idx.
keep_pic_flag[j]:
equal to 1 specifies that the corresponding j th short term reference picture from the reference picture set in the picture parameter set with index short_term_ref_pic_set_idx should be kept.
equal to 0 specifies that the corresponding j th short term reference picture from the reference picture set in the picture parameter set with index short_term_ref_pic_set_idx should be deleted (omitted).

## Slide 6: Use Case U1 Example (1/2)
U1: Signaling RPS for picture in first GOP after RAP (e.g. use case 2.1 in JCTVC-G1036d03)
For the first GOP after random access point some of the reference pictures indicated in RPS are not available.
This can be signaled efficiently using our proposed method.
As an example for first GOP for picture with POC 4 the reference picture set {-4, 4} can be signaled efficiently by referring to RPS {-4,-6,4} sent in PPS and signaling a delete for -6.
This will be more efficient than signaling the new correct RPS {-4,4} in slice header.
<number>

## Slide 7: Use Case U1 Example (2/2)
First GOP (also applies to first GOP after a RAP)
<number>

## Slide 8: Use Case U2 Example (1/3)
U2: Signaling RPS via a delete operation on a previous signaled RPS for the case where a reference picture was lost (e.g. use case 3.3 in JCTVC-G1036d03 and similar use case in non low delay conditions)
Without Any Picture Loss:
<number>

## Slide 9: Use Case U2 Example (2/3)
With Picture Loss/ Corruption: Assume picture with POC 6 was received corrupted/ lost at the decoder, this was signaled by decoder by feedback to the encoder and encoder then did not use picture 6 as reference picture when encoding next GOP – including pictures with POC 10, 12, 16.
<number>

## Slide 10: Use Case U2 Example (3/3)
For pictures 16, 12 and 10 the correct RPS can be signaled efficiently by referring to RPS sent in PPS:
  {-8,-10,-12,-16} with our proposed delete signaling to delete -10,
  {-4,-6,4} with our proposed delete signaling to delete -6,
  {-2,-4,2,6} with our proposed signaling to delete -4.
This will be more efficient than signaling the new correct RPS {-8, -12, -16}, {-4,4}, {-2,2,6} in slice header for each of these pictures.
<number>

## Slide 11: Use Case U3
A memory optimizing encoder which uses one (or more) LTRP for portion of the video may decide to keep the decoder picture buffer memory requirement same as when using only STRPs.
For example if initially the encoder is using random access configuration for encoding as in JCTVC-G1036d03 section 2.1 then decoder picture buffer needs memory to store 5 STRPs.
Suppose for a portion of the video, encoder decides to use one LTRP, then to keep the same reduced memory requirement for the decoder (i.e. not to increase it to 6 frames) encoder may decide to only use 4 STRPs during this time when 1 LTRP is used.
In this case the encoder will choose not to use one of the short-term reference pictures when encoding.
Encoder can efficiently signal this by referring to RPS sent in PPS and signaling a delete operation for one of the STRPs using our proposed syntax.
<number>

## Slide 12: Conclusion
The document proposed syntax to efficiently signal a delete operation for removing select reference pictures from a previously signaled reference picture set (RPS).
This approach can be used to efficiently signal a new partial RPS by referring to a RPS signaled in PPS.
We propose to adopt the proposed approach in HEVC.
<number>