## Slide 1: JCTVC-H0436: CE8 Subset d.1 Reduced Number of Band Offsets in SAO
Woo-Shik Kim, Do-Kyoung Kwon
Texas Instruments Inc., USA

## Slide 2: SAO Parameter Buffer
SAO parameters are coded into adaptation parameter set (APS)
  Need to be stored in a buffer until SAO processing is completed at a decoder side
Buffer size is proportional to the number of partitions and SAO parameter size
Need to consider the worst case to prepare enough size of buffer
  Maximum number of partitions
  Maximum size of SAO parameter  BO uses 16 offsets, while EO uses 4 offsets
Example
  LCU 64x64  256 partitions in the worst case
  10bit video, 6 bits/offset x 16 offsets X 3 color components = 288 bits
  Total buffer size: 10 Kbyte (256x288=9 Kbyte offset + additional information)

## Slide 3: Proposed Solution for SAO Buffer Reduction
Current BO design
  2 band selection, 16 offsets per band
Proposed solution (Test 1)
  4 band selection, 8 offsets per band
SAO buffer size reduction
  HM4.0: 9.0 Kbyte = 256 x 6 x 16 x 3
  Proposed: 4.5 Kbyte = 256 x 6 x 8 x 3
BO 2
BO 1
BO 2
BO 3
BO 1
BO 2
BO 4
 Buffer size reduction by Half

## Slide 4: Proposed Solution
Extended coverage of the first and last sub-band offsets (Test 2)
Overall bitrate reduction
  Bitrate increase to encode BO type
  However, more bitrate decrease in offset coding
…
BO 1
sub-band 1
sub-band 8

## Slide 5: Experimental Results
BD-rate results of Test 1: 8 band offset only
BD-rate results of Test 2: 8 band offset + sub-band extension
(%)
 |  | Y | U | V
HE | All Intra | 0.0 | 0.0 | 0.1
 | Random Access | 0.0 | 0.0 | 0.1
 | Low delay B | 0.0 | -0.1 | 0.2
 | Low delay P | 0.0 | -0.1 | 0.0
Average |  | 0.0 | -0.1 | 0.1
(%)
 |  | Y | U | V
HE | All Intra | 0.0 | -0.2 | -0.1
 | Random Access | 0.0 | -0.3 | -0.2
 | Low delay B | 0.0 | -0.5 | -0.5
 | Low delay P | 0.0 | -0.4 | -0.7
Average |  | 0.0 | -0.4 | -0.4

## Slide 6: Experimental Results
Subjective quality evaluation
  Settings are the same as in JCTVC-G684
  No subjective quality degradation is observed
 | HM-5.0 | G682 | Neutral
Test1 | 4 | 23 | 73
Test2 | 25 | 11 | 64
Vote percentage (%)

## Slide 7: Conclusions
SAO parameter buffer size is reduced by half
  Number of band offset reduced from 16 to 8
  BO types are increased from 2 to 4
  Maintain the similar overall subjective and objective qualities without complexity increase