## Slide 1: JCTVC-H0438: Non-CE8 New Chroma Band Offset (BO) Design in SAO
Woo-Shik Kim, Do-Kyoung Kwon
Texas Instruments Inc., USA
Yukinobu Yasugi, Tomohiro Ikai
Sharp Corporation, JAPAN

## Slide 2: SAO Parameter Buffer
SAO parameters are coded into adaptation parameter set (APS)
  Need to be stored in a buffer until SAO processing is completed at a decoder side
Buffer size is proportional to the number of partitions and SAO parameter size
Need to consider the worst case to prepare enough size of buffer
  Maximum number of partitions
  Maximum size of SAO parameter
Example
  LCU 64x64  256 partitions in the worst case
  10bit video, 6 bits/offset x 16 offsets x 3 color components = 288 bits
  Total buffer size = 10 Kbyte (256 x 288 = 9 Kbyte offset + additional information)
BO 2
BO 1
BO 2
- Current BO design: 2 band selection, 16 offsets per band

## Slide 3: Reconstructed Pixel Statistics
Reconstructed Luma and Chroma statistics are quite different
  Reconstructed Luma pixels spread out whole dynamic ranges
  But reconstructed Chroma pixels concentrate on middle ranges
  Implies that different BO designs are necessary for Luma and Chroma
- Histograms of reconstructed Luma pixels in different BO types
- Histograms of reconstructed Chorma pixels in different BO types

## Slide 4: Proposed Solution
4 bands and 8 offsets per band
Different BO designs for Luma and Chroam based on the statistics
Advantages of the proposed solutions
  SAO buffer size reduction by half
    HM-5.0: 9.0 Kbyte = 256 x 6 x 16 x 3
    Proposed: 4.5 Kbyte = 256 x 6 x 8 x 3
  Overall bitrate reduction for Chroma
BO 3
BO 1
BO 2
BO 4
BO 1
BO 2
BO 3
BO 4
- Proposed BO design for Luma
- Proposed BO design for Chroma

## Slide 5: Experimental Results
BD-rate results
(%)
 |  | Y | U | V
HE | All Intra | 0.1 | -0.6 | -0.7
 | Random Access | 0.0 | -0.8 | -0.8
 | Random Access 10 | 0.1 | -0.9 | -0.9
 | Low Delay B | 0.0 | -1.7 | -1.6
 | Low Delay P | 0.1 | -0.9 | -0.7

## Slide 6: Conclusions
SAO parameter buffer size is reduced by half
  BO types are increased from 2 to 4
  Number of band offset reduced from 16 to 8
BO design based on the statistics
  Luma and Chroma have different statistics
  Chroma BO design is further modified to improve coding efficiency
Many thanks to MediaTek for cross-checking this contribution (JCTVC-H0338)