## Slide 1: H0441 - Motion Compensation Restrictions to Alleviate Memory Bandwidth Concerns for High Resolution Video
Tim Hellman & Wade Wan
Broadcom Corporation

## Slide 2: Motion Compensation Bandwidth
HEVC MComp Bandwidth is much higher than AVC (Worst-case)
  Larger filter for both Y & UV
  AVC has a limit on Motion Vectors (for high level)
  HEVC only limits 4x4 Prediction (presently)
  HEVC worst case BW: More than double AVC for same picture size
4x8 and 8x4 are the culprits
  Minimum DRAM burst size leads to lots of wasted bandwidth
<number>

## Slide 3: Proposed Solution
AVC Limit: 16 MVs per MBlock pair
  Somewhat awkward for encoder
  Made more difficult by temporal reference (harder to control the limit)
  Variable-sized CUs
Proposed for HEVC: Uni-directional 4x8 & 8x4
  Limit only imposed at high levels (like AVC)
  Reduces worst-case bandwidth to 20% more than AVC
  Negligible loss (0.2% Y, 0.2% UV) for Class A/B, per G392 (case C)
    This is with no syntax change. Could optimize syntax, as is done for 4x4
<number>