## Slide 1: CE11: Harmonization of residual coding and NSQT
J. Sole, M. Karczewicz Qualcomm
J. Kim, B. Jeon LGE
JCTVC-H0443

## Slide 2: Motivation
NSQT uses non-square transforms
  Block sizes: 32×8, 8×32, 16×4, 4×16
NSQT blocks use the large transform entropy coding method based on the neighborhood despite of their size
  8×8 blocks use position-based context for the significance map
  16×4 and 4×16 have the same number of coefficients but use neighborhood method
Harmonization: blocks with same number of coefficients use the same significance map coding method
  16×4 and 4×16 use the 8×8 method and contexts
JCT-VC, San Jose, February 2012
<number>

## Slide 3: NSQT harmonization
In HM5.0, 8×8 significance map contexts are obtained from a 4×4 table (called map8x8)
  map8x8[4 * (uiPosY >> 1) + (uiPosX >> 1)]
The same table is used to accommodate sizes 16×4/4×16
  4×16 case : map8x8[4 * (uiPosY >> 2) + uiPosX]
  16×4 case: map8x8[4 * (uiPosX >> 2) + uiPosY]
Contexts and tables of the 8×8 blocks are re-used
  Method applies same contexts to coefficients with similar frequencies
  Contexts depend on the position, so the method can be applied to any context tables used for 8×8 blocks
<number>
JCT-VC, San Jose, February 2012

## Slide 4: Results
Common conditions
  Cross-check: Sony (JCTVC-H0402)
<number>
 | Random Access HE |  |  | Low delay B HE |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.05% | 0.03% | -0.07% |  |  |  | 0.04% | -0.06% | 0.09%
Class B | 0.04% | 0.02% | 0.01% | 0.05% | 0.08% | 0.43% | 0.06% | 0.15% | 0.11%
Class C | 0.06% | -0.02% | 0.05% | 0.12% | 0.17% | 0.29% |  |  | 
Class D | 0.10% | -0.08% | 0.06% | 0.17% | -0.22% | 0.25% |  |  | 
Class E |  |  |  | 0.04% | -0.06% | 0.46% |  |  | 
Overall | 0.06% | -0.02% | 0.02% | 0.10% | 0.00% | 0.35% | 0.05% | 0.06% | 0.10%
 | 0.06% | -0.04% | 0.04% | 0.09% | 0.03% | 0.29% | 0.05% | 0.04% | 0.13%
Class F | -0.02% | 0.03% | 0.00% | 0.19% | 0.22% | -0.13% |  |  | 
EncT[%] | 99% |  |  | 99% |  |  | 99% |  | 
DecT[%] | 96% |  |  | 97% |  |  | 96% |  | 
JCT-VC, San Jose, February 2012

## Slide 5: Conclusions
Simple harmonization of NSQT blocks
  TU with same number of coefficients use same method
Complexity reduction
  Removal of the neighborhood computation for 16×4/4×16
Slightly worse BD-rate
<number>
JCT-VC, San Jose, February 2012

## Slide 6: Thank you!
<number>
JCT-VC, San Jose, February 2012