## Slide 1: Non-CE11: Low complexity parallel significance map coding
J. Sole, V. Seregin, M. Karczewicz Qualcomm
T. Tsukuba, T. Ikai
SHARP corporation
JCTVC-H0445

## Slide 2: Motivation
For large transforms, significance map context depends on the number of non-zero coefficients in a neighbourhood
  Up to 10 conditions have to be checked
  Allow 2-bin in parallel processing
This contribution reduces the number of conditions to check while allowing 3-bin parallel processing
Combination of
  JCTVC-H0095: position-based context for high frequencies
  JCTVC-H0427: modified neighbourhood to reduce conditions
JCT-VC, San Jose, February 2012
<number>

## Slide 3: HEVC LTU Significance Context
Two types of templates depending on the coefficient position within a 4×4 sub-block
  Check if parts of the neighborhood template is out of the block
  Up to 10 conditions and 2 bins in parallel
  DC context is position based
<number>

## Slide 4: Proposal
Two modifications to reduce complexity
Position-based context for high-frequencies
  (X>>2) + (Y>>2) >= 3*(Tsize>>4)
Modified template for low frequencies
<number>
Template-based
Position-based
context
Notes: <number>

## Slide 5: Advantages
3-bins parallelization and reduction in the number of conditions:
High percentage of contexts are position-based
For template-based contexts
  No need to check boundary conditions
  Two positions have different template (as in HM5.0)
<number>
Notes: <number>

## Slide 6: Results
Common conditions and low QP (12, 17, 22, 27)
  Encoding and decoding times similar to anchor
Two cases as in JCTVC-H0095
  Additional context for high-frequencies (one for luma, one for chroma)
  No additional context
<number>
Case | Conditions | AI-HE | RA-HE | LB-HE | AI-LC | RA-LC | LB-HE | RA10
1 | Common | 0.12% | 0.10% | 0.11% | 0.05% | 0.08% | 0.06% | 0.18%
1 | Low QP | 0.03% | 0.05% | 0.05% | -0.01% | 0.02% | 0.03% | 0.04%
2 | Common | 0.14% | 0.12% | 0.15% | 0.06% | 0.08% | 0.07% | 0.16%
2 | Low QP | 0.04% | 0.07% | 0.06% | 0.00% | 0.03% | 0.02% | 0.04%
JCT-VC, San Jose, February 2012

## Slide 7: Conclusions
Proposal allows 3 bins in parallel while greatly reducing the number of conditions
Slightly worse BD-rate
<number>
JCT-VC, San Jose, February 2012

## Slide 8: Thank you!
<number>
JCT-VC, San Jose, February 2012

## Slide 9: Results case 1, common conditions
<number>
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.08% | 0.21% | 0.32% | 0.02% | 0.10% | 0.15% |  |  | 
Class B | 0.12% | 0.38% | 0.40% | 0.04% | 0.12% | 0.13% |  |  | 
Class C | 0.09% | 0.12% | 0.14% | 0.04% | 0.15% | 0.15% |  |  | 
Class D | 0.08% | 0.19% | 0.15% | 0.04% | 0.14% | 0.07% |  |  | 
Class E | 0.23% | 0.38% | 0.43% | 0.10% | 0.48% | 0.41% |  |  | 
Overall | 0.12% | 0.26% | 0.28% | 0.05% | 0.19% | 0.17% |  |  | 
 | 0.12% | 0.27% | 0.29% | 0.05% | 0.19% | 0.17% |  |  | 
Class F | 0.09% | 0.17% | 0.05% | 0.04% | 0.14% | 0.08% |  |  | 
Enc Time[%] | 100% |  |  | 98% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 101% |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.06% | 0.11% | 0.01% | 0.08% | 0.19% | -0.18% | 0.19% | 0.30% | 0.48%
Class B | 0.13% | 0.30% | 0.27% | 0.10% | 0.28% | 0.16% | 0.18% | 0.14% | 0.32%
Class C | 0.08% | 0.00% | 0.14% | 0.09% | 0.20% | 0.03% |  |  | 
Class D | 0.09% | 0.04% | 0.33% | 0.04% | 0.15% | -0.12% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.10% | 0.13% | 0.21% | 0.08% | 0.21% | 0.00% | 0.18% | 0.21% | 0.39%
 | 0.10% | 0.11% | 0.24% | 0.08% | 0.19% | -0.05% | 0.19% | 0.21% | 0.34%
Class F | 0.05% | 0.08% | 0.06% | 0.10% | 0.01% | 0.11% |  |  | 
Enc Time[%] | 99% |  |  | 99% |  |  | 98% |  | 
Dec Time[%] | 101% |  |  | 100% |  |  | 102% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.13% | 0.35% | 0.41% | 0.05% | -0.35% | 0.14% |  |  | 
Class C | 0.11% | 0.07% | 0.16% | 0.07% | 0.32% | 0.02% |  |  | 
Class D | 0.09% | -0.16% | 0.09% | 0.00% | 0.53% | 0.00% |  |  | 
Class E | 0.09% | -0.14% | -0.67% | 0.13% | -0.20% | 0.29% |  |  | 
Overall | 0.11% | 0.06% | 0.07% | 0.06% | 0.07% | 0.10% |  |  | 
 | 0.10% | 0.12% | 0.04% | 0.06% | 0.03% | 0.12% |  |  | 
Class F | 0.02% | 0.60% | -0.19% | 0.03% | -1.08% | -0.30% |  |  | 
Enc Time[%] | 100% |  |  | 99% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 101% |  |  |  |  | 

## Slide 10: Results case 2, common conditions
<number>
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.09% | 0.21% | 0.31% | 0.04% | 0.13% | 0.20% |  |  | 
Class B | 0.14% | 0.40% | 0.43% | 0.05% | 0.19% | 0.18% |  |  | 
Class C | 0.12% | 0.15% | 0.20% | 0.05% | 0.18% | 0.18% |  |  | 
Class D | 0.10% | 0.25% | 0.21% | 0.04% | 0.13% | 0.09% |  |  | 
Class E | 0.24% | 0.47% | 0.50% | 0.10% | 0.44% | 0.42% |  |  | 
Overall | 0.14% | 0.30% | 0.33% | 0.06% | 0.21% | 0.20% |  |  | 
 | 0.13% | 0.30% | 0.33% | 0.05% | 0.21% | 0.20% |  |  | 
Class F | 0.09% | 0.18% | 0.13% | 0.05% | 0.16% | 0.04% |  |  | 
Enc Time[%] | 99% |  |  | 97% |  |  |  |  | 
Dec Time[%] | 98% |  |  | 99% |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.09% | 0.08% | -0.07% | 0.06% | 0.28% | 0.04% | 0.16% | 0.26% | 0.86%
Class B | 0.13% | 0.34% | 0.24% | 0.12% | 0.33% | 0.18% | 0.16% | 0.26% | 0.23%
Class C | 0.10% | 0.07% | 0.22% | 0.09% | 0.01% | 0.00% |  |  | 
Class D | 0.12% | -0.09% | 0.16% | 0.03% | 0.16% | -0.16% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.12% | 0.12% | 0.17% | 0.08% | 0.19% | 0.02% | 0.16% | 0.26% | 0.51%
 | 0.12% | 0.08% | 0.18% | 0.08% | 0.17% | 0.00% | 0.15% | 0.29% | 0.49%
Class F | -0.02% | 0.14% | -0.03% | 0.06% | -0.01% | 0.12% |  |  | 
Enc Time[%] | 99% |  |  | 100% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 98% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.18% | 0.14% | 0.54% | 0.06% | -0.11% | 0.20% |  |  | 
Class C | 0.09% | -0.05% | 0.04% | 0.12% | 0.20% | 0.07% |  |  | 
Class D | 0.14% | -0.52% | -0.37% | -0.01% | 0.62% | -0.17% |  |  | 
Class E | 0.17% | 1.11% | -0.44% | 0.11% | -1.04% | -0.44% |  |  | 
Overall | 0.15% | 0.11% | 0.00% | 0.07% | -0.03% | -0.04% |  |  | 
 | 0.14% | 0.08% | -0.02% | 0.07% | -0.03% | 0.02% |  |  | 
Class F | 0.10% | 0.22% | -0.14% | -0.25% | -1.08% | -0.86% |  |  | 
Enc Time[%] | 99% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 99% |  |  | 100% |  |  |  |  |