## Slide 1: JCTVC-H0448: AHG6: Deblocking of IPCM Blocks Containing Reconstructed Samples
Geert Van der Auwera, Xianglin Wang, Marta Karczewicz
Qualcomm Inc.

## Slide 2: Summary
Contribution proposes fix for deblocking filter to properly support filtering of edges of IPCM blocks containing reconstructed samples
HM5 deblocking filter assigns QP = 0 to IPCM blocks, independent of pcm_loop_filter_disable_flag value, resulting in inadequate deblocking parameter values
Proposal:
  In case deblocking is enabled on IPCM samples (pcm_loop_filter_disable_flag equals 0), assign the reconstructed QP value (QPY) to the IPCM blocks
  In case deblocking is disabled on IPCM samples (pcm_loop_filter_disable_flag equals 1), deblocking of non-IPCM samples is determined by the reconstructed QPY value of the non-IPCM block that is neighboring the IPCM block, while the IPCM block is assigned QP value 0

## Slide 3: IPCM and Loop Filtering
IPCM mode usages:
  Ensure that coded representation does not exceed size of uncompressed data
  To avoid encoder pipeline stalls; encoder decides to represent non-original samples (reconstructed) as IPCM
pcm_loop_filter_disable_flag (SPS)
  Disable/enable loop filter processes on IPCM samples (deblocking, SAO, ALF)
    Filters are not required in case of IPCM block containing original samples
    Filters are required in case of IPCM with reconstructed samples
IPCM
pcm_loop_filter_disable_flag = true (deblocking is OFF for IPCM samples)
IPCM
pcm_loop_filter_disable_flag = false (deblocking is ON for IPCM samples)

## Slide 4: IPCM and Deblocking
WD5 specifies that QP of IPCM blocks equals 0 for deblocking, which results in following QPL (average QP of neighboring P and Q blocks) values to deblock the IPCM block edge, independent of pcm_loop_filter_disable_flag value
Proposed to assign reconstructed QPY to IPCM blocks if deblocking enabled, and if disabled, keep QP=0 for IPCM block and assign QPY of neighboring non-IPCM block to QPL
P block is IPCM? | Q block is IPCM? | QPL
No | Yes | QPP / 2
Yes | No | QPQ / 2
Yes | Yes | 0
pcm_loop_filter_disable_flag | P block is IPCM? | Q block is IPCM? | QPL
true (deblocking is disabled on IPCM samples) | No | Yes | QPP
 | Yes | No | QPQ
 | Yes | Yes | 0
false (deblocking is enabled on IPCM samples) | No | Yes | QPavg
 | Yes | No | 
 | Yes | Yes | 

## Slide 5: Conclusion
Recommended to assign reconstructed QPY to IPCM blocks if deblocking of IPCM samples is enabled, and if disabled, keep QP=0 for IPCM block and assign QPY of neighboring non-IPCM block to QPL
Proposed to adopt in HM6
Thanks to NEC for cross checking!

## Slide 6: Source Code Change
if(pcCU->getIPCMFlag(uiPartQIdx))
{
#if DBF_IPCM
if (bPCMFilter) {iQP_Q = 0; iQP_P <<= 1;}
#else
iQP_Q = 0;
#endif
}
if(pcCUP->getIPCMFlag(uiPartPIdx))
{
#if DBF_IPCM
if (bPCMFilter) {iQP_P = 0; iQP_Q <<= 1;}
#else
iQP_P = 0;
#endif
}
iQP = QpUV((iQP_P + iQP_Q + 1) >> 1);