## Slide 1: JCTVC-H0460: High-level Syntaxes for Scaling Matrices Parameters and Parametric coding
Munsi Haque, Ehsan Maani, Ali Tabatabai
February 01, 2012

## Slide 2: Introduction
<number>
JCTVC-F91
Encoders may select on how accurate scaling list matrices need to be coded
  just parametric models only - no residual prediction error
  Or some tradeoffs - send parameters and a limited amount of residual errors
Example syntax for a group of scaling list parameters
  modeling a class of scaling list matrices in scaling_list_param() sets
some results on parametric model based coding of scaling matrices

## Slide 3: scaling_list_param() syntax structure for APS
<number>
JCTVC-F91
scaling_list_param() | Descriptor
{ | 
param_model_index | u(3)
if( param_model_index = 1) { // symmetric quadratic parameter model | 
parameter_coding_flag // flag for uniform or VLC coding? | u(1)
if (!parameter_coding_flag) // position-based uniform coding as an example | 
get_params() // get "a, b, c, d" parameters of the quadratic model | u(n)
else { // VLC (EGC, etc).coding of "a, b, c, d" parameters of the quadratic model } | ue(v)
} // end of param_model_index = 1 | 
else { // Other parameter model indices: asymmetric quadratic, HVS, etc. } | 
residual_error_present_flag | u(1)
if( residual_error_present_flag) { | 
residual_coding_mode | u(3)
if (residual_coding_mode = 0) { // AVC DPCM } | 
else if (residual_coding_mode = 1) { // Sony-TI or similar DPCM coding. } | 
else { // 2 to 7 - reserved ? } | 
} // end of residual_error_present_flag | 
} // end of scaling_list_param | 
Parameter Model Index (param_model_index) | Parameter Model Type description | Parametric models
0 | reserved | 
1 | Symmetric Quadratic | q(x, y) = a (x*x + y*y) + b xy + c (x + y) + d
2 | Asymmetric Quadratic | q(x, y) = (a1 x + b1 y + c1) ( a2 x + b2 y + c2)
3 | HVS | H(u,v) = a (b + c f (u,v)) exp( - (c f(u,v))**d ); Q(u,v) = q / H(u,v)
4-7 | reserved | ...

## Slide 4: Parametric Modeling and Coding Results
<number>
JCTVC-F91
For the simulation runs, Quadratic parameter models are used to predict 4x4 and 8x8 Scaling List Matrices
Two possible ways to code the Scaling List Matrices
  Parameter Only Coding
  Parameters and Residual Error Coding
For Live-update, a limited number of parameters can be sent for matrices
  No prediction error
  For 16x16 and 32x32 matrices, the parameters of 8x8 matrices and fractional grids to interpolate the elements of larger matrices, without coding any other parameters for them.
  Used EGC coding for the parameters
For Residual Error Coding, example coding method of CE4 Subtest 2.1 are considered
  As in CE4 Subtest 2.1, option-1, two sets (symmetric & asymmetric) of matrix files are used for simulation
Notes: <number>

## Slide 5: Bit-count for Scaling List Matrices
<number>
JCTVC-F91
Symmetric Matrix Files
Asymmetric Matrix Files
Bit-counts for Parametric Model based coding compared with CE4 2.1 Sony DPCM case varies from 109.13% to 129.57% for symmetric matrix files, and 106.76% to 116.29% for asymmetric matrix files

## Slide 6: Conclusion
<number>
JCTVC-F91
This contribution has 2 parts
  an example syntax structure for the scaling_matrix_param() group to enable sending parameters of scaling list matrices to the decoder-side
  Some compression results for Parametric Model based Scaling List Matrix coding are presented
The parametric model based coding results are comparable with those of DPCM method
  tradeoff studies on bit-allocations between parameters and residual coding can be further enhanced
We believe such coding mechanism of Scaling List matrices result in more compact representation
encoder may decide what kind of scaling list matrices are sufficient for coding, as far as residual errors concerned
Parametric models can co-exist with other models and hence need high-level syntax support, as shown in the example

## Slide 7
Notes: <number>