## Slide 1: JCTVC-H0461: On HVS only Default Scaling List Matrices
Munsi Haque, Ali Tabatabai, Jun Xu, Cheung Auyeung
Yoshitaka Morigami, Teruhiko Suzuki
February 01 2012

## Slide 2: Introduction
<number>
JCTVC-F91
HM5.0 Default Scaling List Matrices
  Includes 4x4 and 8x8 AVC matrices, and 16x16 and 32x32 HVS model based matrices
  AVC 4x4/8x8 Scaling list matrices are relatively steeper near DC (0,0) coefficient-area
    DC value is 6 or 9 for AVC 4x4/8x8 matrices, while for HVS, it is 16
  HEVC transforms are different than AVC transforms and so are the need for different Scaling List Matrices
H0461 proposes
  Substitute 4x4 and 8x8 AVC matrices with the corresponding HVS model-based matrices to make an ALL HVS matrices
  HVS 8x8 Intra matrix is MPEG-4 Part-2 (ASP) Default Quantization Matrix

## Slide 3: Objective Performance Measure
<number>
JCTVC-F91
HM5.0 Default matrices as Anchor, HVS only matrices provide BD bit-rate reduction of 6.5% (AI-HE), 3.6% (RA-HE), 1.8% (LD-B-HE).
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | -5.9% | -6.7% | -6.0% | -9.8% | 11.5% | 7.9%
Class B | -5.3% | -3.7% | -3.3% | -9.2% | 12.1% | 17.7%
Class C | -7.8% | -6.1% | -5.5% | -11.6% | 4.2% | 7.4%
Class D | -7.9% | -5.7% | -5.9% | -11.0% | 5.6% | 6.2%
Class E | -5.3% | -5.9% | -5.8% | -10.2% | 39.6% | 31.3%
Overall | -6.5% | -5.4% | -5.1% | -10.4% | 13.4% | 14.4%
 | -6.5% | -5.4% | -5.1% | -10.4% | 13.2% | 14.8%
Enc Time[%] | - |  |  | - |  | 
Dec Time[%] | - |  |  | - |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | -3.2% | -1.8% | -0.4% | -5.6% | 22.2% | 32.2%
Class B | -2.9% | 1.0% | 2.0% | -5.5% | 20.1% | 31.5%
Class C | -4.3% | -2.2% | -1.4% | -6.5% | 9.2% | 12.9%
Class D | -4.1% | -0.1% | 0.6% | -6.0% | 15.1% | 16.6%
Class E |  |  |  |  |  | 
Overall | -3.6% | -0.5% | 0.4% | -5.9% | 16.1% | 22.7%
 | -3.6% | -0.5% | 0.3% | -5.9% | 15.9% | 22.3%
Enc Time[%] | - |  |  | - |  | 
Dec Time[%] | - |  |  | - |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -1.6% | -1.3% | -1.3% | -3.6% | 8.8% | 12.8%
Class C | -2.3% | -2.7% | -2.4% | -4.6% | 3.7% | 6.2%
Class D | -2.1% | -2.4% | -1.5% | -3.6% | 9.4% | 10.1%
Class E | -1.0% | 1.4% | -0.1% | -2.5% | 35.1% | 33.9%
Overall | -1.8% | -1.4% | -1.4% | -3.6% | 12.6% | 14.4%
 | -1.8% | -1.4% | -1.5% | -3.6% | 12.2% | 13.9%
Enc Time[%] | - |  |  | - |  | 
Dec Time[%] | - |  |  | - |  | 

## Slide 4: Subjective Performance Evaluation
<number>
JCTVC-F91
In-house subjective evaluation demo was conducted with more than 10 people participating
Performance for All HVS matrices are compared against HM5.0 default matrices
  In some class B sequences (BQTerrace, Kimono1 with QP32), color looks more stable for All HVS cases
  In a class E sequence (Vidyo3 with QP37), picture quality looks better, as shown in next slides.
  For other sequences (with QP32), relative performances in picture quality are hard to distinguish

## Slide 5: Subjective evaluation
The followings are compared
  Anchor (HM5.0 Default) vs. All HVS (All matrices are HVS model based)
The Subjective evaluation shows better All HVS results than Anchor’s
Focus
Bit-rate Adjustment: Anchor vs Target |  |  |  |  | 
Default HM5.0 QMs as Anchor | Bitrate | Y-PSNR | U-PSNR | V-PSNR | 
QP37 | 5810.101 | 36.37 | 45.9296 | 44.4131 | 
All HVS QMs as Target | Bitrate | Y-PSNR | U-PSNR | V-PSNR | Bitrate difference %
QP35 | 6339.636 | 37.4974 | 44.8854 | 43.156 | 9.10%
QP36 | 5741.594 | 36.9139 | 44.4798 | 42.7136 | 1.20%
QP37 | 5196.578 | 36.2898 | 44.5447 | 42.7479 | 10.60%
Bitrate difference % = (Anchor - All HVS) / Anchor * 100 |  |  |  |  | 

## Slide 6: Anchor (4x4 8x8 AVC, 16x16 32x32 HVS) QP=37, Intra_LC, frame#40
out of focus

## Slide 7: All HVS (All matrices are HVS model based) QP=37, Intra_LC, frame#40
clear

## Slide 8: Conclusion
<number>
JCTVC-F91
While comparing with HM5.0 Default Scaling List matrices as Anchor
  performance of HVS only matrices provide BD bit-rate reduction of 6.5% (AI-HE), 3.6% (RA-HE), 1.8% (LD-B-HE).
  In some test sequences, Subjective evaluation by Sony researchers shows relatively better visual quality for HVS only matrices than for default HM5.0 matrices
Substitute 4x4 and 8x8 AVC matrices by HVS model based matrices and make an all HVS based Scaling list matrices
  Note: 8x8 Intra HVS matrix = MPEG-4:2 (ASP) QM
Many thanks to Edouard Francois (Canon) for the cross-checking help (JCTVC-0696)

## Slide 9
Notes: <number>

## Slide 10: Backup
<number>
JCTVC-F91

## Slide 11: HM5.0 (Flat QM) vs Default QM
<number>
JCTVC-F91
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 6.7% | 6.6% | 5.4% | 11.1% | -9.4% | -15.8%
Class B | 7.4% | 0.8% | 0.3% | 11.2% | -14.8% | -18.0%
Class C | 12.3% | 3.4% | 2.3% | 17.1% | -5.2% | -8.5%
Class D | 13.1% | 2.0% | 2.8% | 17.3% | -7.8% | -7.1%
Class E | 6.1% | 4.5% | 4.4% | 12.2% | -31.3% | -26.4%
Overall | 9.5% | 2.9% | 2.5% | 14.0% | -13.3% | -14.6%
 | 9.4% | 2.9% | 2.6% | 14.0% | -13.1% | -14.4%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.2% | 0.7% | 0.0% | 0.1% | 1.4% | 0.8%
Class B | 0.6% | -1.7% | -2.2% | 0.0% | -1.3% | -1.6%
Class C | 3.4% | -0.2% | -0.8% | 4.0% | 0.9% | 0.1%
Class D | 3.9% | -2.1% | -1.7% | 4.5% | -1.1% | -1.3%
Class E |  |  |  |  |  | 
Overall | 2.2% | -1.1% | -1.4% | 2.3% | -0.3% | -0.7%
 | 2.1% | -1.1% | -1.4% | 2.3% | -0.3% | -0.7%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.4% | -2.5% | -3.0% | -0.2% | -4.2% | -4.4%
Class C | 2.1% | -1.9% | -2.2% | 3.5% | -2.5% | -3.0%
Class D | 1.8% | -4.0% | -3.7% | 3.0% | -4.2% | -5.0%
Class E | 0.2% | -0.6% | -1.6% | 0.8% | -2.8% | -2.9%
Overall | 1.1% | -2.4% | -2.7% | 1.7% | -3.5% | -3.9%
 | 1.1% | -2.3% | -2.7% | 1.7% | -3.4% | -3.8%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 

## Slide 12: HM5.0 (Flat QM) vs HVS QMs
<number>
JCTVC-F91
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.4% | -0.5% | -0.9% | 0.2% | -0.3% | -1.3%
Class B | 1.8% | -3.0% | -3.1% | 1.2% | -4.3% | -4.7%
Class C | 3.7% | -3.0% | -3.4% | 3.7% | -1.7% | -2.6%
Class D | 4.4% | -3.9% | -3.4% | 4.6% | -3.4% | -2.5%
Class E | 0.5% | -1.7% | -1.6% | 0.7% | -3.7% | -3.2%
Overall | 2.4% | -2.7% | -2.7% | 2.3% | -3.0% | -3.1%
 | 2.4% | -2.6% | -2.6% | 2.3% | -2.9% | -3.1%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.2% | 0.7% | 0.0% | 0.1% | 1.4% | 0.8%
Class B | 0.6% | -1.7% | -2.2% | 0.0% | -1.3% | -1.6%
Class C | 3.4% | -0.2% | -0.8% | 4.0% | 0.9% | 0.1%
Class D | 3.9% | -2.1% | -1.7% | 4.5% | -1.1% | -1.3%
Class E |  |  |  |  |  | 
Overall | 2.2% | -1.1% | -1.4% | 2.3% | -0.3% | -0.7%
 | 2.1% | -1.1% | -1.4% | 2.3% | -0.3% | -0.7%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.4% | -2.5% | -3.0% | -0.2% | -4.2% | -4.4%
Class C | 2.1% | -1.9% | -2.2% | 3.5% | -2.5% | -3.0%
Class D | 1.8% | -4.0% | -3.7% | 3.0% | -4.2% | -5.0%
Class E | 0.2% | -0.6% | -1.6% | 0.8% | -2.8% | -2.9%
Overall | 1.1% | -2.4% | -2.7% | 1.7% | -3.5% | -3.9%
 | 1.1% | -2.3% | -2.7% | 1.7% | -3.4% | -3.8%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  |