## Slide 1: Using averaged down-sampling reference pixels in LM parameter generation
JCTVC-H0464
Santa Clara University and HiSilicon Co. Ltd.
Lingzhi Liu, Guichun Li, Nam Ling, Li Song, Jianhua Zheng, Philipp Zhang

## Slide 2: Introduction
A method of reducing the number of multiplications for calculating parameter Alpha and Beta for Intra LM mode is proposed
The averaged down-sampled reference luma and chroma samples are used instead of the original neighbouring reference samples.
Notes: Parameters Alpha and Beta are derived from reconstructed samples around the current block. The equation used for calculating Alpha (and Beta) is the ordinary least square (OLS) solution:

## Slide 3: Proposed Simplification Approaches
For Chroma blocks with size 16x16, average every 2 neighbouring reference samples and use the 8 result values on each side as new reference samples (Down to 8x8)
For Chroma blocks with size 16x16, average every 4 neigbouring reference samples; for 8x8 blocks, average every 2 reference samples, and use 4 result values on each side as new reference samples (Down to 4x4)

## Slide 4: Averaged Reference down sampling from 8x8 to 4x4
N = 8
ND = 4

## Slide 5: Simulation Results
  (1) Averaged down sampling to 4x4 vs. HM-5.0 Anchor
 | All Intra HE |  | 
 | Y | U | V
Class A (8bit) | 0.00% | 0.00% | 0.05%
Class B | -0.01% | 0.00% | 0.05%
Class C | 0.00% | 0.00% | 0.02%
Class D | 0.00% | 0.04% | -0.01%
Class E | 0.00% | -0.04% | -0.01%
Overall | 0.00% | 0.00% | 0.02%
 | 0.00% | 0.01% | 0.02%
Class F | 0.00% | -0.11% | -0.05%
Enc Time[%] | 100% |  | 
Dec Time[%] | 102% |  | 
 | All Intra HE |  | 
 | Y | U | V
Class A (8bit) | 0.02% | 0.05% | 0.15%
Class B | 0.00% | 0.06% | 0.13%
Class C | 0.00% | -0.01% | 0.03%
Class D | 0.00% | 0.08% | 0.02%
Class E | 0.00% | 0.00% | -0.06%
Overall | 0.00% | 0.04% | 0.05%
 | 0.00% | 0.04% | 0.06%
Class F | -0.01% | 0.00% | 0.07%
Enc Time[%] | 100% |  | 
Dec Time[%] | 103% |  | 
  (2) Averaged down sampling 16x16 to 8x8 vs. HM-5.0 Anchor

## Slide 6: Conclusion
As observed in the simulation result, the proposed simplification of LM mode intra prediction has nearly no impact on BD-rate while reducing computational complexity.
It is proposed to consider adopt the method of averaged down sampling to 4x4 (1:4 averaged down-sampling of 16x16 PU and 1:2 averaged down-sampling of 8x8 PU).