## Slide 1: Simplification of Mode Dependent Intra Smoothing
JCTVC-H0465
Santa Clara University and HiSilicon Co. Ltd.
Lingzhi Liu, Guichun Li, Nam Ling, Li Song, Jianhua Zheng, Philipp Zhang

## Slide 2: Introduction
MDIS (Mode Dependent Intra Smoothing) is used in current design of HM.
The PU size and intra prediction mode determines whether 3-tap filter with coefficient [1 2 1] is applied on reference samples or not.
Two approaches of reducing intra smoothing filtering are evaluated

## Slide 3: Proposed Simplification Approaches
Two approaches are proposed and tested:
  Disabling intra smoothing on 8x8 units for all intra modes except intra planar mode;
  Completely disabling intra smoothing on 8x8 units for all intra modes.
  No changes on PUs with size other than 8x8 pixels.

## Slide 4: Modification to MDIS Look-up Table
The original look-up table for 8x8 PUs
(Filtering applied for Intra Mode 0, 4, 7, 10)
  {1, 0, 0, 0, 1, 0, 0, 1, 0, 0, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}
Proposed modifications
  Keep intra smoothing for only Planar mode on 8x8 PUs
  {1, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0
  Disable intra smoothing for all modes on 8x8 PUs
  {0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}

## Slide 5: Simulation Results
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.05% | 0.00% | 0.03% | 0.09% | 0.01% | -0.01%
Class B | 0.04% | 0.00% | 0.00% | 0.07% | 0.00% | -0.01%
Class C | -0.01% | 0.00% | 0.03% | 0.00% | -0.01% | -0.01%
Class D | 0.02% | 0.08% | 0.04% | 0.04% | 0.01% | -0.03%
Class E | 0.05% | 0.03% | 0.07% | 0.09% | -0.02% | 0.00%
Overall | 0.03% | 0.02% | 0.03% | 0.05% | 0.00% | -0.01%
 | 0.03% | 0.02% | 0.04% | 0.05% | 0.00% | -0.01%
Class F | -0.05% | 0.07% | -0.01% | -0.03% | -0.02% | -0.02%
Enc Time[%] | 99% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 93% |  | 
  (1) Filtering only for Planar mode on 8x8 PUs vs. HM-5.0 Anchor

## Slide 6
Simulation Results
  (2) No intra smoothing filtering on 8x8 PUs vs. HM-5.0 Anchor
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.06% | -0.02% | -0.01% | 0.11% | -0.04% | -0.05%
Class B | 0.06% | 0.00% | -0.02% | 0.10% | -0.02% | -0.04%
Class C | 0.00% | 0.01% | 0.04% | 0.03% | -0.01% | -0.02%
Class D | 0.03% | 0.04% | 0.02% | 0.05% | 0.00% | -0.01%
Class E | 0.03% | 0.00% | -0.02% | 0.08% | -0.06% | -0.02%
Overall | 0.04% | 0.01% | 0.00% | 0.07% | -0.02% | -0.03%
 | 0.03% | 0.00% | 0.01% | 0.07% | -0.02% | -0.03%
Class F | -0.03% | -0.03% | -0.01% | -0.01% | -0.02% | -0.04%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 97% |  | 

## Slide 7: Conclusion
As shown in the simulation results, both the proposed simplifications of MDIS have negligible impact on BD-rate while potentially reducing computational complexity in actual implementations.
  It is proposed to consider adoption of disabling intra smoothing for all intra modes on 8x8 PUs.