## Slide 1: Proposal to Improve Ultra Low Delay Coding with Minimal Decoder Impact (JCTVC-H0471)
Osnat Bar-Nir
February, 2012

## Slide 2: Background
Low-delay requires uniform picture size
Large variation in picture size increase the delay due to buffering
A way to achieve a semi-uniform picture size is to replace the I-pictures with a progressive intra-refresh mechanism
Column intra refresh is preferable:
  Easier to get accurate rate control (which is critical due to minimal buffer size)
  Enables lower percentage of Intra blocks in the picture (due to picture dimensions)
  Provides more uniform bit distribution within the picture

## Slide 3: Background
 |  | Refreshed Area |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Non Refreshed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Intra-refresh column |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Progressive intra refresh imposes some constraints on both inter and intra prediction:
pixels from the non-refreshed area can’t be used in the refreshed area
“refresh border”
moves one LCU to the right each frame

## Slide 4: Background
In-loop filtering constraint the predictions more:
pixels from the non-refreshed area contaminate the refreshed area -
“refresh border”
After In-loop Filtering
“Contaminate” pixels
 |  | Refreshed Area |  |  |  |  | 
 |  | Non Refreshed |  |  |  |  | 
 |  | Intra-refresh column |  |  |  |  | 
Next Frame
In-loop filters in previous frame
break inter prediction of this CU column

## Slide 5: Background
Pixels contaminated by filtering preclude (0,0) and other small MV, in the CU column left to the intra refresh column
Static texture areas can’t be predicted due to contamination, hence coded as Intra instead of skip
In average, more than 5% BD-Rate loss due to increased percentage of intra predicted CU in the column left to the intra refresh column
Class E videos lose more than 8% BD-Rate, due to highly textured static background
The loss can be avoided by disabling in-loop filtering across refresh border

## Slide 6: Proposal
Disable in-loop filtering across the refresh border and provide the refresh border location to the decoder
Refresh location can be indicated in PPS, Slice header or at least by a dedicated SEI message with a VUI flag
A normative approach is preferable