## Slide 1: JCTVC-H0477 On Just Noticeable Distortion Quantization in the HEVC Codec
R&D
© BBC MMXII
Matteo Naccari, Marta Mrak
BBC Research and Development

## Slide 2: Human visual system characteristics
The Human Visual System (HVS) shows a varying sensitivity to the distortion introduced by lossy coding:
Lower distortion areas
Higher distortion areas
Therefore one can perform:
  Coarse quantization → areas where the HVS is less sensitive to the distortion.
  Finer quantization → otherwise.

## Slide 3: HVS masking phenomena and just noticeable distortion
The HVS varying distortion sensitivity is due to some masking phenomena:
  Spatial masking: frequency decomposition, average pixel intensity, particular patterns.
  Temporal masking: motion component.
HVS Just Noticeable Distortion (JND): maximum distortion level that can be introduced in an image area without being noticeable to human observers.
With the JND level the quantization step Q can be modulated to obtain:
QJND = Q × JNDlevel.
QJND is the perceptual quantization step.

## Slide 4: Masking considered in this proposal
For perceptual quantization the masking due to the average pixel intensity is considered:
JND profile
Average original image TU pixel intensity
When integrating the perceptual quantization in the HEVC codec, two issues must be addressed:
  How to recover at the decoder the average pixel intensity µ (the original TU is needed).
  How to transmit the JND profile values.

## Slide 5: Integration in the HEVC codec: average pixel intensity estimation
Instead of sending the average pixel intensity µ for TU, it is estimated at the decoder as:
M, N are the block height and width.
P(·) is the block predictor (spatial or temporal).
Bitstream
Entropy decoding
Q-1
IDCT
+
Decoded
frame
Frame buffer
Intra
prediction
Motion compensation
Motion vectors
JND profile
In terms of decoder block diagram:
In-loop filters

## Slide 6: Integration in the HEVC codec: JND profile values transmission
The JND profile values are transmitted assuming linear piecewise approximation:
Four characteristics points may be noted (A, B, C and D).
Only the values JNDA, µB, JNDB, µC and JNDD are transmitted in the PPS.
The intermediate values are obtained by computing the straight lines passing through (A,B), (B,C) and (C,D).

## Slide 7: Summary
A set of informal subjective viewing has been conducted by the authors at the BBC R&D premises.
Using JND quantization the perceptual quality can remain the same and, bitrate reductions of up to 25% are observed:
Configuration | Sequence | QP | Bitrate reduction
ra_he | bqterrace | 22 | -25.42
ra_he | bqterrace | 27 | -17.87
ld_lc | vidyo4 | 22 | -20.92
ld_lc | vidyo4 | 27 | -13.59
The JND profile can be sent for each frame (as Quantization Matrices, QMs) with a lower bitrate than QMs.
The quantization step can be tuned at TU level, i.e. finer than dQP.
We recommend to include this tool to the standard, in a similar fashion as the QMs (optional tool for HVS-based improvements).
Many thanks to RIM for crosschecking!

## Slide 8: Used JND profile for experiments