## Slide 1: AHG21: Improvements to RPS Intra Prediction JCTVC-H0482 Jie Zhao and Andrew Segall
l
Notes: <number>

## Slide 2: Introduction
We observe that: RPS for RA test conditions, typically the first negative and the first positive delta POC have the same absolute value
Propose to initialize the first positive delta POC based on the symmetry with the first negative delta POC.
RPS for RA common test condition GOP size 8

## Slide 3: Proposal
The change to syntax table is in blue.
Signal a symmetric flag to indicate if the smallest positive delta POC is the same as the smallest absolute value of negative delta POC. When not present, symmetric_flag is default to 0.
If this symmetric_flag is true, then there is not need to read the first positive delta POC, it can be simply initialized to the smallest absolute value of negative delta POC.

## Slide 4: Proposed Change to Working Draft
7.4.3.1 Short-term reference picture set semantics
delta_poc_s1_minus1[ i ] plus 1 specifies an absolute difference between two picture order count values. The value of delta_poc_s1_minus1[ i ] shall be in the range of 0 to 215 – 1, inclusive.
The variable DeltaPocS1[ idx ][ i ] is derived as follows.
if (i== 0) {
if (symmetric_flag)
DeltaPocS1[ idx ][ i ] = -DeltaPocS0[ idx ][ i ]
else DeltaPocS1[ idx ][ i ] = delta_poc_s1_minus1[ i ] + 1 (7‑9)
}
else DeltaPocS1[ idx ][ i ] = DeltaPocS1[ idx ][ i – 1 ] + ( delta_poc_s1_minus1[ i ] + 1 )
Note: The only change is the red line
DeltaPocS0 contrains the negative delta POC and DeltaPocS1 contains the positive delta POC

## Slide 5: Combined with POC granularity in JCTVC-G643
We implemented POC granularity proposed in JCTVC-G643 (Also in JCTVC-H0425) as a delta POC scale
  DeltaPocS0[ idx ][ i ] = DeltaPocS0[ idx ][ i – 1 ] – (( delta_poc_s0_minus1[ i ] + 1 )<<deltaPOCScale) when i != 0
  DeltaPocS1[ idx ][ i ] = DeltaPocS1[ idx ][ i – 1 ] + (( delta_poc_s1_minus1[ i ] + 1 )<<deltaPOCScale) when i != 0
These two techniques both explore RPS intra prediction to save RPS bits.
They can be combined without conflict since POC granularity applies to DeltaPocS0 [ idx ][ i ] and DeltaPocS1 [ idx ][ i ] when i != 0; While our symmetric init technology only apply to DeltaPocS1 [ idx ][ i ] when i== 0.

## Slide 6: Result
Result: RA common test condition. Inter RPS off.
Note: * for POC scale, 3 extra bits are sent outside of RPS to signal deltaPOCScale=1

## Slide 7: Result
JCTVC-G1036 AHG21 Test Conditions

## Slide 8: Conclusion
The proposed positive delta POC symmetric init method reduces the bit-rate for RPS for random access configurations.
With this simple change, it saves about 6% RPSs bits when RPS is signaled without inter prediction.
Moreover, the technique also works with other intra RPS prediction such as delta POC granularity method in JCTVC-G643 to further improves the intra RPS prediction. Together, they can save over 20% RPS bits.
These intra RPS techniques are complementary to inter RPS technology. They are most advantageous for scenarios that use intra-RPS exclusively – such as encoders that only signal RPS information in the slice header.
Propose to adopt the positive delta POC symmetric init method into HM.