## Slide 1: JCTVC-H0490: Reduce the look-up table entries for LM mode calculation
Lingzhi Liu
Guichun Li

## Slide 2: Proposed
This contribution proposes to reduce the look-up table used in LM mode calculation from 63 entries to 56 entries or further to 32 entries.
  The entries from 1~7 are theoretically not used
  The entries from 1~31 are seldom used

## Slide 3: Current look-up table in LM mode
a3 = a2s < 1 ? 0 : Clip3( -215, 215-1, a1s*lmDiv + ( 1 << ( k1 – 1 ) ) >> k1 ) (14)
  a1s = a1 >> Max(0, log2( abs( a1 ) ) – 14 )
  a2s = abs( a2 >> Max(0, log2( abs( a2 ) ) – 5 ) )
  a2 = ( LL << k2 ) – L*L
  k3 = Max( 0, BitDepthC + log2( nS ) – 14 )
for( Int i = 1; i < 64; i++ )
lmDiv [i-1] = ( (1 << 15) + i/2 ) / i;

## Slide 4: Derivations
a2 = ( LL << k2 ) – L*L
Set
We have
If Δp!=0

## Slide 5: Reduce the number of entries
If the luma references are not all equal, the actual value of a2 is always equal or larger than 8.
Furthermore, if one of the item ΔpY’ is equal or larger than 2 or block size no smaller than 16, a2 will equal or larger than 32 accordingly. In this condition, lmDiv table can be reduced to 32 entries.

## Slide 6: Simulation results
 | All Intra HE |  | 
 | Y | U | V
Class A (8bit) | 0.01% | -0.03% | 0.01%
Class B | 0.00% | -0.01% | 0.02%
Class C | 0.00% | -0.03% | -0.01%
Class D | 0.00% | 0.01% | 0.00%
Class E | 0.00% | 0.02% | 0.01%
Overall | 0.00% | -0.01% | 0.00%
 | 0.00% | -0.01% | 0.00%
Class F | 0.00% | -0.01% | 0.03%
Enc Time[%] | 100% |  | 
Dec Time[%] | 101% |  | 
Testing results of 56 entries
Testing results of 32 entries
 | All Intra HE |  | 
 | Y | U | V
Class A (8bit) | 0.01% | -0.03% | -0.03%
Class B | 0.00% | 0.00% | 0.01%
Class C | 0.00% | -0.01% | 0.00%
Class D | -0.01% | 0.01% | -0.04%
Class E | 0.00% | -0.01% | -0.01%
Overall | 0.00% | -0.01% | -0.01%
 | 0.00% | -0.01% | -0.01%
Class F | -0.01% | -0.01% | 0.00%
Enc Time[%] | 100% |  | 
Dec Time[%] | 99% |  | 

## Slide 7
Thank You