## Slide 1: JCTVC-H0491: Remove the large multiplier for LM mode calculation
Lingzhi Liu
Guichun Li
Yongbing Lin

## Slide 2: Proposed
The proposed method removes the 13 (AI-HE) or 15-bit (AI-HE10) multipliers by 8 or 10-bit multipliers.
The BD-Rate for this optimization is: AI-HE: Y: 0.0%, U: 0.1%, V: 0.0% and AI-HE10: Y: 0.0%, U: 0.1%, V: 0.0%.
These modifications will contribute to complexity reduction both for HW and SW implementation.

## Slide 3: Steps of LM calculaiton in WD
Computational Complexity

## Slide 4: a1 and a2 in LM mode
Parameters:
a1 = ( LC << k2 ) – L*C a2 = ( LL << k2 ) – L*L
beta = ( L – ( ( alpha * C ) >> k1 ) + ( 1 << ( k2 – 1 ) ) ) >> k2
13-b by 13-b (IBD=8)
15-b by 15-b
(IBD=10)
26-b (IBD=8)
30-b
(IBD=10)
8-b (IBD=8)
10-b
(IBD=10)
13-b

## Slide 5: Remove the Large Multiplier
Set

## Slide 6: New calculation of LC and LL
beta = avgC – ( ( alpha * avgY’ ) >> k1 )
8-b singed (IBD=8)
10-b (IBD=10)
8-b

## Slide 7: Using unsigned multipliers
Set
8-b unsinged (IBD=8)
10-b (IBD=10)

## Slide 8: Steps (original vs unsiged version)

## Slide 9: Steps (original vs siged version)

## Slide 10: Complexity analysis
Step | Original LM |  |  | Prep. 1 |  |  | Prep. 2 |  | 
 | Mul | Add | Shift | Mul | Add | Shift | Mul | Add | Shift
Cal. of L, C | - | 2*2N M-b | - | - | 2*2N M-b | - | - | 2*2N M-b | -
Cal. of ΔpY, Δp | - | - | - | - | - | - | - | 2*2N 8-b | -
Cal. of LL, LC | 2*2N 8-b | 2*2N M-b | - | 2*2N 8-b | 2*2N M-b |  | 2N 8-b 2N 8-b (signed) | 2*2N M-b | -
Cal. of avgY’, avgC | - | - | - | - | - | 2 | - | - | 2
Cal. of RErrY’, RErrC | - | - | - | - | 2 xor | 2 | - | - | -
Cal. of a1 | 1 13-b | 1 26-b | 1 | 3 8-b | 2 16-b 1 8-b | 2 | - | - | -
Cal. of a2 | 1 13-b | 1 26-b | 1 | 2 8-b | 2 16-b | 2 | - | - | -
Cal. of beta | 1 13-b | 2 13-b | 3 | 1 8-b | 1 8-b | 1 | 1 8-b | 1 8-b | 1
Total operations | 4N 8-b 3 13-b | 8N M-b 2 13-b 2 26-b | 5 | 4N+6 8-b | 8N M-b 2 8-b 4 16-b 2 xor | 9 | 2N+1 8-b 2N 8-b (signed) | 8N M-b 4N 8-b | 3
Here N=4, 8 or 16, and M-b means multiple bit-length operators will be used.

## Slide 11: Testing results
 | All Intra HE |  | 
 | Y | U | V
Class A (8bit) | 0.0% | 0.1% | 0.1%
Class B | 0.0% | 0.3% | 0.0%
Class C | 0.0% | 0.1% | 0.0%
Class D | 0.0% | 0.1% | 0.0%
Class E | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.1% | 0.0%
 | 0.0% | 0.1% | 0.0%
Class F | 0.0% | 0.0% | 0.2%
Enc Time[%] | 99% |  | 
Dec Time[%] | 97% |  | 
 | All Intra HE10 |  | 
 | Y | U | V
Class A | 0.0% | 0.2% | 0.2%
Class B | 0.0% | 0.1% | 0.0%
Class C | 0.0% | 0.0% | 0.1%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.1% | 0.0%
 | 0.0% | 0.1% | 0.0%
Class F | 0.0% | 0.1% | 0.2%
Enc Time[%] | 103% |  | 
Dec Time[%] | 100% |  | 

## Slide 12
Thank You