## Slide 1: <JCTVC-H0510> Non-CE1: High Throughput Binarization (HTB) method with modified level coding
Seung-Hwan Kim, Kiran Misra,
Louis Kerofsky, Andrew Segall
<number>
Notes: <number>

## Slide 2: Motivation
Contribution
  Improve throughput efficiency (in level coding)
  - Replace the regular coded bins with bypass bins
  - Simplify the level coding structure (one pass coding)
  Flexible HTB structure
  - Selectively employ the HTB coding mode in each sub-block
  - Controlling the trade-off between coding efficiency and throughput
  efficiency
  Modified level coding for keeping coding performance
  - Combine sign information and level information
  - Binarizaton based on VLC tables in CAVLC
  - Binarization based on Golomb-rice code in HM
<number>
Notes: <number>

## Slide 3: Proposal: Coding Structure
<number>
Level coding in one-pass
Selective selection of HTB mode in each sub-block
Last_position_X
Last_position_Y
Significance Map
Level Coding
Greater_1
Greater_2
Sign coding
Absolute-3
END
Level Coding
END
Absolute-1
HTB==1 ?
No
Yes
If (# of significant_coeffs < = TH)
HTB =0;
Else HTB=1;
Notes: <number>

## Slide 4: Proposed level coding and binarization
<number>
sign | level | Input
+ | 1 | 0
- | 1 | 1
+ | 2 | 2
- | 2 | 3
+ | 3 | 4
- | 3 | 5
+ | 4 | 6
- | 4 | 7
… | … | …
  Mapping Table for Input Value
  1. Generate an “input value” by combining level
  information (absolute value-1) and sign information
  as follows
  input = (abs (coefficient[i])-1)<<1 + sign
  Golomb-rice code
  - The range of Golomb-rice parameter is extened to [0.1.2.3.4]
B. Binarization
A. Combined sign information and level
Notes: <number>

## Slide 5: BD-Rate vs. Throughput efficiency
Table 1. Common test conditions
 | M1 | M2+TH_2 | M2+TH_8
BD-Rate | 2.1 % | 1.2 % | 0.1 %
AVG-Saving | 20 % | 15 % | 6 %
AVG-W_saving | 24 % | 18 % | 9 %
Table 2. Low QP [1,5,9,13]
 | M1 | M2+TH_2 | M2+TH_8
BD-Rate | 2.2% | 2.0% | 1.0 %
AVG-Saving | 38 % | 37 % | 28 %
AVG-W_saving | 45 % | 45 % | 38 %
1. Method 1
  1. Binarization based on VLC tables
  2. TH=0
2. Method 2 + TH_2
  1. Binarization based on Golomb-rice
  2. TH=2
3. Method 2 + TH_8
  1. Binarization based on Golomb-rice
  2. TH=8

## Slide 6: Conclusion
Conclusion
  Propose flexible HTB coding structure between coding performance and HT efficiency
  Efficient coding performance with combined sign and level coding
  Compatibility with current entropy codec by employed existing binarization method
<number>

## Slide 7: Results
<number>
Table 1. BD-Rate performance at common test conditions Qp= [22, 27, 32, 37]
 | M1 |  |  | M2+TH_2 |  |  | M2+TH_8 |  | 
 | Y | U | V | Y | U | V | Y | U | V
AI-HE | 2.2% | 2.7% | 2.6% | 1.2% | 1.3% | 1.3% | 0.2% | 0.3% | 0.3%
RA-HE | 1.9% | 2.4% | 2.4% | 1.2% | 1.0% | 1.0% | 0.1% | 0.1% | 0.1%
LB-HE | 2.2% | 3.6% | 3.2% | 1.6% | 0.9% | 0.7% | 0.2% | 0.0% | 0.2%
AI-LC | 2.3% | 2.7% | 2.7% | 1.0% | 1.1% | 1.1% | 0.0% | 0.1% | 0.0%
RA-LC | 1.5% | 1.8% | 1.6% | 0.6% | 0.6% | 0.5% | 0.0% | 0.0% | -0.1%
LB-LC | 1.8% | 2.5% | 2.3% | 0.7% | 0.2% | 0.0% | 0.0% | -0.2% | -0.1%
RA-HE10 | 2.8% | 3.5% | 3.4% | 2.0% | 1.4% | 1.6% | 0.0% | -0.2% | -0.1%
Average | 2.1% | 2.7% | 2.6% | 1.2% | 0.9% | 0.9% | 0.1% | 0.0% | 0.0%

## Slide 8: Results
<number>
Table 2. BD-Rate performance at low QP test conditions Qp= [1, 5, 9, 13]
Configuration | M1 |  |  | M2+TH_2 |  |  | M2+TH_8 |  | 
 | Y | U | V | Y | U | V | Y | U | V
AI-HE | 1.3% | 1.2% | 1.2% | 0.9% | 1.3% | 1.4% | 0.6% | 0.8% | 0.8%
RA-HE | 2.7% | 3.4% | 3.2% | 3.1% | 3.5% | 3.3% | 1.9% | 1.9% | 1.7%
LB-HE | 2.9% | 3.4% | 3.4% | 1.6% | 0.9% | 0.7% | 0.3% | 0.4% | 0.4%
AI-LC | 1.3% | 1.0% | 1.0% | 0.7% | 0.9% | 0.9% | 0.3% | 0.4% | 0.4%
RA-LC | 2.1% | 2.3% | 2.1% | 1.8% | 2.1% | 1.9% | 0.6% | 0.7% | 0.6%
LB-LC | 2.1% | 2.3% | 2.3% | 2.0% | 2.1% | 2.0% | 0.8% | 0.7% | 0.7%
RA-HE10 | 2.9% | 4.4% | 4.4% | 3.7% | 4.2% | 3.9% | 2.0% | 2.0% | 1.8%
Average | 2.2% | 2.9% | 2.5% | 2.0% | 2.1% | 2.0% | 0.9% | 1.0% | 0.9%

## Slide 9: Results
<number>
Table3. Average savings of context coded bin at each configuration
Configuration | M1 |  | M2+TH_2 |  | M2+TH_8 | 
 | Common | Low QP | Common | Low QP | Common | Low QP
AI-HE | 29% | 45% | 25% | 44% | 11% | 37%
RA-HE | 19% | 38% | 16% | 37% | 5% | 27%
LB-HE | 17% | 37% | 12% | 38% | 3% | 28%
AI-LC | 25% | 43% | 20% | 42% | 8% | 35%
RA-LC | 15% | 33% | 11% | 32% | 3% | 19%
LB-LC | 13% | 32% | 8% | 30% | 1% | 19%
RA-HE10 | 23% | 39% | 9% | 39% | 9% | 28%
Average | 20% | 38% | 15% | 37% | 6% | 28%

## Slide 10: Results
<number>
Table3. Average savings of maximum context coded bin at each configuration
Configuration | M1 |  | M2+TH_2 |  | M2+TH_8 | 
 | Common | Low QP | Common | Low QP | Common | Low QP
AI-HE | 31% | 51% | 29% | 50% | 15% | 48%
RA-HE | 25% | 46% | 21% | 49% | 8% | 37%
LB-HE | 22% | 43% | 18% | 43% | 6% | 37%
AI-LC | 28% | 51% | 25% | 49% | 11% | 41%
RA-LC | 19% | 41% | 14% | 43% | 5% | 36%
LB-LC | 15% | 41% | 10% | 40% | 4% | 31%
RA-HE10 | 27% | 43% | 11% | 44% | 11% | 36%
Average | 24% | 45% | 18% | 45% | 9% | 38%