## Slide 1: CE1 B3: 8-bit Linear Initialization for CABAC (JCTVC-H0535)
Liwei Guo, Marta Karczewicz, Joel Sole, Rajan Joshi
Qualcomm Incorporated
Chuohao Yeo, Yih Han Tan, Zhengguo Li
Institute for Infocomm Research

## Slide 2: Introduction
HM5 piece-wise linear initialization
  Probability range is divided into several segments and each has its own slope
  3 Tables needed to specify the segments and calculate the slope.
Proposed method
  Linear initialization – no segments, one slope for the whole range
  No table needed

## Slide 3: Proposed method(1)
8 bit initialization value consists of two parts: 4-bit SlopeIdx and 4-bit IntersecIdx
SlopeIdx and IntersecIdx are converted into
slope m and offset n for linear initialization

## Slide 4: Proposed method (2)
Formula 1
  m = (SlopeIdx*78-689)>>4
  n = (IntersecIdx<<3) – 13
Formula 2
  A simplification of Formula 1
  m = SlopeIdx*5-45
  n = (IntersecIdx<<3) – 16

## Slide 5: Proposed method (3)
The following process is the same as HM4.0 to calculate CABAC state and MPS value, i.e.,
(1) ProbState = Clip(1,126, (m*QP>>4) + n);
(2) valMPS = ProbState>=64 ;
(3) m_ucState = valMps? (ProbState - 64 ):(63-ProbState);
(4) m_ucState = (m_ucState<<1) + valMps;

## Slide 6: Comparison with HM5.0 method
 | HM5 | Formula1 | Formula2
# of Tables | 3 | 0 | 0
Total table size (bytes) | 48 | 0 | 0
Number of operations | 24 | 17 | 16
WD Texts | 3 tables + texts | texts | texts

## Slide 7: Simulation
HM5.0 + linear initialization
  No new training performed. Initial values converted from HM5 initial values.
Common test conditions
  QP: 22-37
  Low QP: 17-32
  High QP: 27-42

## Slide 8: Simulation (Formula1)
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
normalQP | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
highQP | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
lowQP | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
normalQP | 0.0% | -0.1% | -0.1% | 0.0% | 0.2% | -0.1% | 0.0% | 0.0% | 0.1%
highQP | 0.0% | -0.2% | -0.1% | 0.0% | 0.2% | -0.2% | 0.0% | 0.1% | 0.1%
lowQP | 0.0% | -0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.1%
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
normalQP | 0.0% | -0.1% | -0.3% | 0.0% | -0.4% | -0.2% | 0.0% | 0.0% | 0.0%
highQP | 0.0% | -0.2% | -0.3% | 0.0% | -0.7% | -0.5% | 0.0% | 0.1% | 0.1%
lowQP | 0.0% | -0.1% | -0.2% | 0.0% | -0.2% | 0.0% | 0.0% | -0.1% | 0.0%
 | Low delay P HE |  |  | Low delay P LC |  |  | Low delay P HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
normalQP | 0.0% | 0.1% | -0.2% | 0.0% | -0.3% | -0.1% | -0.1% | 0.0% | 0.1%
highQP | 0.0% | 0.2% | -0.4% | 0.0% | -0.5% | 0.1% | 0.0% | 0.1% | 0.2%
lowQP | 0.0% | -0.1% | 0.0% | 0.0% | -0.2% | -0.1% | 0.0% | -0.1% | 0.0%

## Slide 9: Simulation (Formula2)
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
normalQP | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
highQP | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
lowQP | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
normalQP | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.1%
highQP | 0.0% | -0.1% | 0.0% | 0.0% | 0.2% | -0.2% | 0.0% | 0.0% | 0.1%
lowQP | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1%
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
normalQP | 0.0% | 0.1% | 0.0% | 0.0% | -0.3% | 0.0% | -0.1% | -0.1% | -0.1%
highQP | 0.0% | -0.2% | -0.4% | 0.0% | -0.9% | -0.2% | 0.0% | -0.2% | -0.2%
lowQP | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | Low delay P HE |  |  | Low delay P LC |  |  | Low delay P HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
normalQP | 0.0% | 0.2% | -0.1% | 0.1% | -0.1% | -0.3% | 0.0% | 0.1% | -0.1%
highQP | 0.0% | 0.2% | -0.6% | 0.0% | -0.3% | -0.2% | 0.0% | 0.0% | 0.0%
lowQP | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | -0.2% | 0.0% | 0.1% | -0.1%

## Slide 10: Conclusions
Simplified initialization process
  No segments for the probability
  One slope for the whole probability range
  No table needed for the software or WD texts
Same performance as current initialization in HM5.
Recommend adoption of Formula2 into HM.
Thanks to HHI for cross-checking

## Slide 11: Appendix
The next two pages show the WD texts change for Formula 2.

## Slide 12: Appendix: