## Slide 1: CABAC Contexts Reduction for Last Position Coding (JCTVC-H0537)
Liwei Guo, Marta Karczewicz, Wei-Jung Chien, Xianglin Wang
Feb. 2012

## Slide 2: Introduction
Last position coding in HM5
  Last position is encoded as a binary string
  ai : encoded with contexts
  bi : encoded without contexts (by pass)
  In total 60 contexts are used for last position coding
Proposed method:
  Merge contexts for bins with similar statistics
  Reduce contexts number from 60 to 44
  Reportedly 0.0% Y BD-rate change

## Slide 3: Contexts for last position coding in HM5
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 0 | 1 | 2 |  |  |  |  |  | 
TU 8x8 | 3 | 4 | 5 | 5 | 6 |  |  |  | 
TU 16x16 | 7 | 8 | 9 | 9 | 10 | 10 | 11 |  | 
TU 32x32 | 12 | 13 | 14 | 14 | 15 | 15 | 16 | 16 | 17
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 0 | 1 | 2 |  |  |  |  |  | 
TU 8x8 | 3 | 4 | 5 | 5 | 6 |  |  |  | 
TU 16x16 | 7 | 8 | 9 | 9 | 10 | 10 | 11 |  | 
Luma (18 contexts)
Chroma (12 contexts)
Last in X dimension and Y dimension have separate contexts, so
total contexts = (18+12)x2 = 60

## Slide 4: Proposed contexts for Last position coding
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 0 | 1 | 2 |  |  |  |  |  | 
TU 8x8 | 3 | 4 | 5 | 5 | 2 |  |  |  | 
TU 16x16 | 6 | 7 | 8 | 8 | 9 | 9 | 2 |  | 
TU 32x32 | 10 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 2
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 0 | 1 | 2 |  |  |  |  |  | 
TU 8x8 | 3 | 4 | 5 | 5 | 2 |  |  |  | 
TU 16x16 | 3 | 4 | 5 | 5 | 6 | 6 | 2 |  | 
Luma (15 contexts)
Chroma (7 contexts)
Total contexts = (15+7)x2 = 44
The last bins with context (an-1) from different block sizes share the same contexts.
Chroma 8x8 block and chroma 16x16 block share the same context set.

## Slide 5: Reduction in contexts
 | HM5 |  | Proposed | 
 | Luma | Chroma | Luma | Chroma
LastX | 18 | 12 | 15 | 7
LastY | 18 | 12 | 15 | 7
Total | 60 |  | 44 | 

## Slide 6: Simulation results
All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
0.00% | 0.06% | 0.07% | 0.01% | 0.05% | 0.03% |  |  | 
Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
-0.02% | -0.05% | 0.00% | 0.01% | 0.20% | -0.04% | 0.03% | 0.00% | 0.08%
Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
-0.03% | -0.02% | -0.02% | -0.04% | -0.04% | -0.12% |  |  | 
No increase in encoding time or decoding time is observed.

## Slide 7: Conclusions
Reduce 16 contexts for last position coding (a 26% reduction of the total 60 contexts in HM5)
0.0% Y BD-rate change
Recommend adoption of the proposed contexts
Thanks to Mitsubishi (JCTVC-H0612) for cross-checking

## Slide 8: Detail results- normal QP (1)
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.00% | 0.02% | 0.08% | 0.01% | 0.04% | 0.01%
Class B | 0.00% | 0.09% | 0.14% | 0.04% | 0.08% | 0.08%
Class C | 0.00% | 0.04% | 0.05% | 0.01% | 0.02% | 0.03%
Class D | -0.02% | 0.10% | 0.03% | 0.00% | 0.04% | -0.03%
Class E | -0.01% | 0.10% | 0.10% | 0.00% | 0.06% | 0.06%
Class F | -0.01% | -0.03% | 0.03% | 0.01% | 0.02% | -0.03%
Overall | 0.00% | 0.06% | 0.07% | 0.01% | 0.05% | 0.03%
 | 0.00% | 0.07% | 0.07% | 0.01% | 0.05% | 0.03%
Enc Time[%] | 97.03% |  |  | 98.20% |  | 
Dec Time[%] | 94.67% |  |  | 93.08% |  | 

## Slide 9: Detail results- normal QP (2)
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.01% | 0.02% | -0.32% | 0.02% | 0.01% | -0.17% | 0.05% | 0.23% | 0.25%
Class B | -0.02% | 0.09% | 0.10% | 0.03% | 0.19% | -0.03% | 0.03% | -0.07% | 0.09%
Class C | -0.02% | -0.02% | -0.07% | 0.01% | 0.12% | 0.03% | 0.01% | 0.19% | -0.04%
Class D | -0.03% | -0.30% | 0.12% | -0.02% | 0.41% | -0.04% | 0.02% | -0.35% | 0.02%
Class E |  |  |  |  |  |  |  |  | 
Class F | -0.06% | 0.14% | 0.12% | 0.00% | -0.15% | 0.12% | 0.01% | 0.01% | -0.04%
Overall | -0.02% | -0.05% | 0.00% | 0.01% | 0.20% | -0.04% | 0.03% | 0.00% | 0.08%
 | -0.02% | -0.08% | 0.00% | 0.01% | 0.21% | -0.06% | 0.03% | 0.02% | 0.08%
Enc Time[%] | 96.60% |  |  | 96.60% |  |  | 94.11% |  | 
Dec Time[%] | 94.35% |  |  | 94.84% |  |  | 93.18% |  | 

## Slide 10: Detail results- normal QP (3)
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.02% | 0.02% | 0.41% | 0.02% | 0.00% | 0.22%
Class C | 0.00% | 0.09% | 0.37% | -0.01% | 0.17% | -0.02%
Class D | 0.02% | -0.13% | -0.31% | -0.02% | 0.70% | -0.48%
Class E | -0.04% | -0.03% | -0.93% | -0.01% | -0.36% | 0.20%
Class F | -0.12% | -0.07% | 0.04% | -0.17% | -0.78% | -0.52%
Overall | -0.03% | -0.02% | -0.02% | -0.04% | -0.04% | -0.12%
 | -0.03% | -0.04% | -0.02% | -0.03% | -0.01% | -0.07%
Enc Time[%] | 96.26% |  |  | 97.75% |  | 
Dec Time[%] | 93.33% |  |  | 92.85% |  | 

## Slide 11: Detail results- normal QP (4)
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.01% | 0.17% | 0.03% | 0.00% | 0.27% | -0.17%
Class C | 0.04% | 0.13% | -0.16% | 0.01% | -0.01% | 0.11%
Class D | -0.01% | 0.53% | -0.46% | -0.02% | 0.13% | 0.53%
Class E | -0.01% | 0.02% | -1.08% | -0.01% | -0.64% | -0.10%
Class F | 0.08% | 0.43% | 0.45% | -0.08% | 0.21% | 0.71%
Overall | 0.02% | 0.26% | -0.19% | -0.02% | 0.04% | 0.21%
 | 0.02% | 0.22% | -0.23% | -0.02% | 0.03% | 0.16%
Enc Time[%] | 97.35% |  |  | 97.31% |  | 
Dec Time[%] | 92.13% |  |  | 93.40% |  | 

## Slide 12: Additional results- low QP 12-27 (1)
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.01% | 0.02% | 0.03% | 0.02% | 0.02% | 0.02%
Class B | 0.02% | 0.03% | 0.08% | 0.04% | 0.07% | 0.07%
Class C | 0.00% | 0.02% | 0.04% | 0.01% | 0.03% | 0.04%
Class D | 0.00% | 0.02% | 0.01% | 0.00% | 0.02% | 0.01%
Class E | 0.00% | 0.11% | 0.12% | 0.02% | 0.05% | 0.06%
Class F | 0.00% | 0.00% | 0.02% | 0.01% | 0.02% | 0.06%
Overall | 0.01% | 0.03% | 0.05% | 0.02% | 0.04% | 0.04%
 | 0.01% | 0.03% | 0.05% | 0.02% | 0.04% | 0.04%

## Slide 13: Additional results- low QP 12-27(2)
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.04% | 0.02% | 0.02% | -0.01% | 0.01% | 0.02% | 0.00% | 0.06% | 0.01%
Class B | 0.01% | 0.08% | 0.12% | 0.01% | 0.08% | 0.11% | 0.02% | 0.05% | 0.05%
Class C | 0.00% | 0.07% | 0.00% | 0.00% | 0.12% | 0.05% |  |  | 
Class D | -0.01% | -0.03% | 0.05% | -0.01% | 0.14% | -0.04% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Class F | -0.05% | 0.06% | 0.01% | 0.04% | -0.02% | 0.05% |  |  | 
Overall | 0.01% | 0.04% | 0.06% | 0.00% | 0.10% | 0.04% |  |  | 
 | 0.01% | 0.04% | 0.06% | 0.00% | 0.10% | 0.04% |  |  | 

## Slide 14: Additional results- low QP 12-27(3)
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.01% | 0.08% | 0.13% | 0.02% | 0.12% | 0.03%
Class C | 0.00% | 0.00% | 0.12% | 0.01% | 0.08% | 0.08%
Class D | 0.01% | 0.03% | -0.10% | -0.02% | 0.04% | -0.05%
Class E | -0.01% | 0.12% | 0.28% | 0.00% | -0.08% | 0.27%
Class F | -0.11% | -0.11% | -0.11% | 0.11% | 0.36% | -0.04%
Overall | -0.02% | 0.02% | 0.06% | 0.02% | 0.11% | 0.05%
 | -0.02% | 0.01% | 0.07% | 0.02% | 0.13% | 0.06%

## Slide 15: Additional results- low QP 12-27 (4)
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.01% | 0.02% | 0.14% | 0.02% | 0.11% | -0.01%
Class C | 0.01% | 0.03% | 0.07% | 0.01% | 0.02% | 0.02%
Class D | -0.01% | 0.03% | -0.16% | -0.02% | 0.00% | 0.15%
Class E | 0.02% | -0.01% | -0.02% | 0.02% | -0.66% | -0.10%
Class F | -0.17% | 0.05% | 0.11% | -0.02% | 0.00% | -0.09%
Overall | -0.03% | 0.03% | 0.03% | 0.00% | -0.07% | 0.00%
 | -0.03% | 0.03% | 0.04% | 0.00% | -0.06% | 0.00%

## Slide 16
Thank you!