## Slide 1: CE1 subtest B4: On CABAC_init_idc JCTVC-H0540 [JCTVC-G716] Kiran Misra and Andrew Segall
l
Notes: <number>

## Slide 2: Overview
We propose to clarify the meaning of cabac_init_idc
Our benefits
  Reduced number of tables compared to AVC
  Improvements in coding efficiency
  Clarification of the HEVC design
Software was distributed to CE1 participants

## Slide 3: Background
cabac_init_idc (H.264/AVC)
  cabac_init_idc is signaled to control the initialization of CABAC
  For P and B slices, cabac_init_idc allows selection between three initialization tables
  Total number of tables: 7
      (1-Intra, 3-P, 3-B)
HEVC Working Draft 5
  aps_cabac_init_idc syntax in the APS
  Semantics indicate support for 7 tables
aps_cabac_init_idc specifies the index for determining the initialisation table used in the initialisation process for context variables of SAO and ALF. The value of cabac_init_idc shall be in the range of 0 to 2, inclusive.
HEVC WD5
      7.3.2.3 Adaptation parameter set RBSP syntax

## Slide 4: Further Motivation
Our findings
  We observe that selectively using the P slice table for B slices (and B slice tables for P slices) does provide coding benefit.

## Slide 5: Problem
Our proposal
  Maintain the number of tables for CABAC initialization to three.
  Define cabac_init_idc to be a one-bit flag to allow for P slice types to be initialized with either the “P slice type” table or “B slice type” table. Similarly, to allow for B slice types to be initialized with either the “P slice type” table or “B slice type” table.
  Signal the presence of cabac_init_idc in the PPS (or SPS if single entropy coder)
  Optionally, rename the syntax element to cabac_init_flag.

## Slide 6: Background
Synatax and semantics
cabac_init_idc specifies the index for determining the initialisation table used in the initialisation process for context variables. When cabac_init_idc is not present, it shall be inferred to be 0.
HEVC WD4
cabac_init_idc_enabled_flag equal to 0 specifies that cabac_init_idc is not present in the slice header. When cabac_init_idc_enabled_flag is not present, it shall be inferred to be 0.
7.3.3 Slice Header Syntax
7.3.2.2 Picture parameter set RBSP syntax

## Slide 7: Result [Cross check JCTVC-H0167]
Average Impact on BD rate
Common conditions QP: 22, 27, 32, 37
  LD_B_HE : -0.2% (Y) 0.1% (U) -0.2% (V) LD_B_LC : -0.2% (Y) -0.1% (U) -0.1% (V)
  RA_HE : -0.1% (Y) -0.2% (U) -0.2% (V) RA_LC : -0.1% (Y) -0.2% (U) -0.2% (V)
  RA_HE_10 : -0.1% (Y) -0.2% (U) -0.1% (V)
  AI_HE : 0.0% (Y) 0.0% (U) 0.0% (V) AI_LC : 0.0% (Y) 0.0% (U) 0.0% (V)
Class F results:
  LD_B_HE [Class F H0540] : -0.3% (Y) -0.5% (U) -0.7% (V)
Observations:
The average Y BD bitrate for inter-predicted cases is between -0.1% and -0.2%
Difference in JCTVC-H0540 from JCTVC-G716:
A process to initialize a forward predicted B-slice with the P-slice table was removed.
The encoder control was modified to use a 2-pass approach

## Slide 8: Result [Cross check JCTVC-H0167]
Remaining BD rate results [CE1 subtest B conditions defined JCTVC-G1201]
High QP: 27, 32, 37, 42
  LD_B_HE : -0.2% (Y) -0.1% (U) -0.3% (V) LD_B_LC : -0.2% (Y) -0.3% (U) -0.2% (V)
  RA_HE : -0.1% (Y) -0.3% (U) -0.3% (V) RA_LC : -0.2% (Y) -0.3% (U) -0.3% (V)
  RA_HE_10 : -0.1% (Y) -0.1% (U) -0.2% (V)
  AI_HE : 0.0% (Y) 0.0% (U) 0.0% (V) AI_LC : 0.0% (Y) 0.0% (U) 0.0% (V)
Low QP: 17, 22, 27, 32
  LD_B_HE : -0.1% (Y) 0.0% (U) -0.2% (V) LD_B_LC : -0.2% (Y) -0.1% (U) 0.0% (V)
  RA_HE : -0.1% (Y) -0.1% (U) -0.1% (V) RA_LC : -0.1% (Y) -0.1% (U) -0.1% (V)
  RA_HE_10 : -0.1% (Y) -0.1% (U) -0.1% (V)
  AI_HE : 0.0% (Y) 0.0% (U) 0.0% (V) AI_LC : 0.0% (Y) 0.0% (U) 0.0% (V)

## Slide 9: Supplemental Information
We observe gains for sequences outside of the test set when using one pass encoding
QCIF (with 1500 byte slices – HM 5.1)
Low delay B HE | BD-rate (piecewise cubic) |  | 
QCIF | Y | U | V
akiyo | -0.7% | -1.9% | -1.7%
bowing | -0.4% | 0.3% | 0.3%
carphone | 0.4% | 0.4% | 3.7%
coastguard | 0.3% | 0.4% | 6.1%
container | -0.7% | 0.6% | 0.8%
football | 0.0% | 0.2% | -0.7%
foreman | -0.5% | -0.4% | -0.2%
mobile | -0.5% | -0.4% | -0.2%
motherdaughter | -0.5% | -1.1% | 2.1%
news | -0.1% | -1.9% | -0.8%
silent | 0.4% | 0.6% | -0.5%
stefan | 0.0% | -0.3% | 0.4%
table | -0.1% | -1.1% | -0.3%
AVERAGE | -0.2% | -0.4% | 0.7%
Low delay B LC | BD-rate (piecewise cubic) |  | 
QCIF | Y | U | V
akiyo | -0.2% | -0.4% | -1.3%
bowing | 0.0% | -0.4% | 1.1%
carphone | -0.6% | -3.0% | -1.5%
coastguard | 0.2% | -3.0% | 2.6%
container | 0.0% | 1.3% | 0.5%
football | 0.0% | -0.2% | -0.4%
foreman | -0.3% | -0.2% | -0.5%
mobile | -0.3% | -0.2% | -0.5%
motherdaughter | 0.1% | -1.6% | -1.0%
news | -0.2% | 0.8% | 0.0%
silent | -0.4% | -1.5% | -0.4%
stefan | -0.2% | -0.7% | -0.5%
table | -0.4% | 3.3% | -0.2%
AVERAGE | -0.2% | -0.4% | -0.1%

## Slide 10: Supplemental Information
We observe gains for sequences outside of the test set when using one pass encoding
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | 0.0% | 0.2%
Class C | 0.0% | 0.0% | 0.1%
Class D | 0.0% | -0.1% | 0.1%
Class E | 0.0% | 0.0% | -0.1%
Class F | -0.2% | -0.3% | -0.2%
Overall | 0.0% | -0.1% | 0.0%
 | 0.0% | -0.1% | 0.0%
Common Test Conditions

## Slide 11: Conclusions
Conclusions
  We propose clarification of the cabac_init_idc flag
  Two components
    Number of CABAC initialization tables defined to be 3
    cabac_init_idc is defined as a binary flag that allows selection of either the “P” or “B” table for all inter-predicted slices.
  Benefits
    Clarification of the design
    Reduced number of number of tables compared to H.264/AVC
    Coding efficiency improvement
  Propose to adopt to WD.