## Slide 1: JCTVC-H0312: Clipping of Transformed Coefficients before Dequantization
Xiang Li, Xun Guo, Louis Kerofsky, Shawmin Lei, and Andrew Segall
<number>
JCTVC-H0541: Limiting dynamic range when using a quantization weighing matrix
Notes: <number>

## Slide 2: Motivation
BoG on Quantization in Geneva (JCTVC-G1044):
  Analyzed the bit-width requirements of supporting a quantization weighting matrix.
  Identified the possibility that level values could exceed 16-bits when small weighting values and low QP are used with large coefficients.
  Identified a possible 32-bit overflow in dequantization with using large weighting values
This contribution: We refine the dynamic range analysis. Specifically, we:
  Identify conditions when level values will exceed 16-bits
  Refine the conditions that lead to 32-bit overflow (compared to JCTVC-G1044)
  Propose solution to ensure (i) input to dequantization does not exceed 16-bits and (ii) 32-bit overflow is avoided during dequantization.
Note: Similar approach is reported in JCTVC-H0312. The authors have discussed in detail off-line leading to this joint proposal
<number>
Notes: <number>

## Slide 3: Dequantization with weighting matrix
Background and Definitions:
  B = internal bit depth (typically B=8)
  N = transform size
  M = log2(N)
  IQ = g(QP%6), where g(x) = {40,45,51,57,64,72}, x=0,…,5
  W[i][j] = 8-bit unsigned weighting matrix
Equations:
  coeffQ[i][j] = ((level[i][j]*W[i][j]*IQ[QP%6] << (QP/6)) + offset)>>(M-1+(B-8)+4),
  offset = 1<<(M-2+(B-8)+4), with i=0…nW-1, j = 0..nH-1
  coeffQ = min(32767,max(-32768,coeffQ))
To reduce overflow compute as:
iShift = M-1+B-8+4;
offset = 1<<(iShift-QP/6-1);
If (iShift > QP/6)
coeffQ[i][j] = (level[i][j]*W[i][j]*IQ[QP%6] + offset)>>(iShift-QP/6);
else
coeffQ[i][j] = (level[i][j]*W[i][j]*IQ[QP%6] + offset) << (QP/6-iShift);
coeffQ = min(32767,max(-32768,coeffQ))
Confidential
<number>

## Slide 4: Levels exceeding 16-bits
Topic #1: Will level values exceed 16-bits in practice?
Analysis:
The plot below shows the Max Level produced from a maximum 16-bit coefficient assuming a weighting value of 1 for various QP. (Note: Quantization with weighting value less than 16 has the effect of using a smaller bin size.)
  MaxLevel = (32768<<(M+3))>>(QP/6)/(IQ[QP%6])
Observe for QP≥16, the Max Level does not exceed 16-bits; however for lower QP the Max Level value may exceed 16-bits.
Confidential
<number>

## Slide 5: 32-bit overflow
Topic #2: 32-bit overflow
Analysis: The potential for 32-bit overflow was identified in JCTVC-G1044 based on combination of worst case inputs to the formula:
  coeffQ[i][j] = (level[i][j]*W[i][j]*IQ[QP%6] + offset) << (QP/6-iShift)
  A worst case combination notes: Level 16-bits, W 8-bits, IQ 7-bits, QP/6-iShift = 3
  Combination yields: 16+8+7+3 = 34 >32
This can be refined by noting on the limited range QP=(0-51), the worst case combination of 7-bits for IQ does not occur at the worst case of QP/6-iShift. Additionally, tracking the block size in iShift yields a worst case:
  At extreme, Level 16-bits, W 8-bits, IQ 6-bits, QP/6-iShift = QP/6-M-3 =5-M
  Combination yields: 16+8+6+5-M = 35-M =(33,32,31,30) for M=(2,3,4,5)
A plot of bit-width versus QP assuming W=255 is shown below. Note 32-bit overflow is confined to M=4 and QP≥47
Confidential
<number>

## Slide 6: Proposed Change
Proposed solution: Both identified issues can be addressed by clipping the level data prior to dequantization:
  To ensure 16-bit level values -- the level data should be clipped to 16-bits
  To ensure 32-bit dequantization – the level data should be clipped to 15-bits for 4x4 blocks and large QPs.
  Note: This change supports all block sizes as well as NSQT.
Proposed text
We request adoption of the method to ensure (i) 16-bit level values and (ii) 32-bit de-quantization