## Slide 1: CE6.a:: New Modes for Chroma Intra Prediction (LML and LMA)
Xingyu Zhang, Oscar C. Au,
Jingjing Dai, Feng Zou, Chao Pang, Xing Wen

## Slide 2: JCTVC-H544
Outline
1. Overview
2. Proposed Modes LML and LMA
Simulation results
Conclusion

## Slide 3
Chroma Intra Prediction Mode | Codeword | IntraPredMode |  |  |  | 
 |  | 0 | 1 | 2 | 3 | X ( 0 <= X < 35 )
DM | 0 | 0 | 1 | 2 | 3 | X
LM | 10 | LM | LM | LM | LM | LM
Planar | 110 | 7 | 0 | 0 | 0 | 0
Vertical | 1110 | 1 | 7 | 1 | 1 | 1
Horizontal | 11110 | 2 | 2 | 7 | 2 | 2
DC | 11111 | 3 | 3 | 3 | 7 | 3
JCTVC-H544
Overview
6 modes are used in chroma intra prediction:
DM, LM, Planar, Vertical, Horizontal, and DC.
When one of the last four modes is the same with DM, Ver+8 will replace it.

## Slide 4: JCTVC-H544
LM mode: Using a linear model to predict Chroma from Luma.
Parameters alpha and beta are very important for prediction correctness.
Fig. 1 2N neighboring samples are used for parameters derivation in LM mode (L shape template)
Overview

## Slide 5: JCTVC-H544
Analysis
However, hints of B can be found in the left lower portion of the neighborhood.
A
B
In the example, no training samples in the L-shape neighborhood can give any hint of object B.
Thus, object B cannot be well predicted by LM mode.

## Slide 6: JCTVC-H544
Proposed Modes: LML and LMA
Fig. 2 In total, 2N neighboring samples are used for parameters derivation in LML mode
Fig. 3 In total, 2N neighboring samples are used for parameters derivation in LMA mode
(Essentially same as LM except training samples taken at different locations)

## Slide 7: JCTVC-H544
Results
 | All Intra HE |  |  | 
 | Y | U | V | YUV
Class A (8bit) | -0.1% | -2.0% | -1.6% | -0.4%
Class B | -0.1% | -2.6% | -2.1% | -0.5%
Class C | -0.2% | -2.3% | -2.9% | -0.6%
Class D | -0.1% | -2.1% | -2.3% | -0.5%
Class E | 0.0% | -1.7% | -1.8% | -0.3%
Overall | -0.11% | -2.22% | -2.21% | -0.47%
 | -0.1% | -2.2% | -2.2% | -0.5%
Class F | -0.4% | -2.5% | -3.0% | -0.8%
Enc Time[%] | 104% |  |  | 
Dec Time[%] | 101% |  |  | 
 | All Intra HE |  |  |  | All Intra HE-10 |  |  | 
 | Y | U | V | YUV | Y | U | V | YUV
Class A | -0.2% | -9.0% | -9.3% | -1.4% | -0.2% | -9.0% | -9.7% | -1.4%
Class B | -0.1% | -2.6% | -2.1% | -0.5% | -0.1% | -2.8% | -2.2% | -0.5%
Class C | -0.2% | -2.3% | -2.9% | -0.6% | -0.2% | -2.4% | -3.0% | -0.6%
Class D | -0.1% | -2.1% | -2.3% | -0.5% | -0.1% | -2.2% | -2.4% | -0.5%
Class E | 0.0% | -1.7% | -1.8% | -0.3% | 0.0% | -1.8% | -1.9% | -0.3%
Class F | -0.4% | -2.5% | -3.0% | -0.8% | -0.4% | -2.5% | -3.3% | -0.8%
Overall | -0.2% | -3.4% | -3.6% | -0.7% | -0.2% | -3.5% | -3.7% | -0.7%
 | -0.2% | -3.4% | -3.5% | -0.7% | -0.2% | -3.5% | -3.7% | -0.7%
Enc Time[%] | 104% |  |  |  | 104% |  |  | 
Dec Time[%] | 101% |  |  |  | 100% |  |  | 
LML and LMA are added as two independent modes in HM5.0. It is placed after DM mode and LM mode.

## Slide 8: JCTVC-H544
Conclusion
Good RD performance
Complexity of LMA and LML similar to that of LM
No new syntax

## Slide 9: Thank you

## Slide 10: JCTVC-H544
Appendix
 | All Intra HE |  |  | 
 | Y | U | V | YUV
Class A (8bit) | -0.1% | -2.0% | -1.6% | -0.4%
Class B | -0.1% | -2.6% | -2.1% | -0.5%
Class C | -0.2% | -2.3% | -2.9% | -0.6%
Class D | -0.1% | -2.1% | -2.3% | -0.5%
Class E | 0.0% | -1.7% | -1.8% | -0.3%
Overall | -0.11% | -2.22% | -2.21% | -0.47%
 | -0.1% | -2.2% | -2.2% | -0.5%
Class F | -0.4% | -2.5% | -3.0% | -0.8%
Enc Time[%] | 104% |  |  | 
Dec Time[%] | 101% |  |  | 
Trivial loss when applying 2:1 sub-sampling to the neighborhood in LM, LML and LMA.
(All block sizes are included: 16x16, 8x8, and 4x4)
 | All Intra HE |  |  | 
 | Y | U | V | YUV
Class A (8bit) | -0.1% | -2.0% | -1.5% | -0.4%
Class B | -0.1% | -2.7% | -2.0% | -0.5%
Class C | -0.1% | -2.1% | -2.7% | -0.5%
Class D | -0.1% | -1.9% | -2.1% | -0.4%
Class E | 0.0% | -1.7% | -1.9% | -0.4%
Overall | -0.1% | -2.1% | -2.1% | -0.4%
 | -0.1% | -2.1% | -2.1% | -0.4%
Class F | -0.3% | -2.3% | -2.7% | -0.7%
Enc Time[%] | 104% |  |  | 
Dec Time[%] | 100% |  |  | 
Without Subsample
With Subsample
Test 1:

## Slide 11: JCTVC-H544
Appendix
Test 2:
Integration with JCTVC-H0464: Using averaged down-sampling reference pixels in LM parameter generation.
JCTVC-H0464 is applied to LM, LML and LMA at the same time.
 | All Intra HE |  |  | 
 | Y | U | V | YUV
Class A (8bit) | -0.1% | -1.9% | -1.4% | -0.3%
Class B | -0.1% | -2.3% | -2.0% | -0.4%
Class C | -0.1% | -2.3% | -2.8% | -0.6%
Class D | -0.1% | -2.0% | -2.2% | -0.4%
Class E | 0.0% | -1.7% | -2.1% | -0.4%
Overall | -0.1% | -2.1% | -2.2% | -0.4%
 | -0.1% | -2.1% | -2.2% | -0.4%
Class F | -0.3% | -2.4% | -2.9% | -0.8%
 | All Intra HE |  |  | 
 | Y | U | V | YUV
Class A (8bit) | -0.1% | -1.9% | -1.5% | -0.3%
Class B | -0.1% | -2.4% | -2.0% | -0.5%
Class C | -0.1% | -2.2% | -2.8% | -0.6%
Class D | -0.1% | -2.1% | -2.3% | -0.4%
Class E | 0.0% | -1.7% | -1.9% | -0.4%
Overall | -0.1% | -2.1% | -2.2% | -0.4%
 | -0.1% | -2.1% | -2.1% | -0.4%
Class F | -0.3% | -2.3% | -2.9% | -0.8%
H0544+H0464_Case1
H0544+H0464_Case2