## Slide 1: JCTVC-H0545:Context modeling for asymmetric partitioning on partition mode
Wei-Jung Chien, Xianglin Wang, Marta Karczewicz
Qualcomm

## Slide 2: Introduction
Syntax element, part_mode, specifies the partition mode for the CU
  1st bin is to specifiy whether the current CU contains multiple PUs.
  2nd bin signal the orientation of the partition direction (vertical or horizontal).
  3rd bin
  3rd bin is to indicate whether the size of the first partition is one-fourth or three-fourth of the CU size.
  Total 4 contexts are used in the 2nd and the 3rd bins.
JCTVC-H099: removing all 4 contexts
Proposed method: 1 context on 2nd bin only

## Slide 3: Simulation results
 | Random Access HE |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.1% |  |  | 
Class D | 0.0% | -0.1% | -0.1% |  |  | 
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class F | -0.1% | -0.1% | 0.0% |  |  | 
Enc Time[%] | 101% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.1% | 0.2% |  |  | 
Class C | 0.0% | -0.2% | 0.0% |  |  | 
Class D | 0.0% | -0.3% | -0.1% |  |  | 
Class E | 0.0% | 0.2% | 0.4% |  |  | 
Overall | 0.0% | -0.1% | 0.1% |  |  | 
 | 0.0% | -0.1% | 0.1% |  |  | 
Class F | -0.1% | -0.2% | -0.5% |  |  | 
Enc Time[%] | 101% |  |  |  |  | 
Dec Time[%] | 100% |  |  |  |  | 

## Slide 4: Simulation results of disabling AMP at encoder RDO (HM5.0 vs JCTVC-H0099)
 | Random Access HE |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.3% | 0.2% | 0.2% | 0.2% | 0.2% | 0.0%
Class B | 0.2% | 0.2% | 0.2% | 0.2% | 0.1% | 0.1%
Class C | 0.2% | 0.2% | 0.2% |  |  | 
Class D | 0.1% | -0.1% | 0.0% |  |  | 
Class E |  |  |  |  |  | 
Overall | 0.2% | 0.1% | 0.1% | 0.2% | 0.1% | 0.1%
 | 0.2% | 0.1% | 0.1% | 0.2% | 0.1% | 0.1%
Class F | 0.1% | 0.1% | 0.1% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.3% | 0.5% | 0.5% |  |  | 
Class C | 0.2% | 0.2% | 0.2% |  |  | 
Class D | 0.1% | 0.3% | 0.1% |  |  | 
Class E | 0.5% | 0.9% | 0.2% |  |  | 
Overall | 0.3% | 0.4% | 0.3% |  |  | 
 | 0.3% | 0.4% | 0.2% |  |  | 
Class F | 0.1% | 0.0% | -0.3% |  |  | 
Enc Time[%] | 99% |  |  |  |  | 
Dec Time[%] | 100% |  |  |  |  | 

## Slide 5: Simulation results of disabling AMP at encoder RDO (HM5.0 vs Proposed method)
 | Random Access HE |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V
Class A (8bit) | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.1% |  |  | 
Class D | 0.0% | -0.1% | -0.1% |  |  | 
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class F | 0.0% | 0.1% | 0.0% |  |  | 
Enc Time[%] | 99% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | 0.0% | 0.3% |  |  | 
Class C | -0.1% | -0.2% | -0.1% |  |  | 
Class D | -0.1% | 0.0% | -0.2% |  |  | 
Class E | -0.1% | 0.3% | 0.0% |  |  | 
Overall | -0.1% | 0.0% | 0.0% |  |  | 
 | -0.1% | 0.0% | 0.0% |  |  | 
Class F | -0.2% | -0.5% | -0.5% |  |  | 
Enc Time[%] | 100% |  |  |  |  | 
Dec Time[%] | 100% |  |  |  |  | 

## Slide 6: Conclusions
Removing 3 redundant contexts from partition mode
No performance difference under different test cases
  Common test condition
  Disabling AMP at encoder RDO
Suggest to adopt the proposed solution into HM.