## Slide 1: AHG4: Harmonized method for signalling entry points of tiles and WPP substreams JCTVC-H0566 Hendry, Sangoh Jeong, Seung Wook Park, Byeong Moon Jeon (LG), Kiran Misra, Andrew Segall (Sharp)
l
Notes: <number>

## Slide 2: Overview
In the Torino JCTVC meeting [Jul 2011], WPP and Tiles were adopted into HM
Both approaches include a system for signaling entry points to the decoder
  Required for WPP decoding
  Enables parallel processing
  Allows for low latency decoding of Tiles
We propose to harmonize the solutions and use a single method for signaling the entry points

## Slide 3: Progression
 | Torino Jul 2011 | Geneva Nov 2011 | Proposed
Tiles WPP | Byte-aligned [JCTVC F335] Bit-aligned [JCTVC F274] | Byte-aligned Tiles + Bit-aligned WPP [JCTVC G722] | Byte-aligned Tiles + Byte-aligned WPP [JCTVC H0556]
 | Separate signaling mechanism | Single signaling mechanism | Single signaling mechanism

## Slide 4: Proposed Change
Proposed Changes
  Byte-align WPP substreams
  Merge substream and tile signaling into single syntax
slice_header( ) { | Descriptor
… | 
entry_point_locations_flag | u(1)
if (entry_point_locations_flag == 1) { | 
entry_point_locations () | 
} | 
} | 
entry_point_locations_flag indicates the presence of entry point information in the bit-stream When not present, entry_point_locations_flag shall be 0.
Syntax element in Slice header

## Slide 5: Location information syntax
entry_point_ locations() | Descriptor
num_of_entry_points_minus1 | ue(v)
entry_point_offset_length_minus1 | ue(v)
for (i=0; i<=num_of_entry_points_minus1; i++) { | 
if ((num_tile_columns_minus1 > 0 ¦¦ num_tile_rows_minus1 > 0) && num_substreams_minus1 > 0) { | 
entry_point_type[i] | u(1)
} | 
else if (num_substreams_minus1 > 0) { | 
entry_point_type [i] = 1 | 
} | 
else { | 
entry_point_type [i] = 0 | 
} | 
entry_point_offset[i] | u(v)
} | 
} | 
num_of_entry_points_minus1 plus 1 defines the number of bit-stream entry points in the slice
entry_point_offset_length_minus1 plus 1 specifies the number of bits used to signal entry_point_offset[i] entries.
entry_point_type[i] indicates the entry point type. entry_point_type[i] equals to 0 indicates a tile entry point; entry_point_type[i] equals to 1 indicates a substream entry point.
entry_point_offset [i] specifies the number of bytes between two entry points. When i equals 0, it specifies the number of bytes between the end of the slice header and the first entry point in the slice; otherwise, it defines the number of bytes between the entry point i - 1 and entry point i. The length of entry_point_offset [i] is entry_point_offset_length_minus1 + 1 bits.
Entry point location information

## Slide 6: Results for unified signalling of entry points of tiles and WPP substreams
The setting used for the test is:
- 4 independent tiles (2 rows and 2 columns)
- 2 WPP substreams in each tile (WaveFrontSynchro = 1)
 | Y | U | V
INHE | 0.0% | 0.0% | 0.0%
INLC | 0.0% | 0.0% | 0.0%
RAHE | -0.2% | -0.2% | -0.2%
RALC | -0.2% | -0.2% | -0.2%
LBHE | -0.1% | -0.1% | -0.1%
LBLC | -0.3% | -0.3% | -0.3%
LPHE | -0.3% | -0.3% | -0.3%
LPLC | -0.3% | -0.3% | -0.3%

## Slide 7: Conclusions
Conclusions
  Propose harmonized method for signaling WPP and Tile entry points
  Request adoption of this technique to HM

## Slide 8: Result from byte-aligned WPP substreams with original entry point signaling
 | Y | U | V
INHE | 0.0% | 0.0% | 0.0%
INLC | 0.0% | 0.0% | 0.0%
RAHE | 0.0% | 0.0% | 0.0%
RALC | 0.0% | 0.0% | 0.0%
LBHE | 0.1% | 0.1% | 0.1%
LBLC | 0.1% | 0.1% | 0.1%
LPHE | 0.1% | 0.1% | 0.1%
LPLC | 0.1% | 0.1% | 0.1%

## Slide 9: Result from byte-aligned WPP substreams with modification to WPP substreams’s entry point signalling
 | Y | U | V
INHE | 0.0% | 0.0% | 0.0%
INLC | 0.0% | 0.0% | 0.0%
RAHE | 0.0% | 0.0% | 0.0%
RALC | 0.0% | 0.0% | 0.0%
LBHE | -0.1% | -0.1% | -0.1%
LBLC | -0.1% | -0.1% | -0.1%
LPHE | -0.1% | -0.1% | -0.1%
LPLC | -0.1% | -0.1% | -0.1%